## Slide 1: Initial Thoughts on High Level MAC Procedures
Date: 2017-2-13
Authors:

## Slide 2: Outline
This presentation discusses some basic MAC procedures for the wakeup radio
  Wakeup procedure for one or more WUR STAs
  Beacon frame for WUR
  Channel Access for wakeup frames

## Slide 3: Wakeup procedure for a single STA – Opt1
Main procedure:
  Step 1: the AP sends a wakeup packet to the STA carrying the STA’s wakeup ID
  Step 2: the STA’s WUR receives the wakeup packet, then wakeup the main radio
  Step 3: the STA sends a PS-Poll frame to the AP to solicit its buffer unit, receives the following DL frame, and sends a block ACK
Error recovery:
  After sending the wakeup packet, if no PS-Poll has been received within a timeout duration, the AP can retransmit the wakeup packet until the max retransmit time is reached
Wakeup packet
Data packet
AP
WuR
Main radio
Wakeup packet
timeout
wakeup
PS-Poll
BA

## Slide 4: Wakeup procedure for a single STA – Opt2
Main procedure:
  Step 1: the AP sends a wakeup packet to the STA carrying the STA’s wakeup ID
  Step 2: the STA’s WUR receives the wakeup packet, replies an ACK, then wakeup the main radio
  Step 3: the AP sends the buffer unit, and receives the following BA frame
Error recovery:
  After sending the wakeup packet, if no ACK has been received within a timeout duration, the AP will retransmit the wakeup packet until the max retransmit time is reached
Wakeup packet
Data packet
AP
WuR
Main radio
Wakeup packet
timeout
ACK
BA

## Slide 5: Wakeup procedure for a single STA
Analysis:
We prefer Opt1
 | Pros | Cons
Opt1 | Simple, can reuse current frames and procedures | The delay for error recovery is longer compared with Opt2
Opt2 | The error recovery procedure is quick | Requires additional transmit capability of the WUR, e.g., PA The ACK transmitted by the WUR may not contain L-Preamble

## Slide 6: Wakeup procedure for multiple STAs – Opt1
Main procedure:
  Step 1: the AP sends a wakeup packet to multiple STAs carrying the STAs’ wakeup IDs
  Step 2: the STAs’ WURs receive the wakeup packet, then wakeup the main radios
  Step 3: each STA sends a PS-Poll frame to the AP to solicit its buffer unit, receives the following DL frame, and sends a block ACK
Wakeup packet for multiple STAs
Data
AP
WuR
Main radio
wakeup
PS-Poll
BA
STA1:
WuR
Main radio
wakeup
PS-Poll
BA
STA2:
Data

## Slide 7: Wakeup procedure for multiple STAs – Opt2
Main procedure:
  Step 1: the AP sends a wakeup packet to multiple STAs carrying the STAs’ wakeup IDs
  Step 2: the STAs’ WURs receive the wakeup packet, then wakeup the main radios
  Step 3: the AP sends a “trigger for PS-Poll” frame to the STAs to solicit the PS-Poll frame from each STA, followed by the transmission of DL data frames
Analysis:
  Opt1 is suitable for non-MU capable STAs, Opt2 is more efficient for MU capable STAs
Wakeup packet for multiple STAs
Trigger for PS-Poll
AP
WuR
Main radio
wakeup
PS-Poll
BA
STA1:
WuR
Main radio
wakeup
PS-Poll
BA
STA2:
Data
Data

## Slide 8: Beacon frame for WUR
The AP can periodically send WUR Beacon frames to achieve the following functions
  Heart Beat
    enabling STAs to know whether they are within the range of the BSS
  Time synchronization
    correcting the clock drift of the WUR
  Group addressed wakeup (by TIM)
    TIM (traffic indication map) can indicate the presence of DL BU for the STAs, hence the TIM can also behave as a wakeup indication
WUR Beacon
WUR Beacon
WUR Beacon
WUR Beacon
WUR Beacon

## Slide 9: Channel Access for wakeup frames
There is a coexistence requirement in the PAR of WUR [1]
  “The WUR devices coexist with legacy IEEE 802.11 devices in the same band.”
In order to satisfy the coexistence requirement and to avoid collisions among multiple wakeup frames, we propose to use the CSMA/CA based EDCA scheme to send wakeup frames
Wakeup Frame
EDCA backoff

## Slide 10: Conclusion
In this contribution, we share our initial thoughts on MAC procedures of WUR, including
  Wakeup procedures
  Wakeup Beacon
  Channel Access Scheme

## Slide 11: Reference
11-16-1045-09-0wur-a-par-proposal-wur-sg
11-16-1445-01-0wur-overall-mac-procedure-for-wur
11-16-1460-01-0wur-wur-mac-discussion
11-16-1470-00-0wur-wake-up-and-data-exchange-sequences
11-16-1400-00-0wur-power-efficient-wur-ap-discovery
11-16-1501-00-0wur-ap-discovery-using-wur
11-16-1504-01-0wur-discussion-of-wur-packets-design

## Slide 12: Straw Poll 1
Do you agree that the STA should send a response frame to the AP using primary connectivity radio after receiving a wakeup packet?

## Slide 13: Straw Poll 2
Do you agree that a STA shall not transmit WUR signal if the primary connectivity radio of the STA is turned off?

## Slide 14: Straw Poll 3
Do you agree that the AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wakeup packet to the STA(s)?

## Slide 15: Straw Poll 4
Do you agree to define a WUR Beacon frame which can be transmitted periodically?
  The WUR Beacon is transmitted to WURs

## Slide 16: Straw Poll 5
Do you agree to use EDCA to send wakeup packets?
  The EDCA parameter set for wakeup packets is TBD

## Slide 17: Motion 1
Move to add the following to the 802.11ba SFD:
  A STA should send a response frame to the AP using primary connectivity radio after receiving a wakeup packet

## Slide 18: Motion 2
Move to add the following to the 802.11ba SFD :
  A STA shall not transmit WUR signal if the primary connectivity radio of the STA is turned off

## Slide 19: Motion 3
Move to add the following to the 802.11ba SFD :
  The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wakeup packet to the STA(s)?

## Slide 20: Motion 4
Move to add the following to the 802.11ba SFD:
  Define a WUR Beacon frame which can be transmitted periodically
    The WUR Beacon is transmitted to WURs

## Slide 21: Motion 5
Move to use EDCA to send wakeup packets
  The EDCA parameter set for wakeup packets is TBD