## Slide 1: A Narrow-Band Bipolar OOK Signal
Date: March 13-17 2017
Authors:
Name | Affiliations | Address | Phone | Email
Shouxing Simon Qu | BlackBerry, Ltd. | 1001 Farrar Rd., Ottawa, ON, Canada | 1-613-595-4205 | squ@blackberry.com
Stephen McCann | BlackBerry, Ltd. |  |  | smccann@blackberry.com
James Lepp | BlackBerry, Ltd |  |  | jlepp@blackberry.com

## Slide 2: Abstract
A narrow-band bipolar OOK (NBB OOK) signal is proposed in this contribution.
On-off keying (OOK) is a potential candidate modulation scheme for WUR [1].
The spectrum efficiency of regular non-return-to-zero (NRZ) OOK signal is analyzed.
The spectrum efficiency of NBB OOK signal is higher compared to the regular OOK signal.

## Slide 3: NRZ OOK Baseband Waveform:
Conceptual NRZ OOK Signal Generator:
NRZ OOK Signal (1)

## Slide 4: NRZ OOK Signal (2)
Baseband OOK signal:
, (1)
{}: input bit stream, independently takes 1 or 0 with equal probability.
: a non-return-to zero (NRZ) pulse,
. (2)
Non-coherent detection: Envelope detector (ED), i.e. detection based on the absolute value of Rx baseband signal.

## Slide 5: Normalized PSD of NRZ OOK Signal
  null-to-null bandwidth: W = 2/T.
  has non-zero discrete DC component (not shown).
(3)

## Slide 6: Motivation for Narrow-Band Bipolar OOK
Proposing a new signal suitable for WUR.
Providing higher spectrum efficiency.
Slightly increasing transmitter complexity.
Do not increase receiver complexity:
  The new signal can be demodulated with the same envelope detector (ED) used as for the above OOK.
  Same error rate performance in AWGN channel.

## Slide 7: NBB OOK Baseband Waveform:
Narrow-Band Bipolar (NBB) OOK (1)
Bipolar: with three levels: {+1, 0 -1}.
  Adjacent pulses have same polarity;
  Non-adjacent pulses have alternate polarities.
Level varies cyclically: +1  0  -1  0  +1…

## Slide 8: Narrow-Band Bipolar OOK (2)
Baseband signal:
, (4)
where, , (5)
: the last-non-zero symbol.

## Slide 9: Narrow-Band Bipolar OOK (3)
Encoding Rule:
  If , ; otherwise,
  If , i.e. transmit the same pulse as previous one;
  otherwise, if and , , i.e. transmitting the pulse with opposite polarity of the last-non-zero pulse.
Non-coherent detection: with the same envelope detector as for the NRZ OOK.

## Slide 10: Narrow-Band Bipolar OOK (4)
NBB OOK Signal Generator: the switch moves as
1 0 -1 0

## Slide 11
Whenever , the output of the switch is connected to Terminal “0” and stays there until an input bit of 1 arrives.
When changes from 0 to 1:
  if the output previously switched from Terminal “1” to “0”, it switches to Terminal “-1”, and stays there
  if the output previously switched from Terminal “-1” to Terminal “0”, it switches to Terminal “1”, and stays there
Switch Connection

## Slide 12: Normalized PSD of NBB OOK
(6)
  No discrete DC component.

## Slide 13: PSD of OOK Signals (theoretical, Eq.(6))

## Slide 14: PSD of NBB OOK Signal (simulation results)

## Slide 15: Bandwidth Efficiency Comparison
Double-Sided Bandwidth (f T) | Energy Ratio within Given Bandwidth (%) | 
 | NRZ OOK | NBB OOK
0.5 | 46.7 | 80.4
0.6 | 54.5 | 84.1
0.8 | 67.6 | 87.9
1.0 | 77.4 | 90.0
1.2 | 83.9 | 91.4
1.4 | 87.8 | 92.5
1.6 | 89.6 | 93.6
1.8 | 90.2 | 94.8
2.0 | 90.3 | 95.0

## Slide 16: Conclusions
By introducing proper correlation among symbols, the proposed narrow-band bipolar OOK signal provides improved spectrum/bandwidth efficiency.
The bandwidth needed to transmit the NBB OOK signal is significantly narrower than to transmit the NRZ OOK signal.
The out-of-band energy leakage is reduced.
No increase of Rx complexity:
  Demodulation with the same ED for the NRZ OOK; yielding same error rate performance in AWGN channel.
Transmitter complexity increases slightly.
The principle is applicable to other unipolar binary signals.

## Slide 17
REFERENCES
:
[1] ] Minyoung Park at.al, “LP-WUR (Low-Power Wake-Up
Receiver) Follow-Up”, IEEE 802.11-16/0341r0, Mar. 14, 2016.
[2] S. Benedetto, E. Biglieri and V. Castellani, Digital Transmission
Theory, Prentice-Hall, 1988.