## Slide 1: CIDs Related to 20MHz-only STAs operating on non-primary 20 MHz channels
Date: March 13, 2017
Authors:
Name | Affiliations | Address | Phone | email
Guoqing Li | Apple |  |  | Guoqing_li@apple.com
Jarkko Kneck |  |  |  | 
Chris Hartman |  |  |  | 
Yunbo Li | Huawei |  |  | 
Tomoko Adachi | Toshiba |  |  | 
Zhou Lan | Broadcom |  |  | 
David Kloper | Cisco |  |  | 
Saishanka Nandagopalan | Cypress |  |  | 

## Slide 2: Introduction
802.11ax draft 1.0 introduces 20 MHz-only STAs which operate at 20MHz BW only
The spec is not clear on whether and how these STAs can operate on non-primary 20MHz channel, see text below
This contribution proposes the protocol components and some considerations that will allow these STAs to operate on non-primary 20MHz channel

## Slide 3: CIDs Related to 20MHz-only Operation on Secondary Channel
8811 | 28.3.3.6 | "A 20 MHz only HE STA operates in the primary 20 MHz channel as a mandatory mode." is not correct language for a standard. | Change to "A 20 MHz only HE STA shall only operate in the primary 20 MHz channel." | Revised. Propose that 20MHz only STA shall support operating on primary channel and may optionally operate on non-primary channels. Please see the proposed text for details
8810 | 9.2.4.6.4.3 | "A 20 MHz only HE STA operates in the primary 20 MHz channel as a mandatory mode." is not correct language for a standard. | Change to "A 20 MHz only HE STA shall only operate in the primary 20 MHz channel." | Revised. Propose to allow 20 MHz-operating STA to operate on any 20 MHz. Please see the text for details
The following three CIDs are related to 20MHz-only STA operating on secondary channel

## Slide 4: Proposed Resolution
Clarify that 20MHz-only STA can operate on any non-primary 20MHz as an optional mode
This mode can also be used by 80MHz capable STA operating at 20MHz. However, for 80MHz capable STAs, it is better to operate in 80MHz to receive the wideband PPDU
Define the protocol elements that allows a 20MHz-only STA to operate on any 20MHz channel
  Capability indication that a 20MHz-only STA is able to operate on non-primary channel
  Signalings (IE, Action frames etc.) that enable a 20MHz-only STA to switch the operating 20MHz channel
Specify the normative behavior for a 20MHz-only STA operating on non-primary 20 MHz channel such as channel access, channel switch procedure

## Slide 5: Motivation
In order for AP to utilize the entire 80 MHz bandwidth, 20MHz-only STA is required to be able to participate in wideband OFDMA
An illustration of OFDMA transmission with 20MHz-only STA mixed with 80MHz-STAs
  RU restrictions when allocating to 20MHz-only STAs are listed in 28.3.3.5 and not shown in this figure
STA1
STA2
STA3
STA4
STA8
STA7
STA6
STA5
STA9
STA3
STA5
STA9
20MHz STA
80MHz STA
Primary 20
Secondary 20
STA2
STA1
Note: Secondary 40 is not shown here due to space limitation

## Slide 6: Motivation (cont.)
However, 20MHz-only STAs are envisioned to be low power low complexity devices such as IoT devices
In IoT deployment such as home scenarios, a BSS may have a lot of 20MHz-only STAs
When these devices only operate on primary 20MHz, the BSS will be forced to operate on primary 20 only and the rest of the 60MHz is wasted most of the time
STA1
STA2
STA3
STA4
STA5
STA3
20MHz STA
80MHz STA
STA1
STA2
Primary 20
Secondary 20
STA2
Waste of BW when 80MHz STA do not have traffic
STA1
Note: Secondary 40 is not shown here due to space limitation
STA4

## Slide 7: Solution: Enable 20MHz STAs to Operate on Any 20MHz channel
If a STA can operate on any 20MHz channel, then an AP can mix 20MHz STAs with 20MHz STAs in wideband OFDMA, see figure below
Compared to the previous slide, channels can be utilized more efficiently and flexibly since full BSS BW can be used more often
From AP’s point of view, this mode allows AP to do intelligent load balancing, interference management and maximize spectrum utilization
From STA’s point of view, STAs can achieve better power efficiency since no energy is spent on sensing
Apple
STA1
STA2
STA3
STA4
STA5
STA3
20MHz STA
80MHz STA
STA1
STA3
Primary 20
Secondary 20
STA2
STA1
Note: Secondary 40 is not shown here due to space limitation
STA4

## Slide 8: The Operation on Non-Primary Channel
Legacy STAs cannot operate on non-primary channel since legacy STAs can only use EDCA
  If a STA uses EDCA on non-primary channel, then the following scenario will happen
    While the AP and STA 1 are communication on primary 20 channel STA 2 operating only on non-primary channel cannot decode neither AP’s or STA1’s transmission and STA 2 will start transmission to AP
    For legacy STAs, we need each STA to monitor the primary 20 to synchronize the status of the BSS activities
Now since 11ax introduces UL MU transmission where the UL transmission is scheduled by AP, STAs operating on non-primary channel only becomes possible

## Slide 9: 20MHz Operation in 11ax
11ax defined 20MHz-only STA which is only capable of operating at 20MHz channel bandwidth
11ax spec allows 20MHz-only STA to participate in wideband PPDU where 20MHz-only STA only occupy the RUs on its operating 20MHz channel
  11ax spec also listed the RU restrictions which ensures the receiving performance at 20MHz-only STA when these STAs participate in wideband PPDDU
With UL MU capability and with the capability to participate in wideband PPDU, 20MHz STA operation on non-primary becomes feasible now

## Slide 10: Issues to Check
STA channel access
STA operation channel switch procedure
STA’s recovery mechanism when it experience issues on non-primary channel
Beacon reception and synchronization
Examining any PHY issues

## Slide 11: Channel Access and Protection
The STAs staying on non-primary 20MHz channel can only use MU transmission in uplink since it is blind to the status on the primary channel
  i.e., STAs on non-primary channel cannot use EDCA to transmit
These devices need to rely on AP for protection
  UL transmission is protected by trigger frame
  AP can solicit MU-RTS and CTS before any MU transmission
STAs follow the same channel sensing requirement for UL MU operation
  If a STA decodes a frame on non-primary channel, it still sets NAV as if it operates on primary channel

## Slide 12: Operating Channel Switch
New IEs and actions frames are defined
  STA Channel Switch Request/response element
  STA Channel Switch Request/response frame
The IE sent by non-AP STA contains channel index list which the STA is willing to operate on
  This IE can be put in (Re)Association request since the STA scans the channel before joining the BSS and can provide this list to AP during association
AP should decide the channel for STAs since it has global information across the BSS and can perform global optimization
STA channel switching is not expected to be very dynamic process, i.e., not packet-based

## Slide 13: Operation Timer
It is recommended to define a recovery mechanism so that if the STA does not receive a trigger on the non-primary channel for a long time it can switch back to the primary channel to use regular EDCA
Similar to MU EDCA timer, we can define a non-primary channel operation timer for STAs on non-primary channel to switch back to primary channel upon timeout
The STA shall send a notification to the AP to inform the channel switch upon time-out after it switches back to primary
  Any frame that needs acknowledgement sent by the STA can serve this purpose

## Slide 14: Channel Switch Time
Channel switch takes time and during this period of time, the STA cannot transmit or receive any data
STA can provide its channel switch time during association
However, how to handle channel switch time can be left to AP’s implementation choices
  A complex AP can take individual STA’s channel switch time into account and do things differently with different STAs to maximize channel utilization efficiency
  A simpler AP may choose to ignore the channel switch time differences to simply its implementation

## Slide 15: Beacon Reception and Synchronization
STAs on non-primary channels need to receive Beacon to get important operating parameters as well as to synchronize its clock with the AP
Since Beacon is transmitted in non-HT format, we have a few options for STAS on non-primary channel to receive Beacon and multicast frames
  AP sends Beacon in non-HT duplicate format—violation of baseline spec, confuses legacy STAs
  AP switches STA back to receive Beacon—this requires explicit signaling and can cause high overhead when there are a lot of STAs operating on non-primary channel
  STA switches back without explicit signaling during a period that is announced by AP and AP shall not transmit to STAs on non-primary channel during this period—preferred approach

## Slide 16: DL transmissions to STAs on non-primary channel
AP use either non-HT Duplicate format or HE MU PPDU when transiting STAs on non-primary channel
AP should avoid the possibility that when AP starts DL transmission the buffered DL traffic is only destined for STAs on non-primary channels
  AP can either group STAs in a way to minimize such possibility or delay the transmission on non-primary channel to wait for traffic on primary channel or ping STAs on primary channel such as BSR, BQR
In case the AP needs to transmit to STAs on non-primary channel only, draft 1.0 allows the AP to transmit only preamble on primary channel and leave the data field on primary channel empty or fill the data field with dummy bits
  STA ID 2046 in SIG-B User Specific field or RU allocation “0110001” in SIG-B common part are already defined to indicate that the 242 RU is empty
  If AP does not want to leave the data field empty, then AP can fill the RU with dummy bits using an unallocated STAID
  Other constraints in draft 1.0 still apply. AP can transmit dummy bits to fill out the RUs across the BW to satisfy this requirements
No new PHY requirements are needed for DL transmission to STAs on non-primary channel

## Slide 17: UL transmission
STAs on non-primary channel can transmit only when triggered, i.e., no EDCA allowed
Trigger frame shall be non-HT duplicate format if it allocates RUs to STAs on non-primary channel so STAs on non-primary channel can receive it
AP should minimize the possibility of triggering STAs on non-primary channel only
  However, even if AP only triggers STAs on non-primary channel the trigger-based PPDU will be the same as if AP triggers some STAs on primary channel but those STAs did not respond to trigger due to CCA/NAV busy
  So there is no new PHY requirement needed for UL transmission for STAs on non-primary channel

## Slide 18: MU-RTS and CTS
Currently, MU-RTS and CTS procedure assumes that the CTS has to cover primary 20 and AP can consider MU-RTS/CTS success if it receives CTS only on primary channel
  However, AP does not know which STA respond with CTS and the following MU PPDU may not match STA’s busy/idle status and RUs may be allocated to STAs that did not respond CTS
  An intelligent AP can implement in a way to receive multiple CTS on multiple 20MHz so channel bandwidth can be allocated more efficiently
    For example, AP do not allocate RUs on the 20MHz where no CTS is received
STA operating on non-primary channel solve the over-protection problem of current MU-RTS/CTS

## Slide 19: MU-RTS and CTS (cont.)
How AP handles MU-RTS/CTS can be left to AP’s implementation
  AP does not send MU-RTS to the STAs on non-primary channel
  Or when AP sends MU-RTS to non-primary STAs, it always include STAs on primary channel
  Or if AP can decodes CTS on non-primary channels, it can adjust its allocation more intelligent and utilize BW more efficiently. This solves the over-protection problem of MU-RTS/CTS
Spec does not need to mandate which mode the AP has to operate

## Slide 20: OBSS Coexistence
20MHz-only STAs on non-primary channels do not have co-existence issue with IntraBSS STAs since all TXs/RXs are scheduled by AP
A 20MHz-only STA’s transmission is the same as a regular STA’s transmission being allocated RUs on a specific 20MHz, so it has the same effect on OBSS as regular STAs
STAs on non-primary channel reply on AP for protection and though 20MHz STA cannot decode OBSS hidden node’s frames on primary channel, Wi-Fi today has many similar coexistence cases already. For example,
  Narrowband STAs cannot OBSS wideband PPDU
  STAs cannot decode OBSS frames who use different primary channel
  STAs in infrastructure cannot decode frames in P2P links
  STAs miss OBSS frames due to power save operation

## Slide 21: Summary
As part of comment resolution for CID 8810 and 8811, we propose to allow 20MHz-only STAs to operate on any 20MHz channel as an optional mode
The protocol considerations to enable such operation are discussed in this contribution
The data transfer for these STAs is the same as regular STAs which are always allocated RUs in a particular 20MHz channel except that EDCA is disabled
This operation mode can help AP with load balancing, interference management, can help STA with power saving and can increase BSS efficiency

## Slide 22: Proposed Spec Text (#0370)
Capability indication
Channel Switch signaling
  STA Channel Switch Request/Response element
  STA Channel Switch Request/response action frames
  (Re)Association Request/Response are allowed to include the new IE
Normative behavior on non-primary channel
  STA operation channel switch procedure
  Channel Access
  Non-primary channel operation timeout
  Beacon reception and multicast reception
MLME

## Slide 23: SP
SP1: Do you agree to allow 11ax 20MHz-only STAs to operate optionally on non-primary channel only?
SP2: Do you agree to accept the text described in 0370r2 for CID 8810 and 8811?