## Slide 1: SFD MAC proposal
Date: 2017-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
TGba decided to build Specification Framework Document (SFD) in January meeting
We have submitted WUR MAC procedure presentations
  They were about WUR mode signaling, WUR general operation, WUR retransmission, and channel issue
So now we propose SFD text based on previous WUR MAC submissions

## Slide 3: WUR Mode Signaling [1]
After the association procedure or receiving DL data completely, a STA may request to enter WUR mode for low power operation
After receiving the confirmation (i.e., WUR mode response) from the AP, a STA enters the WUR mode
For this procedure, an explicit WUR mode signaling is needed
  If the STA does not inform its 802.11 main radio turning off, then WUR AP can send 802.11 frames to the STA without sending WUR packet and it can be lost
  WUR operating parameter can be negotiated during WUR mode signaling

## Slide 4: WLAN packet transmission to WUR STA [1]
Whenever an AP wants to send a WLAN packet to a STA in WUR mode, WUR packet should be transmitted to wake up the station
  After transmitting a WUR packet, AP should wait for a specific time before sending a WLAN data frame. WLAN main radio turn-on time can take about a few millisecond.

## Slide 5: WLAN packet transmission to WUR STA [1]
Before WLAN packet transmission, STA’s wake-up can be confirmed through the existing WLAN control signaling (e.g., PS-Poll)

## Slide 6: WUR Error Recovery [1]
To handle the case that wakeup signaling fails, an error recovery mechanism shall be provided.
  When an AP sends data frame after WUR packet and does not receive ACK/BA, AP has to retransmit WUR packet or data frame.
  Retransmission policy at AP should be defined to reduce power consumption and overhead

## Slide 7: WUR Error Recovery [1]
For the case of PS-Poll transmission in response to WUR packet, AP can retransmit WLAN data frame

## Slide 8: WUR channelization [2]
WUR channel can be identical with primary channel of WLAN
  PROS
    AP/STA do not have to change operating channel
    Signaling about WUR channel information can be simple
    AP doesn’t have to manage WUR channel independently
  CONS
    Latency of WU signal can be increased in high density network

## Slide 9: Summary
In this submission, we proposed MAC description texts for Specification Framework Document
  The texts are based on previous technical submissions which are addressed overall MAC procedure and channel issue in WUR

## Slide 10: Straw poll 1 (WUR Mode signaling)
Do you support following sentences?
  Explicit Wake-Up mode signaling shall be performed between WUR AP and WUR STA for the WUR STA to enter the low power mode
  Wake-Up operating parameter shall be negotiated during Wake-Up mode signaling

## Slide 11: Straw poll 2 (WLAN packet transmission)
Do you support following sentences?
  An WUR AP shall wait for a specific time [TBD] before sending a WLAN data frame after transmitting a Wake-Up frame for WUR STA to wake up. If the WUR AP received PS-Poll frame from WUR STA during waiting to send WLAN data frame, WUR AP doesn’t have to wait to send WLAN data frame
  WUR STA may send PS-Poll frame after receiving Wake-Up frame and before receiving DL WLAN data frame from WUR AP

## Slide 12: Straw poll 3 (WUR Error Recovery)
Do you support following sentences?
  When an WUR AP sends WLAN data frame to WUR STA after Wake-Up frame transmission and there isn’t ACK/BA of WLAN data frame, AP shall retransmit Wake-Up frame if there wasn’t PS-poll frame from WUR STA
    Retransmission count of the WLAN data frame doesn’t increase
    Contention window of the WLAN data frame doesn’t increase
  When an WUR AP sends data frame to WUR STA after Wake-Up frame transmission and there isn’t ACK/BA of WLAN data frame, AP may not retransmit Wake-Up frame if there was PS-poll frame from WUR STA

## Slide 13: Straw poll 4 (WUR channelization)
Do you support following sentence?
  The channel where wake-up signal is sent is located within primary 20MHz channel of WLAN radio

## Slide 14: References
[1] 11-16-1445-01-0wur-overall-mac-procedure-for-wur
[2] 11-17-0031-00-00ba-channel-issue-in-wur