## Slide 1: WUR MAC issues follow-up
Date: 2017-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
The following several WUR MAC issues were discussed at the previous meetings [1] and there were some agreements among them
  Broadcast Wake-up
  Group wake-up
  Multicast Wake-up
  WUP (Wake Up Packet) contents design
This contribution discusses details of them and proposes the related SFD texts

## Slide 3: Broadcast Wake-Up (1/2)
Before sending group addressed BU, AP can send a broadcast wake-up packet to wake up all WUR mode STAs which are associated with the AP
Broadcast WUP should be sent early with enough time for those WUR mode STAs to receive DTIM/GA BU correctly after their wake up delay
  Because Broadcast WUP TX can be delayed if channel is busy and,
  Each STA’s wake-up delay could be different according to each STA’s capability or its environment
Broadcast Wakeup
AP
STA1
STA2
STA3
STA4
Wakeup delay
DTIM
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on
Waiting time

## Slide 4: Broadcast Wake-Up (2/2)
AP (or WUR Transmitter) informs the STAs of the Wake-up Completion Time (WCT)
  WCT: the time at which WUR mode STA should finish its wake up procedure to receive the DTIM or Group addressed BU correctly
    e.g., AP can set the WCT to TBTT or Group addressed BU TX start time
  WCT value depends on the time when the broadcast WUP is transmitted (i.e., random back-off)
  Each WUR mode STA decides its WLAN-On start time based on the received WCT value and its wake up delay
WCT is included in Broadcast wake-up packet
AP sends DTIM or Group address BU after the WCT
Wake up start time of STA 3, 4
Wake up start time of STA 1, 2
Broadcast Wakeup
(WCT)
AP
STA1
STA2
STA3
STA4
Wakeup delay
DTIM
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on
WCT

## Slide 5: TF reception after WCT
The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s). [Motion 3, March 2017]
In this case, AP can also include WCT (wake-up completion time) in WUP (s) before sending the Trigger frame so that STA can decide its WLAN-On start time
WUP (STA 1, 2, 3), WCT
AP
STA1
STA2
STA3
STA4
MU PPDU (STA 1, 2, 3)
PS-Polls from STA 1~3
TF
Wakeup delay
WLAN on
WLAN on
WLAN on
WCT
Wake up start time

## Slide 6: Group wake-up
Group wake up
  Group wake up (e.g., using Group ID) can be used for waking up all STAs belonging to a group but it hardly happens
  May not be efficient if it is used for waking up a part of STAs in a group  increasing false alarm
  Need complicate group management like MU-MIMO
WUP
(GID =1)
AP
STA1
STA2
STA3
STA4
WLAN on
Wakeup delay
MU PPDU (STA 1, 2, 3)
STA1, 2, 3, 4, 5 belong to Group 1 (GID=1)
STA5
PS-Polls from STA 1~5
Unnecessary power consumption
Unnecessary power consumption

## Slide 7: Multi-User Wake-Up
Multi-User (MU) Wake Up
  WUR needs to support MU wake-up mode for waking up a part of STAs in a group
  Example 1) WUP may contain multiple receiver IDs  the WU packet size is increased according to the number of STAs
  Example 2) WUP may contain the STA’s position bitmap like TIM
    TIM size should be optimized (e.g., like 11ah hierarchical TIM or using WUR ID1) instead of AID)
A STA should also send a response frame to the AP after receiving MU wake-up packet which is sent for unicast WLAN frame
1) WUR ID can be allocated before entering WUR mode
STA4
WUP (STA 1, 2, 3)
AP
STA1
STA2
STA3
WLAN on
Wakeup delay
PS-Poll
D1
PS-Poll
D2
PS-Poll
D3
WLAN on
WLAN on

## Slide 8: WUP contents format (1/2)
Considerations on Wake-Up Packet (WUP) contents design
  WUP TX frequency as small as possible to minimize the contention with other WLANs/WUPs  Broadcast/Group/MU wake up
  WUP content size should be minimized (e.g., if OOK is used, 1 symbol (4us) is used for delivering 1 bit)  WUP optimization
  Avoid unnecessary false alarm of wake-up  MU wake-up instead of group wake up
  Including WUR operation mode (WOM) information which indicates the STA’s operation after receiving the WUP
    Whether the STA should wake up after receiving the WUP or not
      WUP may be sent for just keep alive check or synchronization(WUR beacon reception). In this case STA does not need to wake up
    Whether the STA should send a response frame (e.g., PS-Poll) based on EDCA though primary connectivity radio after turning on the main radio or not
      E.g., Sending a response for unicast WUP, not sending a response for a broadcast/multicast WUP for group-addressed data TX, may not be sending a response for a WUP for MU polling
      This information is necessary for supporting the following motion text
      A STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up packet. [Motion 1, March 2017, see [1] [6]]

## Slide 9: WUP contents format (2/2)
Various WU packet types according to different length
  Frame Type & Receiver ID
    0: WUR Beacon
    1: Broadcast wake-up, Receiver ID does not need to be included
    2: Individual wake-up, Individual ID is included
    3: MU wake-up, Multiple ID information (e.g., TIM or multiple IDs set) are included instead of individual ID
  WOM(WUR Operation Mode)
    0- No wake-up, 1- Wake-up and EDCA access, 2- Wake-up and No EDCA access
    WOM can be merged with Frame Type field
  Transmitter ID: Partial BSSID (or BSS Color)
  WCT (Wake-up completion time): the time at which WUR mode STA should finish its wake up procedure (slides 4, 5).
    AP sends a frame to STA (s) through the primary connectivity radio after the WCT
    STA can determine its WLAN On Start time based on the WCT
Frame Type
Transmitter ID
(WOM)1)
Receiver ID (optional)
FT=0
Transmitter ID
(WOM)
FT=2
Transmitter ID
FT=3
Transmitter ID
Individual ID
Multiple ID Info
WCT
Timestamp[2]
(WOM)
(WOM)
WCT
WCT
FCS
FCS
FCS
FCS
FT=1
Transmitter ID
(WOM)
WCT
FCS

## Slide 10: Conclusion
For power saving of WUR STAs, AP includes the WCT in a wake-up packet (WUP)
  WUR STA decides when it turns on the primary connectivity radio after the WUP based on the WCT and its wake-up delay
  AP sends WLAN frame to a STA through the PCR after the WCT
A multi-user wake-up packet includes the information of multiple STAs which need to wake up (e.g., multiple IDs or Bitmap type)
A STA should also send a response frame to the AP after receiving MU wake-up packet which is sent for unicast WLAN frame as well as after receiving unicast wake-up packet
Wake-up packet has different types according to its packet length and includes the frame type field for it
WU packet design contains the information for the STA’s operation after receiving WUP (e.g., WUR operation mode (WOM))
  0: No-wake up, 1: wake-up and EDCA access, 2: wake-up and waiting w/o EDCA

## Slide 11: References
[1]11-17/0054, WUR MAC issues
[2] 11-17-0343-00-00ba-wur-beacon

## Slide 12: Straw Poll 1
Do you support the following?
  A wake-up packet (WUP) includes the time information about when WUR mode STAs should complete its wake up procedure after receiving the WUP

## Slide 13: Straw Poll 2
Do you support the following?
  A wake-up packet (WUP) may contain the information to identify the multiple STAs (e.g., multiple individual identifiers, or STA’s position bitmap like TIM).

## Slide 14: Straw Poll 3
Do you support the following?
  WUR has multiple types of a wake-up packet (WUP)

## Slide 15: Straw Poll 4
Do you support the following?
  A wake-up packet (WUP) contains the information to indicate the type of the WUR packet (e.g., Frame Type)

## Slide 16: Straw Poll 5
Do you support the following?
  A wake-up packet (WUP) contains the following information to indicate the STA’s operation after the WUR mode STA receives the wake-up packet
    Whether the WUR mode STA wakes up after receiving the WUP or not
    Whether the STA sends a response frame (e.g., a PS-Poll) after waking up from WUR mode or not