## Slide 1: Purpose Indication of WUR Packets
Date: 2017-03-12
Authors:

## Slide 2
Abstract
In this contribution, we discuss the need and benefits for WUR packets to indicate their purposes.

## Slide 3: Introduction
Many different wake up scenarios have been discussed in WUR SG and TGba using a Wake Up Packet (WUP)
  E.g., an AP may use a WUP to wake up one or more STAs for the following purposes:
    Synchronization [1][3]
    Request STAs to listen to beacon [2]
    Data transmission:
      DL/UL [1][3] and/or SU/MU [1][2]
  E.g., a STA may use a WUP to wake up an AP for the following purposes:
    Discovery and association [4]
    UL Data Transmission [5]
STA behaviors and WUP contents are expected to be different in many of the scenarios described above depending on the purpose of the transmitted WUP.

## Slide 4: Wake up scenario analysis (1)
Scenario 1: An AP sends a WUP to one or more STAs for synchronization:
  Example WUP content: TSF timer
  Example receiving STA behavior: synchronize, no need to turn on Primary Connectivity Radio (PCR)
Scenario 2: An AP sends a WUP to STAs to request the STAs to receive the beacon:
  Example WUP content: beacon TBTT, maybe reason
  Example receiving STA behavior: turn on PCR and receive beacon
Scenario 3: An AP sends a WUP to one or more STAs for SU/MU DL/UL data transmission:
  Example WUP content: DL/UL indication, TOMI/ROMI, SU/MU indications, resource allocation for STAs

## Slide 5: Wake up scenario analysis (2)
Scenario 3: An AP sends a WUP to one or more STAs for SU DL/UL data transmission:
  Example receiving STA behavior:
    Inform AP of waking up/Turn on PCR
    Adjust TOMI/ROMI
    Tx/Rx accordingly
Scenario 4: A STA may send a WUP to an AP for discovery and association:
  Example WUP content: SSID/BSSID requested, Service Requested
  Example receiving AP behavior: send beacon/broadcast probe response to facilitate discovery/association

## Slide 6: Wake up scenario analysis (3)
Scenario 5: A STA may send a WUP to an AP for UL data transmission:
  Example WUP content: DL/UL request indication, TOMI/ROMI indication, BU size indication
  Example receiving AP behavior:
    Inform STA of waking up/Turn on PCR
    Adjust TOMI/ROMI
    Rx accordingly

## Slide 7: WUP Purpose Indication
If the purpose of a WUP is indicated in the WUP:
  It will help receiving STAs to optimize operations following the receptions of the WUP
  It can provide indication of the content of the WUP as well
Can WUP purpose be indicated using other fields, e.g., the Type field?
  The content of a packet is typically indicated by the Type field
  Purposes such as synchronization, request STAs to receive beacons, wake up STAs for UL/DL SU/MU packets are typically not covered by the Type field
Can the purpose of wake up be indicated through the PCR
  Some of the purposes such as UL/DL, SU/MU data transmission may be indicated using PCR; Likely requires additional overhead (packet exchanges)
  Synchronization may not require STAs to turn on their PCRs

## Slide 8: Summary
STA behaviors and WUP contents are expected to be very different in many wake up scenarios depending on the purpose of the transmitted WUP.
Allowing the WUP to indicate the wake up purpose may better prepare receiving STAs for optimized operations
Some of the WUP purposes may include:
  Synchronization
  Request STAs to receive beacon
  UL/DL SU/MU data transmissions
  AP discovery and association

## Slide 9
References
[1] 11-17/0054r1, WUR MAC Issues, Jan. 2017
[2] 11-17/0124r1, WUR MAC and Wakeup Frame, Jan. 2017
[3] 11-17/0034r0, WUR Use Cases and Requirements, Jan. 2017
[4] 11-16/1400r0, Power Efficient WUR AP Discovery, Nov. 2016
[5] 11-16/0029r4, WUR Usage Model Document, Jan. 2017

## Slide 10: Straw Poll
Do you agree that a wake up packet should include a purpose field to indicate the purpose of the wake up operation?