## Slide 1: Association Exchange using Contention based UL OFDMA
Date: 2017-03-01
Authors:

## Slide 2: Introduction
In [1], random access behavior for unassociated STAs is not defined.
Contention based UL OFDMA can be used for the association procedure
  MU transmission can allow multiple unassociated STAs to accomplish the association procedure simultaneously
  UL OFDMA random access can also help unassociated STA at the edge of BSS to access the network quickly due to narrow band transmission
Trigger frame for
random access
DL M-BA
Contention-based UL OFDMA
Probe Request from STA1
ACK/BA to STA1
UL Ack
DL OFDMA
Association response to STA1
Probe Request from STA2
Response frame
(Pre-AID )
Ack

## Slide 3: Question
How does AP response with the acknowledgements to multiple unassociated STAs which sent the association request successfully through UL OFDMA random access?
  Both M-BA frame and OFDMA Ack/BA frame require AID of the receivers
  However, unassociated STAs do not have AID assigned by AP.
  In this contribution, we provide an acknowledgement mechanism throughput M-BA frame and Pre-AID assignment mechanism

## Slide 4: Comments on pre-AID
CID | Clause | Page No. | Comment | Proposed Change | Resolution
5036 | 27.5.2.6.2 | 173.61 | It is mentioned that the acknowledgement procedure for random access is as defined in 10.3.2.10.3; however, for an unassociated STA, due to its absence of an AID, may not be acknowledged as similar to an associated STA; | Suggest to define an MU acknowledgement procedure for unassociated STAs using UL OFDMA-based random access, following a definition of an AID for the TBD in Subclause 27.5.2.3. | 
7254 | 27.5.2.6.2 | 173.64 | Acknowledgment procedure in response to the OFDMA random access request from unassociated STAs needs to be specified. | As in the comment | 
7546 | 27.5.2.6.2 | 173.62 | It is not clear how STA without AID could participate the UL MU ack procedure in 10.3.2.10.3. | describe specifically how STA without AID acquires its ack following the procedure in 10.3.2.10.3, when there are multiple acks to multiple STA without AID | 
8140 | 27.5.2.2.1 | 164.47 | Random Access UL OFDMA for unassociated STAs is mentioned here, but how does such a STA recognize the DL OFDMA response? Such a STA needs some sort of AID value to identify its DL RU allocation - the text refers me to 27.5.2.6 but there is nothing here mentioning what to do for unassociated STA, while over in 27.5.2.3, there is a TBD in a sentence that refers to unassociated STA | Define the rules for unassociated STA operation within UL OFDMA Random Access | 
8520 | 27.5.2.6.2 | 173.01 | The UL OFDMA-based random access procedure for unassociated STAs is not defined | Define | 
8527 | 27.5.2.6 | 174.20 | Random access behavior for unassociated STAs is not defined | Define behavior for unassociated STAs | 
8157 | 9.3.1.9.7 | 38.04 | Now Multi-STA BlockAck can not be used to acknowledge the association request frame because of unassociated STA is not assigned an AID | define a common special AID for all the unassociated STAs such that they can parse the M-BA frame correctly | 
9332 | 172.25 | 27.5.2.6 | Currently, it is considered that both the associated STAs and unassociated STAs are allowed to join the UL OFDMA-based random access. However, the real state that the STA is in and the state that the AP thinks the STA is in according to the… | … | 

## Slide 5: M-BA frame
The agreed M-BA structure is
A value of 15 in the TID subfield in the Per STA Info field of the M-BA frame indicate the successful acknowledgement of a management frame that requires an immediate response and is carried in the soliciting A-MPDU. [MAC Motion 79, March 2016, see [2]]
Under the condition of the unassociated STA without AID, how does AP send the acknowledgement to its association request?
  According to the agreed motion, the TID value shall be set to “1111”
B0-B10= AID
B11=ACK/BA

## Slide 6: Acknowledgement to association exchange
Set AID subfield to an unique AID value, e.g., 2045, in the M-BA frame
  Provide an unique identifier for any unassociated STAs that has used an RU for random access
  RA field is added after the “Per TID info” field
  MAC address field is used to distinguish which STA’s request management frame is successfully delivered through OFDMA random access
  Both Ack type and SSC field are set to 0, keeping consistent with the parsing scheme of the implemented ax device
  Indicate that the total length of subfields following Per TID STA info subfields is 10 bytes
B0-B10= 2045
B11= BA
SSC (2 bytes )
TID=“1111”
RA (6 bytes)
Reserved (2 bytes )

## Slide 7: Per STA Info Subfield Parsing with Proposed M-BA
An associated STA that had transmitted either on a scheduled RU or an RU for random access will determine the length of the Per STA Info subfield based on the ACK Type subfield
  AID 2045 indicates that the Per STA Info subfield is for an unassociated STA
  ACK Type subfield and SSC fields are set to 0 for AID 2045, indicating the presence of the Per STA Info subfield only for an unassociated STA, and has 10 bytes
An unassociated STA that had transmitted on a random access RU will ONLY parse the remaining 10 octets following the Per TID Info subfield when B0-B10 is an AID 2045
  The STA parses Per STA Info subfield to decode the RA field
  If the RA field matches the MAC address of the unassociated STA, it interprets that the HE Trigger-based PPDU transmitted on an RU assigned for random access was received by the AP successfully.

## Slide 8: Pre-AID assignment
HE AP can assign the Pre-AID to the un-associated HE STA through the management response frame for association or other purpose
  Define New element for Pre-AID, which is carried in the management response frame
  This element can be transmitted in response management frame for association, e.g., Probe Response frame, excluding Association Response frame
  The management frame which carries Pre-AID shall be transmitted in SU format
  Propose pre-AID lifetime timer to manage Pre-AID
  An unassociated STA with assigned pre-AID might not complete association with the AP that has assigned the pre-AID
    Example scenario: STA interested in retrieving location information from an AP
  In order to release the Pre-AID assigned to this STA, we need to define a pre-AID lifetime timer
The assigned Pre-AID is automatically released once the association procedure (or other procedure) is completed or Pre-AID life time timer expires
  The Pre-AID value may be assigned to another unassociated STA after it is released
  The Pre-AID value shall not be used between the associated STA and the AP in any UL or DL frame exchange

## Slide 9: Pre-AID Assignment Element in Request and Response Frame
We propose to include the assigned pre-AID of an unassociated STA in the Pre-AID Assignment element
  The STA may include the Pre-AID Assignment element in the Request management frame (example, Probe Request)
  If the Pre-AID Assignment element is present in the Request frame, then the AP includes the element in the solicited Response frame (for example, Probe Response frame)
Propose to include the following subfields in the Pre-AID Assignment element
  Pre-AID Request/Response: This subfield indicates whether the element Request or Response frame;
    If the value is set to 0, Pre-AID and Pre-AID Lifetime Timer fields are reserved
  Pre-AID: A random value assigned by the AP to the unassociated STA identified by the MAC address in Request management frame
    This value is selected from a set of AIDs which are not assigned to associated STAs
  Pre-AID Lifetime Timer: This subfield indicates a timer after which the pre-AID assigned to a unassociated STA will expire
    The unit of the timer is expressed in 1 TU
Element ID | Length | Element ID Extension | Pre-AID Request /Response | Pre-AID | Reserved | Pre-AID Lifetime Timer
Bits 8 8 8 1 11 4 16

## Slide 10: Benefits
Association Exchange using Contention based UL OFDMA
  It allows multiple unassociated STAs to access the network simultaneously
  E.g. considering the 80 MHz BW with 37 26-tone RU and the 37% OFDMA Random access efficiency, more than 13 times the number of unassociated STAs are allowed to access the network simultaneously
  It also solves unbalanced link budget problem between AP and STA
  Pre-AID assignment
  Within the pre-AID lifetime, the AP uses the assigned pre-AID to schedule the unassociated STA to transmit the HE trigger-based PPDU by the Trigger frame
  Or transmits frame in HE MU PPDU to the unassociated STA before association.
  E.g. FTM frame, authentication response, association response

## Slide 11: Summary
  We propose an acknowledgement mechanism throughput M-BA frame to the unassociated STAs
  An unique AID in the M-BA frame is proposed to be as a common identifer of all the unassociated STAs
  MAC address field in the M-BA frame is proposed to distinguish the unassociated STA which successfully transmits frame through UL OFDMA random access
  Pre-AID assignment in the response management frame allows unassociated STAs to join OFDMA MU transmission

## Slide 12: SP 1
  Do you agree to provide a resolution to CID 5036, 7254, 7546, 8140, 8520, 8527 8157, 9332 based on the concept proposed in this contribution?
  Acknowledgement through M-BA

## Slide 13: SP2
  Do you agree to provide a resolution to CID 5036, 7254, 7546, 8140, 8520, 8527 8157, 9332 based on the concept proposed in this contribution?
  only for Acknowledgement through M-BA, excluding Pre-AID assigment

## Slide 14: SP3
Do you agree to have Pre-AID assignment in 11ax?

## Slide 15: References
[1] 802.11 ax D1.0
[2] 11-15-0132-17-00ax-spec-framework.docx