## Slide 1: WUR Link Budget Analysis
Date: 2017-03-13
Authors:

## Slide 2: Introduction
Previous contributions focus on the On Off Keying (OOK) with 250kbps data rate [1,2,3 and etc.]
This contribution takes a top down approach to analyze the link budget of wake-up radio (WUR) in 2.4GHz band
The analysis is based on 802.11ax indoor and outdoor channel models [4]
Discuss the link margin and potential rate options

## Slide 3: Link Budget Settings
fc = 2.4GHz
Tx_Power: 20dBm
Propagation Loss (PL): 802.11ax channel models [1]
Tx/Rx Antenna Gain: 0dB
Rx Noise Figure: NF=15dB [4]
Noise Floor for 20MHz channel: N0=-101dBm
Rx SNR = Tx_Power – PL – 3*Shadowing- N0 - NF

## Slide 4: Indoor Channel B
Link margin of ~30dB at 10m, ~15dB at 20m, ~5dB at 30m

## Slide 5: Indoor Channel D
Link margin of ~30dB at 10m, ~15dB at 20m, ~10dB at 30m

## Slide 6: Outdoor UMi LOS
Link margin of ~20dB at 50m, ~15dB at 100m, ~10dB at 150m

## Slide 7: Outdoor UMi NLOS
No margin for UMi-NLOS at d>30m

## Slide 8: Link Margin Discussion
SNR ceiling due to low power RF design of the WUR
  The noise figure may be nonlinear
  There may be a SNR ceiling limited by RF
  The link margin may not be as large as 30dB at close range
Additional attenuation for floor/wall penetration loss for different application/simulation scenarios [4, 7]

## Slide 9: More Data Rate Options
Link budge analysis shows ~30dB link margin at close distance for indoor channels, but negative values for distance larger than 30m in UMi-NLOS channels
Various data rates will be needed to achieve either better efficiency or coverage
Higher data rate can be accommodated for close range
  With payload of ~50bits [5,6], higher rates can reduce packet duration significantly, and improve 802.11 traffic, also save power
  Options: higher-rate OOK with pulse during <4us, or higher order modulations
Lower data rates will be beneficial for outdoor coverage
  Options: lower-rate OOK with pulse during >4us, or coding

## Slide 10: Discussions
Power consideration:
  Adding more data rate options, slightly more digital processing may be needed
  This will not cause significant power consumption change relative to RF
  Reduction of airtime for higher rate may further save power
Waveform design:
  WUR may not necessarily follow OFDM design (IFFT operation)[1,2,3]
  Single carrier waveform design can be flexible for more rate options
  The waveform format will be determined by the final WUR PPDU format, preamble format and hardware cost

## Slide 11: Straw Poll 1
Do you agree to have more than one data rates for the wake-up packet?
  Yes
  No
  Abstain

## Slide 12: References
[1] Eunsung Park et al., , “Further Investigation on WUR
Performance”, IEEE 802.11-16/1144r0, Sept. 12, 2016.
[2] IEEE 802.11-16-0865-01-0wur-performance-investigation-on-wake-up-receiver
[3] Minyoung Park et al., “LP-WUR (Low-Power Wake-Up Receiver) Follow-Up”, IEEE 802.11-16/0341r0, Mar. 14, 2016.
[4] IEEE 802.11-14/882r4, IEEE 802.11ax channel model document
[5] N.M. Pletcher, S. Gambini, and J.M. Rabaey, “A 2GHz 52 μW Wake-Up Receiver with -72dBm Sensitivity Using Uncertain-IF Architecture”, IEEE Journal of Solid-State Circuits, vol. 44, No. 1, pp. 269-280, Jan. 2009
[6] Liwen et al., “11-17-0124-01-00ba-wur-mac-and-wakeup-frame”, IEEE 802.11-17/0124r1
[7] IEEE 802.11-14/621r3, TGax simulation scenarios