## Slide 1: Use Cases for WUR in ITS
Date: March 2017
Authors:
Name | Affiliations | Address | Phone | Email
James Lepp | BlackBerry Limited | 1001 Farrar Road, Ottawa, ON, Canada | (+1) 613-595-4156 | jlepp@blackberry.com
Stephen McCann | BlackBerry Limited |  |  | smccann@blackberry.com

## Slide 2: Background on 802.11ba (WUR)
802.11ba Wake-up Radio (WUR) is a low power mechanism to enable power saving in 802.11 stations.
In January 2017 it was decided to compile a Usage Model Document for 802.11ba.
This presentation contains Use Cases for the 802.11ba task group to consider when designing the WUR protocol.

## Slide 3: Background on 802.11 ITS systems
802.11-OCB (developed in 802.11p TG) is used as the basis of Intelligent Transportation Systems.
Outside the context of a BSS devices transmit 802.11 frames between vehicle onboard units (OBUs) and infrastructure roadside units (RSUs).
Current 802.11-based ITS systems use a significant amount of energy to operate. To enable a third class of system for pedestrians and cyclists, as a group called vulnerable road users (VRUs), mechanisms to enable power saving are desired.

## Slide 4: Wake Up Vehicle-to-Pedestrian (V2P) Radio
Scenario
  Pedestrian carrying portable device with V2P capability.
  To conserve power, the V2P mode isn’t always operating.
  Roadside infrastructure such as an intersection or an oncoming vehicle sends WUR wake-up trigger frame.
  Pedestrian device wakes up and operates 802.11-OCB based V2P
Wakeup operation
  ITS infrastructure sends WUR wake-up trigger frame
  Pedestrian device wakes up and operates 802.11-OCB
Requirements
  Low power and low latency

## Slide 5: WUR Vehicle-to-Pedestrian (V2P)
Scenario
  Pedestrian carrying portable device.
  Roadside infrastructure such as an intersection or an oncoming vehicle sends WUR wake-up trigger frame containing ITS information.
Wakeup operation
  ITS infrastructure sends WUR wake-up trigger frame
  Pedestrian device receives and decodes ITS related information in the WUR wake-up trigger frame
Requirements
  Low power and low latency
  WUR trigger frame contains small amount of data

## Slide 6: Additional thoughts
Previous power-saving mechanisms in 802.11 were created with expense of high latency.
The combination of low power and low latency means WUR is capable of is applicable to more than just IoT.
Can WUR be transmitted in the DSRC channels 172-178 (aka 5.9 GHz band) and used to enhance V2X communications.

## Slide 7: Straw Poll
Should the 802.11ba task group consider intelligent transportation use cases for WUR?
  Yes
  No
  Maybe