## Slide 1: Protocols for Hybrid Beamforming in 802.11ay
Date: 2017-03-12
Authors:

## Slide 2: Hybrid Beamforming in 802.11ay
Hybrid beamforming has been proposed in 802.11ay to enable transmission of multiple streams for SU and MU-MIMO [1].
  It combines baseband beamforming with analog beamforming to improve performance
In this contribution, we show the performance gain of hybrid beamforming over analog beamforming with and without feedback in SU-MIMO Tx.
Finally, we present protocols to enable hybrid beamforming in SU/MU-MIMO.
Hybrid Beamforming Architecture
Analog Beamforming Architecture

## Slide 3: Current Specification (D0.2)
10.38.9.2.1 General
An EDMG STA may support hybrid precoding (defined as a combination of analog beamforming and digital baseband precoding) for SU-MIMO.
An EDMG STA may support hybrid precoding (defined as a combination of analog beamforming and digital baseband precoding) for MU-MIMO.
Editor Note: need to define the mechanisms to achieve the above.

## Slide 4: Hybrid Beamforming
=
Case 1: FA and FBB unknown
  Estimate H
  Design F for H
  Design FA / FBB from F
Case 2: FA and FBB unknown
  Estimate H
  Design FA and calculate HBB
  Design FBB from HBB
H = channel; HBB = effective baseband channel
FA = Analog beamformer; FBB = Baseband beamformer
F = Ideal baseband precoder; FAFBB = Hybrid beamformer; FAFBB ≈ F

## Slide 5: Beamforming Performance in 802.11ay
We will compare the relative performance of three beamforming methods in 802.11ay
Analog Beamforming with Random Selection:
  Design analog beamformer
  Randomly select N of the M Antenna Weighting Vectors (AWVs)
  No channel knowledge needed at transmitter
Analog Beamforming with Selection:
  Design analog beamformer
  Select the best N of the M AWVs
  Channel knowledge needed at transmitter
Hybrid Beamforming with ideal feedback:
  Design analog beamformer
  Feed back M-dimensional effective digital baseband channel.
  Use SVD based on the time domain channel matrix of the strongest path to transmit N streams

## Slide 6: Simulation Assumptions
Based on 11ad/ay SC PHY [2]
2 spatial streams with spatial stream parser
  Vertical Encoding
MCS index is the same for all streams per PPDU, single CRC per PPDU (use MCS 14: π/2 16QAM, rate ¾) [2]
MMSE receiver
Enterprise Cubicle (CB) scenario in 11ay/ad channel model [3]
STAs located on the table at a height of 0.7m in the cubicle
AP positioned in the middle below the ceiling at a height of 2.9 m
Real channel estimation at receiver
Detailed assumptions can be found in the appendix

## Slide 7: Simulated SU-MIMO Configurations
We implement the following beamformers:
  Analog beamforming random selection
  Analog beamforming with selection
  Hybrid beamforming
We simulate Configuration #4 of the SU-MIMO PAA configurations [3]
  4x4 channel, 2 PAAs with dual polarization on each side

## Slide 8: Numerical Results
Hybrid beamforming shows gain over both types of analog beamforming

## Slide 9: Protocols for Hybrid BF in 802.11ay
To implement hybrid BF in 802.11ay, we need the following:
  Initiator and Responder to agree on hybrid BF support.
    Indicate that initiator can perform hybrid BF
    Indicate that responder can feed back detailed information for a given configuration needed to support hybrid BF
      Note that the actual use of the HB is transparent to the responder
  Explicit baseband channel feedback for baseband precoder design. However, explicit feedback to enable HB is required.
Proposed protocol extends current procedures for SU-MIMO and MU-MIMO in D0.2 [4]

## Slide 10: SU-MIMO Hybrid BF Protocol
Exchange hybrid beamforming capabilities
  AP indicates support for hybrid BF
  STA indicates ability to feed back detailed channel information
AP indicates need for detailed feedback during MIMO setup
  Option 1: Detailed channel feedback occurs during MIMO feedback for SU-MIMO
    (D0.2: the feedback type for the responder link (e.g., SINR or time domain channel response)).
Option 2: Detailed feedback occurs after MIMO feedback: HBB feedback

## Slide 11: MU-MIMO Hybrid BF Protocol
Option 1: (No change between the BF setup and MU-MIMO selection): MU-MIMO FB Poll feeds back all channel details
  D0.2: The BF Feedback frame carries the list of received initiator’s transmit DMG antennas/sectors, each with its corresponding responder’s receive DMG antenna/sector and the associated quality indicated
  Indicate need for detailed feedback during setup
Option 2: (No change between the BF setup and MU-MIMO selection): request for detailed feedback after MU-MIMO selection : Digital Baseband Tracking (see [5])
Option 3: MU-MIMO selection different from BF setup : Digital Baseband Tracking (see [5])

## Slide 12: References
[1] K. Oteri et. al., “Beam Tracking for 802.11ay”, IEEE doc. 11-16/0040r2
[2] IEEE Std 802.11-2016, December 2016
[3] A. Maltsev, et al, “Channel models for IEEE 802 11ay”, IEEE doc. 11-15/1150r8
[4] IEEE P802.11ay™/D0.2, January 2017
[5] K. Oteri et. al., “Further Discussion on Beam Tracking for 802.11ay”, IEEE doc. 11-17/0426r0

## Slide 13: Straw Poll 1
Do you agree to update the 802.11ay specification to reflect that the detailed BRP feedback that occurs during SU-MIMO feedback may be used to support hybrid beamforming for SU-MIMO ?
  In scenarios where the detailed feedback is not carried in the SU-MIMO feedback, the initator may request for the detailed feedback at a later time (e.g. by digital baseband tracking if the device supports that capability).

## Slide 14: Straw Poll 2
Do you agree to update the 802.11ay specification to reflect that a detailed feedback option in the MU-MIMO feedback phase (fed back in addition to the associated quality specified in D0.2) may be used to support hybrid beamforming for MU-MIMO ?
  In scenarios where the detailed feedback is not carried in the MU-MIMO feedback, the initator may request for the detailed feedback at a later time (e.g. by digital baseband tracking if the device supports that capability).
  The channel feedback is TBD
Notes: Do you agree to the proposed hybrid beamforming protocol for SU-MIMO and MU-MIMO in the 802.11ay specification draft ?