## Slide 1: Receiver Architecture, Operational Channels, Power Consumption and Frequency Offset for 11ba
Date: 2017-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Neric Fong |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2
Possible Operational Channels for
11ba Wake-up Signals
Three possible options:
  One fixed channel for WUR in the whole 2.4GHz or 5.8GHz band
    Very inefficient; can not support large number of WUR stations. Given WUR signals need longer airtime, this is basically useless.
  For each 20MHz Channel, there is one fixed channel for WUR operation, say, the center 26-tone RU
    Better efficiency.
  Fully flexible, channelization needed for WUR operation. For example, in each 20MHz, there are can be a few WUR channels.
    Highest efficiency; support the large number of WUR stations.
We will compare the complexity and power consumption of these three options in the following slides.
  Along the comparison, we will also bring discussions on frequency offset and other PHY distortions.

## Slide 3: Basics on WUR Receiver
Given WUR Since WUR signals are transmitted over narrow band channels, out-of-band interferences must be taken care of.
  Note narrow-band analog filter in RF domain is not possible, for example, 2MHz analog filter in 2.4GHz or 5GHz needs extremely high Q and is not doable by state-of-the-art RF circuit design.
Narrow band filter can only be in analog baseband domain or digital filter in digital domain.
  Digital domain narrow band filter suffers two issues:
  Wide-band ADC is needed and wide-band ADC can consume power higher than 1mw itself.
  Interferences reduces the precision of ADC, therefore more bits needed for ADC and more bits translate to more power consumption.
  So Narrow band analog filter in analog baseband domain is the only possible choice.

## Slide 4: The Architecture of WUR Receiver
When narrow band filter is in Analog baseband domain, the WUR receiver must contain mixer. So the WUR receive architecture can be represented by the following:
Envelope
Detector

## Slide 5: Typical power consumption
Circuit Component | Current (uA) at 1V supply (uw) | Note
Frequency Synthesizer Open-loop (subject to frequency drift) Close-loop | ~400 to 600 ~1000 to 1500 | Open loop subject to large frequency drift
LPF | ~200 to 300 | 4-6-th order low-pass filter
XO | ~40 to 70 | Low frequency, low power
ADC (5B, fs = 2MHz) | ~10 to 20 | ADC power consumption rule: linear scaling with 62.5uA 6-bit per 20MHz ADC buffer Rule: 2X ADC current if ADC current > 50uA Else 0.
Total Open-loop RX (subject to frequency drift) Close-loop RX | ~700 to 900 ~1300~1900 | If envelope detector is applied, another 100uw may be saved.

## Slide 6: Answer to the Operational Channels
Since we need to handle the interferences, the mixer is unavoidable.
With the mixer is implemented, there are no extra cost or no extra power consumption to support fully flexible WUR channelization.
  A WUR station just need to adjust the center frequency of the mixer, then it can operates on a different WUR channel. This flexibility does not introduce any extra cost or power consumption!
Fully flexible WUR channelization can greatly increase the efficiency of WUR operations. For example, multiple WUR signals can be transmitted simultaneously within a 20MHz channel.

## Slide 7: Tolerance of Large Frequency offset
To keep the active power consumption for a WUR station below 1mw, the open loop frequency synthesizer is required.
For open loop frequency synthesizer, the frequency offset could be +/- 150ppm. So we need to add the frequency FO in the simulation scenario document d and function requirement document.

## Slide 8: Straw Poll #1
Do you agree that in each 20MHz channel, IEEE 802.11ba shall have multiple channels for the transmission of WUR signals?

## Slide 9: Straw poll #2
Do you agree that IEEE 11ba should support the WUR receivers with open-loop frequency synthesizers?