## Slide 1: Assign and Update Wake-Up Signals in WLAN with Wake-Up Radio Receivers
Date: 2017-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Russell Rongsheng Huang |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: False Wake-up Problems
      Main applications of WUR WLANs include IOT sensors running on batteries. Frequently falsely wake up the main receiver for a regular data packets can quickly drain the battery and ultimately disable the device.
      The following false wake-ups can happen in WUR WLAN
        False wake-ups due to wake-up signals collisions in dense OBSS environment;
        Wake-up attacks by self-generating wake-up signals or re-play wake-up signals.
      When a WUR station detects the false wake-ups or wake-up signal collisions, WUR signal should be updated or re-assigned.

## Slide 3: Assign or Update Wake-up Signals
Wake-up signals are assigned for each STA either:
  As part of the onboarding process, like how a password or a client certificate is provisioned to a STA before it is associated to an AP
  Or as part of the authentication and session key generation process
          Wake-up signals updating can be initiated either by STAs via sending a wake-up signal change request or by the AP via sending a packet that contains wake-up signal change entities directly.
  A WUR STA can initiate a request to change the wake-up signals
    When a STA repeatedly wakes up, but no meaningful regular packet is received or the received packet is not for itself. Then the STA can initiate a process of update of wake-up signals
  AP can initiate the update of wake-up signals
    When an AP detects there are collisions of wake-up signals from OBSS or AP needs to re-assign the wake-up signals for a STA or a group of STAs, then AP can initiate the update of wake-up signals directly.

## Slide 4: Wake-up signals updating
For wake-up signal updating, it is important to make sure that both the AP and the WUR station know if the update is successful.
  A simple send the packet and receive ACK scheme may not work well. For example, if the AP sends the packet with wake-up signal update information, the WUR station updated its wake-up signal, but the ACK is failed at the AP. Then the AP does not know if the WUR station has updated its wake-up signal or not.
The wake-up sequence update or assign is regarded as complete only after successful hand-shaking frame exchange.

## Slide 5: Sequence of Wake-Up Signals Update
AP initiated Wake-Up Signals Update for a single WUR STA:
STA initiated Wake-Up Signals Update:

## Slide 6: Sequence of Wake-Up Signals Update – Immediate ACK Case
In case there is no TXOP protection for the WU signal update message exchange, the exchange sequence can be divided into two updates from both AP and STA sides.
The ACK after SIFS is used instead of immediate UPDATE RSP.

## Slide 7: Sequence of Wake-Up Signals Update
Abnormal failure, for example the reception failure of ACK/UPDATE/RSP frames, will cause the inconsistence of sequence at both sides. Therefore we propose a bilateral handshake protocol.
The REQ and RSP messages both have retransmission mechanism in case of failed packet delivery.
AP update the WU signal for the target STA after receiving the ACK or RSP from the STA. The STA updates its WU signal after receiving the CFM from the AP.
If the RSP is not received by AP, or the CFM not received by STA, after a certain number of times of retransmission, the update procedure fails.
  If AP received a certain number of RSP retransmissions, AP can keep both previous and updated WU signals.
  In next WU signal transmission,
    if updated WU signal successfully wake up the STA, AP will delete the previous WU signal.
    if updated WU signal can not wake up the STA for a number of attempts, AP may try the previous WU signal.

## Slide 8: Straw Poll #1
Do you agree that IEEE 802.11ba shall provide a Wake-Up Signal update mechanism?

## Slide 9: Straw Poll #2
Do you agree the Sequence of Wake-Up Signals Update shown in slide #5?

## Slide 10: Straw Poll #3
Do you agree the Sequence of Wake-Up Signals Update shown in slide #6?