## Slide 1: Synchronization with Low Power Antenna
Date: 2017-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Sleep Mode of Low Power Wakeup Radio
A STA with 802.11 radio and low power radio may turn off both radios to save power:
  Through new defined 802.11 LP SP Negotiation Request/Response, STA and AP negotiates LP SP (start time, SP duration, interval of LP synchronization SP in LP TSF time) during which the STA turn on its low power radio to receive LP WUR frame (low power wakeup request).
    Out side of the negotiated SP, the STA turns off both .11 radio and low power radio.
In order for a STA whose LP radio goes to sleep to receive LP WUR, the low power radio of AP and STA should be synchronized.
.11 TSF (8 octets with 1 us granularity) low power (LP) TSF (6 or 8 octets with 1us or 4us granularity, other granularity is also possible) may be same or different.
  If .11 TSF and low power TSF are different, A STA with low power radio may only maintains LP TSF time.
Low power radio on
11 radio off
Low power radio on
11 radio offc
Low power radio on
11 radio off
Low power radio on
11 radio off
Low power radio off
11 radio off
Low power radio off
11 radio off
STA’s SP duration
STA’s SP duration
STA’s SP duration
STA’s SP interval
STA’s SP interval

## Slide 3: LP TSF Time Adjustment through LP WUR Only
During the STA’s LP synchronization SP, the AP transmits new defined LP WUR frame in LP PPDU to announce the LP TSF time, e.g. in 64-bit, 56-bit, 48-bit, 32-bit long or other suitable length. The STA adjusts its TSF time once the AP’s TSF time is received.
  LP WUR includes the LP TSF time when LP WUR frame is transmitted.
During the broadcast LP synchronization SP, the AP transmit broadcast LP WUR frame in LP PPDU to announce the LP TSF time, The STA adjusts its TSF time once the AP’s TSF time is received.
  LP WUR includes the LP TSF time when LP WUR frame is transmitted.
Type
BSS Color
FCS
Bits:
4
12
4
LP TSF Time
One of 64, 48, 32
Unicast LP WUR for LP TSF time announcement
Type
BSS Color
AID
FCS
Bits:
4
12
12
4
LP TSF Time
One of 64, 48, 32
Unicast LP WUR for LP TSF time announcement

## Slide 4: LP TSF Time Adjustment through LP WUR and .11 Management Frame
AP transmits broadcast LP WUR (low power wakeup Request) and records the LP TSF time when LP WUR is transmitted.
  Broadcast LP WUR frame includes Type, BSS Color, AID, FCS.
When .11 TSF time and low power TSF are same, Probe Response (or Probe Response with only TSF time in frame payload) is transmitted after LP WUR Announcement frame.
When .11 TSF time and low power TSF are different, a new LP TSF Time Announcement is defined and transmitted after LP WUR Announcement frame.
.11PHY Header
Lower Power PPDU which carries LP WUR
.11PHY Header
Broadcast Probe Response or LP TSF Announcement
WUR AP
WUR STA
TXOP
TXOP
Defer time
EDCA backoff before the frame exchange
Type
BSS Color
AID (may not be needed)
FCS
LP Wakeup Request (WUR)
Bits:
4
12
12
4
AP records the LP TSF time (AP LP TSF) when the frame is transmitted

## Slide 5: .11 TSF and Low Power TSF Difference Announcement
When .11 TSF and low power TSF are different, Probe Response, (Re-)Association Response, Beacon will carry the difference between .11 TSF and low power TSF Difference.
The low power STA sets its low power TSF per
  the received .11 TSF value,
  the difference between .11 TSF and low power TSF Difference.

## Slide 6: Reference
[1] 11-16-1460-01-wur-MAC consideration