## Slide 1: UL MU Ranging Options in Light of Rx Power Imbalances
Date: 2017-03-14
Authors:

## Slide 2: Abstract
This presentation conveys some reflections on choices of UL MU ranging options for location in light of the Rx power imbalances that can be present among UL MU users when they are received by an AP.

## Slide 3: UL MU Limitations for Ranging Measurements
11ax specifies support for two classes of client devices
  Class A, TX output power accuracy +/- 3dB and RSSI accuracy +/-3dB resulting in 12dB power discrepancy between peers for UL MU operation
  Class B, TX output power accuracy +/- 9dB and RSSI accuracy +/-5dB resulting in 28dB power discrepancy between peers for UL MU operation
UL MU operations may practically limited to Class A devices
  Tx power imbalance from Class B devices may caused too high errors in channel estimation and interference in data demodulation
Class B devices likely to be scheduled using temporal multiplexing for UL transmissions
Two approaches we could take
  Approach 1- allow spatially multiplexed UL MU ranging for Class A devices only and use temporally multiplexed UL MU ranging for Class B devices
    Results in two modes - Might not be desirable
  Approach 2 – support only temporally multiplexed UL MU ranging for both Class A & B devices
    Trading off potential downsides for Class A devices