## Slide 1: Buffer status report
Date: 2017-03-13
Authors:

## Slide 2: Problem statement
The two methods for reporting queue size (Queue Size field in QoS Data and BSR A-Control) are not compatible with each other.
  The Queue Size in QoS Data is reported per TID while Queue Size in BSR A-Control is reported per AC.
QoS control solution is the preferred option.
  Queue size report is present in every QoS Data frame
  AP must support for Queue Size reporting (Queue Size reporting is mandatory, BSR is optional)
But because of the incompatibility between QoS control and BSR A-ctrl, most of the STAs will use only QoS control.
  AP would need to record BSR report separately from Queue Size report since they are incompatible

## Slide 3: Problem statement
But QoS control is limited in size to 64 768 octets
While BSR A control defines a scaling factor of 2 bits to get the following max sizes:
  SF2: 520KB, SF3: 4.16MB

## Slide 4: Solutions
Most of the time, high throughput STAs will report the max buffers, and the AP will have hard time figuring out how to schedule the STAs
The best approach to solve the problem of buffer report (which is crucial for 11ax UL OFDMA performance) is to modify the scaling factor of the queue size in the QoS control field
  Propose a different unit for QoS control Queue size field for HE STAs

## Slide 5: Different options
Option 1: Fixed modified unit:
  256 octets for legacy, 2 048 for HE for instance
  No changes to the bit assignments of the QoS control field (8 bits queue size) - simple
  No Scaling factor: weaker granularity for small buffers, no saturation for high throughput STAs
Option 2: long term parametrization of a scaling factor for the whole BSS
  2 bits SF included in an IE in Beacons
  Queue size field in QoS control field value in units of 256 octets x SF for all STAs
  Static scaling factor for all STAs of the BSS

## Slide 6: Different options
Option 3: Per STA per TID long term parametrization of a scaling factor
  2 bits SF is included in ADDBA extension element to negotiate a scaling factor per TID per STA
  SF mapping identical to A-ctrl BSR
  Queue size field in QoS control field value in units of 256 octets x SF
  Static scaling factor to adapt to STA’s traffic
Option 4: Dynamic scaling factor included in QoS control field
  Repurpose MSB of TID field in QoS control field to have a 1-bit scaling factor, and keep 8 bits queue size
    Bit set to 0: queue size with units of 256 Octets (legacy)
    Bit set to 1: queue size with units of 2048 Octets

## Slide 7: Different options
Option 5:
  SF included in the 8 bits queue size of QoS control field
0-63 | 0 - 16128 bytes (units of 256 bytes)
64-191 | 18176 - 278272 bytes (units of 2048 bytes)
192-254 | 286464 - 794368 bytes (units of 8192 bytes)