## Slide 1: NDP-Based Measurement Protocol
Date: 2016-03-14

## Slide 2: Outline
Drawing from submission 17/0050r2, propose a NDP-based sounding sequence for the SU measurement protocol in 802.11az

## Slide 3: Motivation
Reuse 11ac PHY architecture for simplicity
Support SU operation for improving efficiency
  Where MU Operation is possible/preferred the protocol outlined in the submission 17/0050r2 will be used
Support MIMO and full bandwidth for enhanced accuracy

## Slide 4: Background
Measurement protocol includes two phases
  Channel sounding phase
  Measurements feedback phase
  These two phases can be within the same or different TxOPs

## Slide 5: Sounding Sequence
Similar to the NDP Sounding protocol described in Cl. 10.34.5 of IEEE 802.11-2016
  NDP Announce (.11az) is the VHT NDPA modified for use in .11az (modification details TBD)
  NDP (.11az) is the VHT NDP modified for use in .11az (modification details TBD)
  The timeline for the responder to respond with a Measurement Feedback frame is TBD
  The contents of the Measurement Feedback frame is TBD

## Slide 6: Conclusion
NDP-based measurement sequence is proposed as a SU range measurement protocol
Measurement protocol is similar to the VHT Sounding Protocol described in IEEE 802.11-2016 Cl. 10.34.5
MIMO and full bandwidth measurement are supported

## Slide 7: Motion
  We agree to the following text for 11az SFD under the “Accuracy and Coverage over 2.4 and 5GHz” subsection:
    The measurement phase for the ranging protocol for SU shall be based on IEEE 802.11 VHT sounding protocol and have the following frame exchange sequence:
    Note : the contents of NDP Announce (.11az), NDP (.11az) and Measurement Feedback; and the spacing between the NDP (.11az) and Measurement Feedback are TBD.

## Slide 8: Discussion

## Slide 9: Potential Measurement Feedback Content
Channel State Information (CSI)
  Channel estimates for obtaining ToD/ToA and/or AoA/AoD (SU case)
  Receiver of the CSI Feedback calculates ToA for both UL and DL (non-critical path calculation)
Location Measurement Response (LMR)
  ToD/ToA and AoA/AoD
  Sender of the feedback pays the computing power
Feedback sender can choose either CSI or LMR