## Slide 1: MIMO phase of SU-MIMO and MU-MIMO Beamforming
Date: 2017-04-05
Authors:

## Slide 2: Background: MIMO phase of SU-MIMO BF
The MIMO phase of SU-MIMO beamforming enables the training of transmit and receive sectors and antennas to determine best combinations of transmit and receive sectors and antennas for SU-MIMO operation, which comprises of three subphases [1]:
  SU-MIMO Setup (based on MIMO Setup frame)
  Initiator/Responder SU-MIMO Training (based on EDMG BRP-RX/TX packet)
  SU-MIMO Feedback (based on MIMO Feedback frame)

## Slide 3: Background: MIMO phase of MU-MIMO BF
The MIMO phase of MU-MIMO beamforming enables the training of transmit sectors and antennas of initiator and receive sectors and antennas of each responder intended to be part of MU group to determine best MU-MIMO configuration, which comprises of four subphases [1]:
  MU-MIMO BF Setup (based on BF Setup frame)
  MU-MIMO BF Training (based on EDMG BRP-RX/TX packet)
  MU-MIMO FB Poll (based on BF Poll frame and BF Feedback frame)
  MU-MIMO Selection (based on BF Selection frame)

## Slide 4: Proposal
Problem statement: Different terminologies are used for similar MIMO subphases of SU-MIMO BF and MU-MIMO BF, which may cause unnecessary confusion
  SU-MIMO Setup v.s. MU-MIMO BF Setup
  SU-MIMO Training v.s. MU-MIMO BF Training
  SU-MIMO Feedback v.s. MU-MIMO FB Poll
Unify terminologies for similar MIMO subphases of SU-MIMO BF and MU-MIMO BF
  SU/MU-MIMO BF Setup
  SU/MU-MIMO BF Training
  SU/MU-MIMO BF Feedback
Rename the MU-MIMO Selection subphase to the MU-MIMO BF Selection subphase in order to keep similar naming convention to other subphases.

## Slide 5: Proposal (cont.)
Problem statement: Different frames are used for similar purposes in the MIMO phase of SU-MIMO BF and MU-MIMO BF, which increases specification complexity
  SU/MU-MIMO BF Setup: MIMO Setup frame v.s. BF Setup frame
  SU/MU-MIMO BF Feedback: MIMO Feedback frame v.s. BF Feedback frame
Unify frames used for similar purposes in the MIMO phase of SU-MIMO BF and MU-MIMO BF
  SU/MU-MIMO BF Setup (based on MIMO BF Setup frame)
  SU/MU-MIMO BF Feedback (based on MIMO BF Feedback frame)
Rename the FB Poll frame to MIMO BF Feedback Poll frame and the BF Selection frame to MIMO BF Selection frame used in MU-MIMO BF in order to keep similar naming convention to other frames

## Slide 6: Proposal (cont.)
MIMO phase of SU-MIMO beamforming

## Slide 7: Proposal (cont.)
MIMO phase of MU-MIMO beamforming

## Slide 8: SP
Do you agree to incorporate the proposed changes on the MIMO phase of SU-MIMO beamforming and MU-MIMO beamforming as shown in IEEE 802.11-17/0541r0 into the next draft 11ay specification?
  Y
  N
  A

## Slide 9: Reference
[1] Draft P802.11ay_D0.3