## Slide 1: Wakeup Frame Length
Date: 2017-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Wakeup Frame Recap[2][3]
12-bit BSS color is long enough to avoid color collision.
AID can indicate broadcast/multicast/unicast receivers.
  AID may not needed for broadcast announcement, e.g. if multiple BSSID is not supported
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type combined AID can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement to announce new BSS operation parameters, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
BSS Color
AID
FCS
Bits:
3
12
11
4
TBD
Payload (Optional)

## Slide 3: Frame Length in 802.11 Baseline
PHY and combined with MAC indicate frame length in bytes.
  In Non-HT, HT PPDU, PHY header indicates the frame length in bytes.
  In VHT, HE PPDU, PHY header indicates the number of OFDM symbols, and MAC indicates the numbers of bytes.
It seems non-HT/HT/VHT/HE methods are not suitable for WUR frame length indication.
  WUR frames are like control frames which have fixed length.
  Length indication in bytes makes low power PHY header longer.

## Slide 4: Length of WUR Frame
The Length of WUR frames should be different for efficiency.
  WUR length for unicast announcement
  WUR length for broadcast announcement
  WUR length. for multicast announcement
  WUR length for Broadcast announcement with management information
  Each one has fixed length
The length of WUR frame is indicated by 2 bits with four different values.
  Another option is use 1 bit for two different values.

## Slide 5: Straw Poll 1
Do you support that WUR frames can have different length?

## Slide 6: Straw Poll 2
Do you support to indicate 4 different lengths in low power radio PHY header by two bits?

## Slide 7: Reference
[1] 11-16/1460R01 WUR MAC consideration
[2] 11-17/124R0 WUR MAC and Wakeup Frame
[3] 11-17/437R0 WUR MAC and Wakeup Frame