## Slide 1: WUR MAC and Wakeup Frame
Date: 2017-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Wakeup Frame Recap[2][3]
12-bit BSS color is long enough to avoid color collision.
AID can indicate broadcast/multicast/unicast receivers.
  AID may not needed for broadcast announcement, e.g. if multiple BSSID is not supported
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type combined AID can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement to announce new BSS operation parameters, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
BSS Color
AID
FCS
Bits:
3
12
11
4
TBD
Payload (Optional)

## Slide 3: Wakeup Frame Recap[3]
A group STAs can wake up together to receive group frames, receive DL MU PPDU.
Static groups (group ID, group member) which are similar to 11ac’s DL MU group are maintained through Action frame.
  An AP can allocates some AIDs which are not used by associated STAs as group ID.
Dynamic group (multicast group without group announcement/negotiation) are defined through different methods:
  Part of multicast MAC address is put in AID field of LP Wakeup frame.
  The hash result of multicast MAC address is put in AID field of LP Wakeup frame.
  AID bit map which is similar to AID bitmap of TIM element is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
  AID set which includes multiple AIDs is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
It seems that part of multicast MAC address or hash result of multicast MAC address being put in AID field of LP Wakeup frame is better for the reception of group frames. AID set/bitmap and/or sequential multiple LP Wakeup frames is better for DL MU reception.

## Slide 4: Proposed WUR Wake Up Frame
The Wakeup frame include
  Type,
    unicast,
    broadcast for data,
    broadcast for new management info,
    multicast
  BSS Identifier,
  Optional AID,
  Optional payload,
  FCS
Type
BSS Color
AID (optional)
FCS
Bits:
4
12
11
8
TBD
Payload (Optional)

## Slide 5: Straw Poll 1
Do you support LP WUR frames at least include the following fields
  Type
  AP identifier
  FCS

## Slide 6: Straw Poll 2
Do you support to have STA identifier in unicast WUR frame

## Slide 7: Reference
[1] 11-16/1460R01 WUR MAC consideration
[2] 11-17/124R0 WUR MAC and Wakeup Frame
[3] 11-17/437R0 WUR MAC and Wakeup Frame