## Slide 1: Indication for WUR Duty Cycle
Date: 2017-05-08
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com

## Slide 2: Abstract
In [1], it is agreed to have duty cycle mode for WUR STA
In [2], the view of duty cycle schedule from the STA is shared
In this presentation, we share our view of duty cycle service period/schedule negotiation, which aligns with the concept introduced in [2] with further flexibility

## Slide 3: Essential Parameters for duty cycle schedule negotiation
There are three essential parameters for duty cycle schedule negotiation
  On Duration
  Period
  Starting point of one schedule (through direct indication or reference point plus offset)
On Duration
Period
Offset
Reference point
On Duration
Period
Starting point

## Slide 4: Negotiation for Essential Parameters for duty cycle schedule negotiation
Our considerations for the design are to
  Simplify the negotiation procedure
  Have flexibility on the STA side based on different power/latency constraints
  Have flexibility on the AP side for optimizing schedules of different STA
Specifically, on the STA side,
  STA negotiates the on duration and period based on different power/latency constraints
  On duration and period follows certain rule indicated by AP (discuss below)
On the AP side,
  AP decides the starting point to optimize schedule
  AP indicates a basic unit of period such that the period negotiated by the STA is a multiple of the indicated basic unit from AP
  AP announces a minimum wake-up duration so that STA does not negotiate an on duration that is too short

## Slide 5: An example to illustrate the proposal
AP indicates unit T for the period
AP Indicates minimum wake-up duration ¼ T
AP decides starting point
STA negotiates on duration and period
STA2 DC=1/16
STA3 DC=1/12
STA4 DC=1/3
STA1 DC=1/4
2T
TON_1 = ½ T
4T
3T
3T
TON_2 = ¼ T
TON_3 = ¼ T
T (e.g. 10ms)
STA4 starts from t1
t0
t1
t2
t3
t4
t5
t6
t7
STA1, STA2, STA3 starts from t0

## Slide 6: Conclusion
We discuss WUR duty cycle schedule indication
We propose the following
  AP indicates the basic unit for the period of WUR duty cycle
  AP Indicates minimum wake-up duration for each WUR duty cycle schedule
  AP decides starting point
  STA negotiates on duration and period

## Slide 7: Straw Poll 1
Do you support the following?
  The period of the WUR duty cycle as shown below is a multiple of a basic unit
  The basic unit is indicated by the AP
  32 Y 0 N 17 A
Period
On Duration

## Slide 8: Straw Poll 2
Do you support the following?
  The on duration in each period for WUR duty cycle as shown below is larger than or equal to a minimum wake-up duration
  The minimum wake-up duration is indicated by the AP
  16 Y 2 N 22 A
Period
On Duration

## Slide 9: Straw Poll 3
Do you support the following?
  AP decides the starting point for one WUR duty cycle schedule
  How to indicate the starting point is TBD
  20 Y 0 N 20 A

## Slide 10: Motion 1
Move to add the following to 11ba SFD:
  The period of the WUR duty cycle as shown below is a multiple of a basic unit
  The basic unit is indicated by the AP
  Move: Po-Kai Huang
  Second: Bin Tian
  Y: 27 N: 3 A: 7
Period
On Duration

## Slide 11: Motion 2
Move to add the following to 11ba SFD:
  The on duration in each period for WUR duty cycle as shown below is larger than or equal to a minimum wake-up duration
  The minimum wake-up duration is indicated by the AP
  Move: Po-Kai Huang
  Second: Suhwook Kim
  Y: 28 N: 1 A: 9
Period
On Duration

## Slide 12: Motion 3
Move to add the following to 11ba SFD:
  AP decides the starting point for one WUR duty cycle schedule
  How to indicate the starting point is TBD
  Move: Po-Kai Huang
  Second: Suhwook Kim
  Y: 26 N: 0 A: 9

## Slide 13: Reference
[1] 11-17-0342-04-00ba WUR Negotiation and Acknowledgement Procedure Follow up
[2] 11-17-0364-00-00ba Low Latency and Medium Utilization