## Slide 1: Multiple Data Rates for WUR
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Recap on [1]
Various symbol types for multiple data rates were introduced
Symbol Types | Data Rate [Kbps] | Pros | Cons
Normal OOK symbol | 250 | - Simple | - Long off duration
Manchester code based OOK symbol | 250 | - Short off duration | - Additional procedure for 2us signal generation
Symbol repetition (n=2) (Manchester code is applied) | 125 | Good performance | - Large overhead
Symbol time reduction (n=2) | 500 | Small overhead | - Poor performance - Additional procedure for 1us (if the Manchester code is applied) or 2us signal generation

## Slide 3: Need for Multiple Data Rates
WUR can benefit from having multiple data rates considering various use cases including both indoor and outdoor cases [2]
The data rate needs to be lower than 250 Kbps as shown in [3] considering the requirement of 11ba which is the same range as the primary connectivity radio [4]
  Data rate of 125Kbps with 8us symbol time using the Manchester code can be a proper option in terms of the performance, overhead and coexistence issue [1][5][6]
    As shown in Appendix, at the data rate of 125Kbps with 8us symbol time, using the Manchester code has a better performance compared to not using the Manchester code in both channel cases assuming 10% PER
    Also, among several data rates considered in this contribution, it can only guarantee the range requirement as shown in the link budget analysis in Appendix
    In addition, the Manchester code can prevent a coexistence problem by reducing an off duration significantly
    Furthermore, a threshold for decoding is not required when using the Manchester code
  A much lower data rate can be also considered (e.g., 62.5Kbps with 16us symbol time) in order to further enhance the performance at the expense of the overhead which incurs a power consumption increase

## Slide 4: Need for Multiple Data Rates
On the other hand, for STAs located near the AP (good link quality), it may be advisable to use higher data rate
  Those STAs have a sufficient received SNR to use higher data rate and thus a low data rate and a long symbol length may be too much burden and waste on them
  Hence, the data rate of 250Kbps with 4us symbol time (such as the normal OOK or the Manchester code based OOK symbol types in [1]) can be considered
    We can derive benefit from applying Manchester code especially in the indoor case
    However, this data rate still can be a burden on some STAs which are located quite close to the AP
  We can also think of data rates of 500Kbps with 2us symbol time or 1Mbps with 1us symbol time (i.e., the symbol time reduction type in [1]) to further increase the data rate and to reduce the overhead which results in a less power consumption at the receiver
    Assuming the target PER of 10%, these data rates seem only applicable to the indoor case because they cannot guarantee it in the UMi channel as shown in Appendix
    The difference between required SNRs of two data rates is not huge in the indoor case and thus there may be a chance to use even much higher data rate
    In addition, the Manchester code can be also applied with a slight performance degradation

## Slide 5: Conclusion
For the range requirement, WUR needs to use the data rate of 125Kbps or lower data rate
For STAs having a high received signal strength, WUR can benefit from utilizing the data rate of 500Kbps or higher data rate
It is desirable to apply the Manchester code to all of the data rates because of its advantages in terms of the coexistence issue, receiver complexity, etc.

## Slide 6: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  11ba supports multiple data rates for the payload part of the wake-up packet
Y/N/A : 24/0/5

## Slide 7: Straw Poll #2
Do you support to have two data rates for WUR?
Y/N/A

## Slide 8: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  11ba uses the Manchester code for all of the data rates for the payload part of the wake-up packet
Y/N/A : 11/0/14

## Slide 9: Straw Poll #4
Do you agree to add the following to the 11ba SFD?
  11ba uses 125Kbps as one of the data rates
Y/N/A

## Slide 10: Straw Poll #5
Do you agree to add the following to the 11ba SFD?
  11ba uses 500Kbps as one of the data rates
Y/N/A

## Slide 11: Straw Poll #6
Do you agree to add the following to the 11ba SFD?
  11ba uses 1Mbps as one of the data rates
Y/N/A

## Slide 12: Straw Poll #7
Do you agree to add the following to the 11ba SFD?
  11ba uses 250Kbps as one of the data rates
Y/N/A

## Slide 13: Straw Poll #8
Do you agree to add the following to the 11ba SFD?
  For the data rate of 125Kbps, each symbol consists of 4us OFF- and ON-Signals and indicates only one bit information (‘0’ or ‘1’) as follows
    The method for computing 4us ON-Signal is TBD
Y/N/A
Symbol for information ‘0’ | Symbol for information ‘1’
4us ON-Signal + 4us OFF-Signal | 4us OFF-Signal + 4us ON-Signal

## Slide 14: Straw Poll #9
Do you agree to add the following to the 11ba SFD?
  For the data rate of 500Kbps, each symbol consists of 1us OFF- and ON-Signals and indicates only one bit information (‘0’ or ‘1’) as follows
    The method for computing 1us ON-Signal is TBD
Y/N/A
Symbol for information ‘0’ | Symbol for information ‘1’
1us ON-Signal + 1us OFF-Signal | 1us OFF-Signal + 1us ON-Signal

## Slide 15: Straw Poll #10
Do you agree to add the following to the 11ba SFD?
  For the data rate of 1Mbps, each symbol consists of 0.5us OFF- and ON-Signals and indicates only one bit information (‘0’ or ‘1’) as follows
    The method for computing 0.5us ON-Signal is TBD
Y/N/A
Symbol for information ‘0’ | Symbol for information ‘1’
0.5us ON-Signal + 0.5us OFF-Signal | 0.5us OFF-Signal + 0.5us ON-Signal

## Slide 16: Straw Poll #11
Do you agree to add the following to the 11ba SFD?
  For the data rate of 250Kbps, each symbol consists of 2us OFF- and ON-Signals and indicates only one bit information (‘0’ or ‘1’) as follows
    The method for computing 2us ON-Signal is TBD
Y/N/A
Symbol for information ‘0’ | Symbol for information ‘1’
2us ON-Signal + 2us OFF-Signal | 2us OFF-Signal + 2us ON-Signal

## Slide 17: Motion #1
Move to add the following to the 11ba SFD
  11ba supports multiple data rates for the payload part of the wake-up packet
Move : Eunsung Park
Second :
Y/N/A :

## Slide 18: Motion #2
Move to add the following to the 11ba SFD
  11ba uses the Manchester code for all of the data rates for the payload part of the wake-up packet
Move : Eunsung Park
Second :
Y/N/A :

## Slide 19: References
[1] IEEE 802.11-17/0350r0 Various Symbol Types for WUR
[2] IEEE 802.11-17/0029r5 WUR Usage Model Document
[3] IEEE 802.11-17/0365r0 Regulations and Noise Figure - Impact on SNR
[4] IEEE 802.11-16/1045r9-0wur-a-par-proposal-wur-sg
[5] IEEE 802.11-17/0366r1 WUR Modulation and Coding
[6] IEEE 802.11-17/0367r0 Studies of PER Performance
[7] IEEE 802.11-17/0188r4 Simulation Scenario and Evaluation Methodology
[8] IEEE 802.11-17/0326r0 WUR Phase Noise Model Follow-Up

## Slide 20: Appendix

## Slide 21: Simulation Assumption (1/2)
13 subcarriers are used for a symbol computation
  A sequence mapped to 13 subcarriers in each symbol type is optimized in terms of the PAPR
Payload consists of 48 symbols
  Symbol structure is dependent on the symbol type
  PER for payload will be shown
  If 48 bits are set to the MAC address, PER is equivalent to the miss detection
CFO [7], Phase noise [8] applied
No timing error
Raised cosine filter with 4MHz bandwidth and 0.2 roll off factor
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz
SNR is defined considering 20MHz bandwidth
L-SIG performance with no CFO, no STO

## Slide 22: Simulation Assumption (2/2)
125Kbps (8us symbol)
250Kbps (4us symbol)
500Kbps (2us symbol)
1Mbps (1us symbol)
 | Symbol for information ‘0’ | Symbol for information ‘1’
Option 1 | 4us ON-Signal + 4us OFF-Signal | 4us OFF-Signal + 4us ON-Signal
Option 2 | 8us OFF-Signal | 8us ON-Signal
 | Symbol for information ‘0’ | Symbol for information ‘1’
Option 1 | 2us ON-Signal + 2us OFF-Signal | 2us OFF-Signal + 2us ON-Signal
Option 2 | 4us OFF-Signal | 4us ON-Signal
 | Symbol for information ‘0’ | Symbol for information ‘1’
Option 1 | 1us ON-Signal + 1us OFF-Signal | 1us OFF-Signal + 1us ON-Signal
Option 2 | 2us OFF-Signal | 2us ON-Signal
 | Symbol for information ‘0’ | Symbol for information ‘1’
Option 1 | 0.5us ON-Signal + 0.5us OFF-Signal | 0.5us OFF-Signal + 0.5us ON-Signal
Option 2 | 1us OFF-Signal | 1us ON-Signal

## Slide 23: Simulation Results
PER comparison
TGnD channel
UMi NLoS channel

## Slide 24: Link Budget
Received SNR
Rx_SNR = Tx_Pwr - PL – 3*Shadowing - NF - N0
Transmit power : Tx_Pwr = 20dBm
Noise figure : NF = 15dBm (802.11ba) / 7dBm (conventional 802.11)
Noise floor : N0 = -174dBm + 10log10BW
Bandwidth : BW = 20MHz
Target PER : 10% (802.11ba) / 1% (conventional 802.11)
No interference
No penetration loss

## Slide 25: Link Budget
TGnD channel
Conventional 802.11
802.11ba

## Slide 26: Link Budget
UMi NLoS channel
Conventional 802.11
802.11ba