## Slide 1: OOK Signal Bandwidth for WUR
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
As shown in [1][2], it is advisable that WUR uses a narrow signal bandwidth given both the performance and the power consumption
  In [1], it was verified that the performance is affected by the sampling rate and is degraded when the signal bandwidth is lower than the sampling rate which may be low in order to reduce the power consumption
  In [2], it was also shown that the power consumption of ADC is related to the signal bandwidth, i.e., the narrower signal bandwidth, the less power consumption of ADC
Thus, by taking into account several narrow signal bandwidths (such as 1, 2, 3, 4 and 5MHz), we investigate the PER performance and compare it with the L-SIG performance to provide insight on the signal bandwidth WUR should use
  WUR receiver noise figure is 8dB worse than that of the conventional Wi-Fi as shown in [3], and thus the required SNR of WUR at the target PER should be 8dB better than the conventional one to meet the range requirement of 11ba

## Slide 3: Simulation Assumption
3, 6, 10, 13 and 16 subcarriers are used for a symbol computation of signal bandwidths of 1, 2, 3, 4 and 5MHz, respectively
  A sequences mapped to available subcarriers are optimized in terms of the PAPR
Payload consists of 48 symbols
  Each symbol has the data rate of 125Kbps with 8us using the Manchester code
  If 48 bits are set to the MAC address, PER is equivalent to the miss detection
CFO [3], Phase noise [4] applied
No timing error
Raised cosine filter with roll off factor of 0.2
  Only the available part (i.e., signal bandwidth) is filtered out
Sampling rate of 20MHz
TGnD and UMi NLoS channels in 2.4GHz
SNR is defined considering 20MHz bandwidth
L-SIG performance with no CFO, no STO

## Slide 4: Simulation Results
PER performance
TGnD
UMi NLoS
Note that the performance does not change until the sampling rate of 5MHz at least as shown in Appendix

## Slide 5: Discussion
Assuming the target PER of 1% and 10% for L-SIG and WUR, respectively, the required SNRs are obtained as follows
If we take the noise figure into account, 3, 4 and 5MHz may be proper options
  Those cases have almost 8dB better required SNR than that of L-SIG
  Note that the actual performance on L-SIG can be further degraded due to several impairments
We can utilize the signal bandwidth of 1 or 2MHz by applying more robust data rate (e.g. 62.5kbps with 16us symbol time)
  However, from the fact that the power consumption is proportional to the signal bandwidth and the decoding time, the gain may be marginal in terms of the power consumption when using the signal bandwidth of 1MHz or 2MHz with a longer symbol time (e.g. 16us) compared to the bandwidth of 4MHz with the symbol time of 8us
  Furthermore, it incurs a severe overhead increase
To determine the signal bandwidth, we also need to consider regulatory power limit [5] and DFS channel issue on the 5GHz band [6]
  Due to those factors, it is hard to use an extremely narrow signal bandwidth
 | 1MHz | 2MHz | 3MHz | 4MHz | 5MHz | L-SIG
TGnD | 1.2 | -0.3 | -1.3 | -1.3 | -1.4 | 6.2
UMi NLoS | 3.6 | -0.1 | -1.2 | -1.3 | -1.4 | 14.6

## Slide 6: Conclusion
Considering only the performance, the signal bandwidths of 3, 4 and 5MHz are preferred for WUR
Among three candidates, the signal bandwidth of 5MHz is the worst in terms of the power consumption
Among three candidates, the signal bandwidth of 3MHz is the worst in terms of the regulatory power limit and DFS channel issue on the 5GHz band
Consequently, if we consider all of the above, it may be advisable to apply the signal bandwidth of 4MHz to the WUR

## Slide 7: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  The OOK waveform of wake-up packet is generated by populating thirteen 802.11 OFDM subcarriers including DC
Y/N/A : 21/0/19

## Slide 8: Straw Poll #2
Do you agree to add the following to the 11ba SFD?
  For the transmission of a wake-up packet using one sub-band, the OOK waveform of wake-up packet is generated by populating 802.11 OFDM subcarriers with the subcarrier spacing of 312.5KHz from -6 to 6
Y/N/A : 13/7/29

## Slide 9: Motion
Move to change the 11ba SFD as follows
  R.3.3.B: For the transmission of wake-up packet using one sub-band, tThe OOK waveform of wake-up packet is generated by populating contiguous thirteen TBD number of 802.11 OFDM subcarriers with the subcarrier spacing of 312.5KHz
    The WUR preamble part is TBD
    The operation in DFS channel is TBD
    Subcarrier indices are TBD
    Coefficients are TBD
Move : Eunsung Park
Second :
Y/N/A :

## Slide 10: References
[1] IEEE 802.11-17/0351r0 Effect of Bandwidth and Sampling Rate on Performance
[2] IEEE 802.11-17/0432r0 Receiver Architecture, Operational Channels, Power Consumption and Frequency Offset for 11ba
[3] IEEE 802.11-17/0188r4 Simulation Scenario and Evaluation Methodology
[4] IEEE 802.11-17/0326r0 WUR Phase Noise Model Follow-Up
[5] IEEE 802.11-17/0365r0 Regulations and Noise Figure - Impact on SNR
[6] IEEE 802.11-17/0377r0 False Radar Pulse Detection on WUR Signal

## Slide 11: Appendix

## Slide 12: Simulation Results
PER performance with the sampling rate of 5MHz
TGnD
UMi NLoS