## Slide 1: Motion on Manchester Coding
Date: 2017-05-07
Authors:

## Slide 2: Introduction
In March [1] we presented simulation results comparing Repetition Coding to Manchester Coding
  Provided in the Backup
We also provided a summary of the benefits of Manchester Coding
A straw poll on Manchester Coding was also held in March
A brief summary will be provided here followed by a Motion on Manchester Coding

## Slide 3: Benefits of Manchester Coding
Manchester coding provides multiple benefits in the WUR PHY Design
1-2 dB SNR advantage over repetition coding, in all channel conditions simulated
Simple implementation. No need to estimate detector threshold.
When there is interference, there is no bias in bit errors. There is equal number of 0 →1 and 1 →0 errors
Ensure 50% waveform duty cycle
Avoid long periods of zero waveform.
  A long period of zero waveform can cause false CCA channel availability detection
  Ensure good waveform structure for symbol clock recovery at the receiver

## Slide 4: March Straw Poll Results [1]
Do you support using Manchester Coding in the WUR PHY Design?
  The structure of the OFDM symbol and the data rate is TBD
  The Preamble design is TBD
Yes: 31
No: 10
Abstain: 22

## Slide 5: Motion
Apply Manchester Coding in the WUR PHY Design
  The structure of the OFDM symbol and the data rate is TBD
  The Preamble design is TBD
Move: Steve Shellhammer
Second: John Notor
Yes: 37
No: 0
Abstain: 0

## Slide 6: References
Steve Shellhammer and Bin Tian, “WUR Modulation and Coding, IEEE 802.11-17/366r1,” March 2017

## Slide 7: Backup Slides (From [1])

## Slide 8: Simulations
Comparison of Three Designs for DATA Field
  All designs on-off modulate the 4 µs OFDM symbols
  10 bit preamble and 100 bit payload
  The exact data rate has not yet been specified. We consider one two methods of improving receiver sensitivity (at lower data rate)
Baseline Multicarrier Multicarrier OOK (250 kb/s)
2x Repetition Code (125 kb/s)
  0 → (0, 0)
  1 → (1, 1)
Manchester Code (125 kb/s)
  0 → (0, 1)
  1 → (1, 0)

## Slide 9: Simulation Model
Applied a Third Order Butterworth Filter to remove noise beyond the signal bandwidth
Used Envelope Detector for low-power non-coherent receiver

## Slide 10: Demodulation – OOK & Manchester Coded OOK
OOK Demodulation requires calculation of detector threshold based on preamble signal
Manchester code Demodulation does not require calculation of threshold based on preamble signal

## Slide 11: Simulation – AWGN

## Slide 12: Simulation – Channel Model D

## Slide 13: Simulation – UMi Channel