## Slide 1: Additional Elements for WUR
Date: May 7 2017
Authors:
Name | Affiliations | Address | Phone | Email
James Lepp | BlackBerry Limited | 1001 Farrar Road, Ottawa, ON, Canada | (+1) 613-595-4156 | jlepp@blackberry.com

## Slide 2: Summary
Additional ideas for elements in the WUR Wake-up Trigger Frame to enable STA power saving
  Source MAC Address is useful for power saving
  Full Groupcast MAC Address is useful for power saving
  Can we shorten groupcast MAC Addresses?

## Slide 3: WUR MAC so far
(1) Most discussion has been around two addresses (transmitter/AP and receiver/STA).
Need further discussion about the impact on the WUR STA of losing the third address (i.e. the source)
(2) Decisions have been made to use shortened identifiers as opposed to full length MAC addresses in WUR.
Need further discussion about the impact on group addresses (multicast and broadcast).

## Slide 4: 802.11’s Three Address Legacy – “downlink” frames
Typical transmission “downlink” from AP to STA:
Source
Transmitter
Receiver/Destination (these are the same in this case)
LAN
AP
STA
STA
STA
Source
Address/Identifier
Transmitter
Address/Identifier
Receiver
Address/Identifier
*Simple Case (non-mesh, non-GLK)

## Slide 5: Source MAC address - use in Saving Power
AP receives frame addressed to a STA in the WUR-sleep state. This can be individually addressed or group addressed.
AP transmits a Wake-up Trigger Frame with the corresponding short identifier (individual or group addressed)
Sleeping STA may not think its worthwhile to wake up for groupcast or chatty neighbors on the LAN/WLAN.
If additional information is available in the Wake-Up Trigger Frame (such as the source address), the STA may stay asleep and ignore messages.

## Slide 6: Source MAC Address
Provide the third address! “Source”
Enable the STA to know where the message came from to determine if its worth waking up for.
Receiver
Transmitter
Source Addr
Other Elements Address

## Slide 7: Benefits of Source MAC Address
Benefits of providing the Source address:
Single purpose IOT devices can sleep through messages from chatty neighbours and only wake-up for messages from the gateway/hub (or any other particular server/device)
If WUR devices are waking up for ARP or mDNS packets 5 times per minute they won’t achieve the power saving targeted in the PAR

## Slide 8: Groupcast Addresses
Proposal has been to reuse AID as receiver address. Sounds reasonable for unicast since AIDs are assigned in the BSS and known to the AP.
How do we shorten a Group Address to be less than the MAC address of the LAN/WLAN device?
Some Multicast and Broadcast addresses are “well-known”.

## Slide 9: Groupcast MAC Address
AID is 11 bits (could be 13 bits from 11ah)
BSS Color is 6 bits (“a value of 1-63” [802.11ax D1.2])
Problem: Groupcast MAC addresses are 47 bits which is much bigger than the AID field
One solution is to convey full MAC address as an element but only when necessary
Receiver
Transmitter
11 bits
6 bits
Elements
Extensible
Groupcast flag
BSS Color
Full Group Address
Elements Address

## Slide 10: Shortening Groupcast Addresses
Regarding groupcast frames, STA needs to decide which groupcast frames to wake up for reception of, and which to sleep across to maximize power saving
Well-known IP addresses turn into well-known MAC addresses via RFC 1112
Is there a way WUR can fit some of these well-known addresses into the AID-sized header field
48-bit address | Commonly used by:
01:00:5E:00:00:FB | IPv4 Bonjour
FF:FF:FF:FF:FF:FF | IPv4 ARP
33-33-00-00-00-01 | IPv6 Neighbor Advertisement
33-33-00-00-00-02 | IPv6 Router Solicitation
33:33:00:00:00:FB | IPv6 Bonjour

## Slide 11: Strawpoll #1
Should TGba consider Source MAC Address and Groupcast MAC address as optional elements in the WUR Wake-up trigger frame?
Yes
No
Abstain

## Slide 12: Strawpoll #2
Should TGba consider a solution to shorten well-known groupcast MAC addresses?
Yes
No
Abstain