## Slide 1: Preamble Design for WUR WLAN
Date: 2017-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Format of wake-up radio (WUR) packet
A WUR packet is a wake-up signal that can be received and resolved by wake-up receivers of WUR stations. A typical format of a WUR packet is shown as the following figure.
  Preamble: contains on-off keying sequences for automatic gain control and frequency/timing synchronization. The timing synchronization can be done through a signature sequence matching.
  Control Information contains the identification of AP (such as, BSS color), the identification of the target station/group (such as assigned ID for the station/group) and wake-up control field.
  To avoid complexity and reduction of efficiency, error control coding shall not be applied to WUR packet.
  However, a cyclic redundancy check (CRC) shall be applied to the control information to avoid false wake-ups due to reception errors.

## Slide 3
Preamble Design of WUR packet
The preamble serves a few purposes:
  Automatic gain control (AGC):
    To adjust the received signal strength to reduce distortions.
  Timing Synchronization:
    To obtain the correct sampling time to minimize the non-coherent detection error.
  Packet detection:
    To identify the WUR packet is received.
  Boundary detection
    To detect the boundary of preamble and control information
  Rate indication: information can be transmit using different data rates.
Packet detection, Boundary detection and rate indication can be realized by insert signature sequences into the preamble.

## Slide 4
Preamble structure:
The AGC/sync-up sequence should enable the following properties:
  Each symbol should be OOK modulated.
  The sequence should guarantee that the power measurement is stable and therefore settles the AGC quickly.
  The sequence also accelerates synchronization by measuring the power within each symbol.
    To find at least symbol boundary for OOK demodulation.
Preamble Design

## Slide 5: AGC and Sync Sequence
We propose that the AGC/sync-up sequences is designed as a sequences with alternative “1” and “0”, such as 1 0 1 0 1 0…, where each symbol 1 or 0 is OOK modulated.
  If each symbol is 4us and when the WUR receiver measures using 8us, then for any measuring window (without synchronization), the power measurement variations are minimized. Therefore AGC adjustments are accurate and quick.
  The sequence also accelerates synchronization by measuring the power within each symbol. The symbol boundary can be easily detected by choosing the 4us window with maximum power.

## Slide 6: WUR signature sequence design
WUR signature sequence is a special sequence with random “1” and “0”, for example, the sequence can be a Barker sequence, a pseudo-random sequence or a Golay sequence.
  Note the common information can be used as signature sequence as well, for example, BSS color.
The WUR receiver relies on the detection of WUR signature sequence to claim the WUR packet detection and to find the boundary between preamble and control information.
  WUR signature sequence should be on-off keying modulated or on-off keying with Manchester coding to enhance the reliability.

## Slide 7: WUR signature sequence design for multi-rate
Since the control information can be transmit with different data rate for different coverage, WUR signature sequence is used also as an indicator of the data rate of WUR packet.
  WUR receiver needs to know the data rate for detection and decoding.
  Our design is to introduce multiple signature sequences and each signature sequence indicates one specific data rate.
    For example, the data rate of the control information can be 125kbps, 250Kbps or 500kbps. Then 3 different signature sequences with large hamming distance are used. The first signature sequence indicates data rate 125kbps, the second signature sequence indicates 250kbps and the third signature sequence indicates 500kbps.
If the data rate is indicated by SIG field, then the SIG field must use the lowest data rate, which causes significant efficiency reduction.
  For example, if the lowest data rate is 125Kbps, then compared to 500Kbps, the efficiency is reduced by more than 3 times!

## Slide 8: Straw poll #1
Do you agree to that the preamble of WUR packet shall be OOK modulated?

## Slide 9: Straw poll #2
Do you agree that the AGC/Sync sequence shall be a sequence with alternative “1” and “0”, such as “1 0 1 0 …”?
  The length of the sequence is TBD.

## Slide 10: Straw poll #3
Do you agree to use different signature sequence to indicate the different data rate if multiple data rates are used for the control information in WUR packets?
  The detailed signature sequence is TBD.