## Slide 1: Wake up packet contents
Date: 2017-05-10
Authors:

## Slide 2: Background
Wake-up packet (WUP) structure is proposed in [1-5]
  WUP structure with legacy preamble part, WUP preamble part and WUP payload part are proposed by many contributors.
  Legacy preamble to protect the WUP packet and spoofing other legacy devices
  WUP preamble part can help WUR STA to
    Adjust AGC, synchronization, packet detection and signal the rate of the following WUP payload part [6].
  WUP content part shall include type field, Tx id field and other contents vary for different type of WUPs.
    Possible type includes WU beacon, SU addressed WUP, group addressed WUP etc.
Legacy preamble part
WUP preamble
Contents in WUP payload
Frame type
Transmitter ID
Receiver ID
OOK modulated part
Other information
May not include
Receiver ID in
Some WUP types.

## Slide 3: WUP contents for WU beacon
WU beacon [7] will be defined to maintain connection and synchronization for WUR STAs.
  TSF/partial TSF is proposed for synchronization. Other information TBD.
We propose to allow WU information appending to the beacon
  Can save the WUP overhead and reduce latency for WUR STAs.
  Appended fields can include Receiver ID or Group ID with additional control information such as wake up complete time(WCT), access category (AC) etc. Existence of appending WU info can be signaled in frame type field.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
TSF
TBD info
type = BEACON
Appending WU info
Receiver ID/Group ID
Type
Frame type = BEACON with WU info
Control info

## Slide 4: WUP contents for WU beacon – cont’d
For WUR STAs in duty cycle mode, appending WU info can
  Reduce latency for WUR STAs. AP do not need to wait till target WUR STA’s next “on duration” to send a WUP.
  Overhead saving. Appending WU info to a beacon can save the overhead of one legacy preamble, one WUR preamble, fields like Frame type and Tx ID etc and also one channel contention.
  Almost no cost for these benefits.
AP:
WUR STA:
WUR on duration for beacon
WUR beacon with
appended WU info
WUR on duration for non beacon WUP
AP:
WUR STA:
Beacon
WUR on duration for beacon
WUR beacon
WUR on duration for non beacon WUP
WUP
WUP

## Slide 5: Content of SU addressed WUP
Propose to include a priority/Access category field
  Priority field indicates the highest AC of the buffered DL data for the target STA.
  For WUP types that not wake up STA for DL traffic, this field may not be included.
  Benefit:
    WU STA can send PS_POLL based on the indicated access category.
      Unlike conventional PS_POLLs after beacon, number of PS_POLLs responding to WUP will be much smaller hence should use higher AC to contend the channel. Allow STA using the data’s AC for PS_POLL is natural.
    WU STA can decide whether wake up or not. In low battery mode, STA may choose to wake up less frequently or wait until higher priority data arrives.
Propose to allow including partial TSF in all type of WUPs
  Early timing synchronization always help WUR STAs to save the power.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
Receiver ID
Priority (AC)
TSF
type = SU
Other info such as WCT etc.

## Slide 6: Content of SU addressed WUP – cont’d
Partial TSF in WU beacon is a synchronization scheme guarantees a minimum sync performance but not necessary the only scheme.
  Earlier timing synchronization always benefit the WU STA’s power consumption.
    WUR STA in duty cycle mode need to gradually increase the “on duration” to compensate the timing mismatch.
    Upon receiving a WUP with TSF sent by the AP, all WUR STAs associated with the AP can get synchronized and reduce the “on duration” close to the minimum “on duration”.
    Partial TSF may only have a few(8?) bits. A small overhead increasing could benefit many WUR STAs in the BSS.
    For 200ppm clock accuracy, minimum “on duration” 2ms, the WUR STA’s actual on duration will be 4ms after 5 seconds. A WUP with partial TSF will bring it back to ~2ms.
AP:
WUR STA:
WUR beacon
WUP with TSF
Minimum on duration
Length of “on duration” can be reduced
after receiving a WUP with TSF.

## Slide 7: Contents of group addressed WUP
Group ID with a TIM is introduced in [2]. We propose to include a per user field for each WUR STA indicated in the TIM.
  Number of per user fields and order of per user fields are decided by the TIM field.
  Per user field can include the AC for this user and other TBD control information.
  WCT can also be signaled in per user field to be more flexible or signaled outside the per user field as a common WCT to save the overhead.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
Group ID
TIM for group
Per User fields
Common WCT
TSF
type = Group
0 0 1 … 0 1 0
Per User field 1
N bits TIM
Per User field 2
…
Per User field K
Indicating user 1
user K

## Slide 8: Problem of WUP carrying more info
Overhead
  Based on WUR’s use cases, WUR STAs have very low duty cycle (minutes, hours or even days). Increasing a few micro seconds overhead at such low duty cycle is negligible. For example: 1000 sensors working at 1 hour duty cycle. 100us extra length in WUR for each sensor will lead to a total ~0.1s extra overhead per hour.
  We care more on power consumption for WUR STAs. If the additional information can help WUR STAs further save some power, a little bit more overhead is a worth tradeoff.
Reliability – The problem people really care
  Longer WUP will lead to less reliability. This is the real problem for a WUP to carry more information.
  This problem can be solved by WUP segmentation and separate FCS check for each WUP segment.

## Slide 9: Segmented FCS check for WUP
We propose to use multiple FCS to check segments of a WUP.
  Different part of WUP has different importance. Some information are more essential while other information improve the performance but WUR STAs still work without these parts.
  One FCS to check the essential segment including frame type, transmitter ID, receiver ID fields etc. If this segment failed, the whole WUP shall be discarded.
  WUR still works without WCT, AC and TSF field etc. These fields shall be placed in other segment(s). The non-essential information fields can also be partitioned into segments and check by separate FCSs. More FCSs will help increase the total number of correctly received information fields.
Legacy preamble part
WUP preamble
WUP contents
Essential segment, including field like
Frame type, Tx id, Rx id etc.
Segment 2
FCS
FCS
Segment 3
FCS

## Slide 10: Discussions
Are the non-essential fields mandatory or optional?
  To make the structure simple, the performance enhancement fields should also be defined as mandatory fields as long as they are placed in a separate segment and not affecting the reception of essential segment.
Problem of optional fields: burden on signaling
  Use control bits to indicate the existence of each field is a bad idea. For example use 1 bit to control a 2 bit field is no economy.
  The only possible way out will be group the optional fields together in a few segments and signal the existence of the segment.

## Slide 11: SP 1
Do you support to allow fields in SU/group addressed WUP appending to the WUR beacon?
  Detailed fields TBD
  Y:
  N:
  Abs:

## Slide 12: SP2
Do you support to include access category field in TBD type of wake up packets?
  The access category field indicates the highest AC of the queuing data for the target WUR STA
  Y:
  N:
  Abs:

## Slide 13: SP3
Do you support to allow partial TSF field included in non WU beacon wake up packets?
  Partial TSF bits/format TBD
  Y:
  N:
  Abs:

## Slide 14: SP4
Do you support to include per user fields in group addressed WUPs?
  Content in per user fields TBD.
  Y:
  N:
  Abs:

## Slide 15: SP5
Do you support to use multiple FCSs to separately check the segments of a WUP?
  WUP segmentation details TBD
  Y:
  N:
  Abs:

## Slide 16: Reference
[1] 11-17-0036-02-00ba-wur-frame-structure
[2] 11-17-0054-03-00ba-wur-mac-issus
[3] 11-17-0066-00-00ba-wur-packet-design
[4] 11-17-0124-01-00ba-wur-mac-and-wakeup-frame
[5] 11-17-0352-01-00ba-wur-frame-structure-follow-up
[6] 11-17-0679-00-00ba WUR packet format and preamble design
[7] 11-17-0343-03-00ba-wur-beacon