## Slide 1: WUR Action Frame Format
Date: 2018-1-11
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
 | Category | WUR Action | Dialog Token | WUR Mode Element
Octets | 1 | 1 | 1 | TBD
Background (1/2)
WUR Action frame is used to enable WUR negotiation and WUR mode signaling [1].
  WUR Action field:
    WUR Mode Setup
    WUR Mode Teardown
 | Element ID | Length | Element ID Extension | Action Type | WUR Mode Response Status | WUR Parameters
Octets: | 1 | 1 | 1 | 1 | 1 | TBD
  Action Type field:
    Enter WUR Mode Request
    Enter WUR Mode Response
    Enter WUR Mode Suspend Request
    Enter WUR Mode Suspend Response
    Enter WUR Mode Suspend
    Enter WUR Mode
  WUR Mode Response Status field:
    Enter WUR Mode Accept
    Enter WUR Mode Suspend Accept
    Enter WUR Mode Denied

## Slide 3
Background (2/2)
WUR Mode
WUR Mode Suspend
No WUR
One-way Teardown
One-way Teardown
Two-way Setup
One-way or two-way Setup
One-way Setup
Two-way Setup
The WUR action frame containing WUR mode element supports the following state machine for WUR mode operation [1][2]
Note: unlike the state machine in [2], here a STA in WUR Mode Suspend is allowed to transit to WUR Mode via two-way Setup if it intends to negotiate new WUR parameters.

## Slide 4: Problem Statement
The existing WUR Action frame does not support updating WUR parameters (e.g., WID or duty cycle schedule of WURx) for a non-AP STA in WUR Mode.
In order to change WUR parameters, the non-AP STA in WUR Mode needs to enter No WUR via one-way Teardown or enter WUR Mode Suspend via one-way Setup and then re-enter WUR Mode via two-way Setup.
  Such kind of MAC operation is not so efficient.
Negotiate new WUR parameters

## Slide 5
Proposal
The WUR action frame shall support updating WUR parameters for a non-AP STA in WUR Mode via one-way or two-way Update.
  If AP initiates to change WUR parameters (e.g., WID), one-way Update is applied;
  If non-AP STA initiates to negotiate new WUR parameters (e.g., duty cycle schedule of WURx), two-way Update is applied
WUR mode
WUR Mode Suspend
No WUR
One-way Teardown
One-way Teardown
Two-way Setup
One-way or two-way Setup
One-way Setup
Two-way Setup
One-way or two-way Update

## Slide 6
 | Category | WUR Action | Dialog Token | WUR Mode Element
Octets | 1 | 1 | 1 | TBD
Proposed WUR Action Frame
  WUR Action field:
    WUR Mode Setup
    WUR Mode Teardown
    WUR Mode Update
 | Element ID | Length | Element ID Extension | Action Type | WUR Mode Response Status | WUR Parameters
Octets: | 1 | 1 | 1 | 1 | 1 | TBD
  Action Type field:
    Enter WUR Mode Request
    Enter WUR Mode Response
    Enter WUR Mode Suspend Request
    Enter WUR Mode Suspend Response
    Enter WUR Mode Suspend
    Enter WUR Mode
    Update WUR Parameter Request
    Update WUR Parameter Response
    Update WUR Parameter

## Slide 7
Examples
One-way update
Two-way update

## Slide 8: Reference
11-17-0575-08-00ba-spec-framework
11-17-1627-02-00ba-WUR-action-frame-format-follow-up

## Slide 9: SP1
  Do you support to modify R.4.2.B in 11ba SFD as follows?
    R.4.2.B: The frame body of WUR Action frame can include the following:
      WUR Action field that includes the following indications: WUR Mode Setup, WUR Mode Update and WUR Mode Teardown
  Y/N/A:

## Slide 10: SP2
  Do you support to modify R.4.2.C in 11ba SFD as follows?
    R.4.2.C: The WUR Mode element can include the following:
      Action Type field that includes the following indications:
        Enter WUR Mode Request
        Enter WUR Mode Response
        Enter WUR Mode Suspend Request
        Enter WUR Mode Suspend Response
        Enter WUR Mode Suspend
        Enter WUR Mode
        Update WUR Parameter Request
        Update WUR Parameter Response
        Update WUR Parameter
  Y/N/A: