## Slide 1: Efficient WUR Mode Signaling
Date: 2017-05-07
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2: Background
WUR Action frames need to be defined to enable WUR negotiation [1-4], e.g.,
  WUR Mode Request frame
  WUR Mode Response frame
WUR operating parameters can be negotiated using a WUR Mode element included in the WUR Action frame, e.g.,
  WUR Beacon interval
  Duty cycle mode of WURx

## Slide 3: Background (cont.)
WUR mode signaling after DL data transmission is completed
WUR mode signaling after UL data transmission is completed

## Slide 4: Purpose
The purpose of this contribution is to address various methods for improving channel efficiency of WUR mode signaling.

## Slide 5: Improved WUR Mode Signaling in case of No More DL Traffic Buffered
After receiving Data frame(s) that indicates no more buffered traffic for a STA, the STA may send
  Option 1: an Acknowledgement frame aggregated with a WUR Mode Request frame in an A-MPDU.
  Option 2: an Acknowledgement frame with a piggybacked WUR mode request
    In this case, the STA intends not to negotiate new WUR operating parameters.
The AP responds with a WUR Mode Response frame.

## Slide 6: Improved WUR Mode Signaling in case of No More DL Traffic Buffered (cont.)
Piggybacked WUR mode request
No more buffered traffic
Example: Option 2 used by the STA

## Slide 7: Improved WUR Mode Signaling in case of No More UL Traffic Buffered
When no more UL buffered traffic, the STA may send
  Option 1: Data frame(s) aggregated with a WUR Mode Request frame in an A-MPDU; or
  Option 2: Data frame(s) with a piggybacked WUR mode request.
    In this case, the STA intends not to negotiate new WUR operating parameters.
In this case, the AP responds with
  Option 1: an Acknowledgement frame aggregated with a WUR Mode Response frame in an A-MPDU; or
    Option 2: an Acknowledgement frame with a piggybacked WUR mode response.
    In this case, the AP intends not to negotiate new WUR operating parameters.

## Slide 8: Improved WUR Mode Signaling in case of No More UL Traffic Buffered(cont.)
Example: Option 2 used by the STA and Option 2 used by the AP
piggybacked WUR mode request
piggybacked WUR mode response

## Slide 9: Acknowledgement Frame with Piggybacked WUR Mode Signaling (Example 1)
The acknowledgement frame with the piggybacked WUR mode request or response may be a new Control frame similar to Ack frame.
  The new Control frame addressed to STA implies WUR mode response.
  The new Control frame addressed to AP implies WUR mode request.
The Type field indicates “Control” and the Subtype field indicates “Ack + WUR Mode Request/Response”

## Slide 10: Acknowledgement Frame with Piggybacked WUR Mode Signaling (Example 2)
The Acknowledgement frame with the piggybacked WUR mode response may be a modified BlockAck frame.
  A reserved bit in BA Control field is used for WUR mode request/response.
  The BlockAck frame transmitted by the AP implies WUR mode response.
  The BlockAck frame transmitted by the STA implies WUR mode request.

## Slide 11: Data Frame with Piggybacked WUR Mode Signaling (Example)
The Data frame with the piggybacked WUR mode request may be a new QoS Data frame. For example,
  The new QoS Data frame is defined especially for data transmission with WUR mode request.
The Type field indicates “Data” and the Subtype field indicates “QoS Data + WUR Mode Request”

## Slide 12: Summary
We suggested various methods for improving channel efficiency of WUR mode signaling.

## Slide 13: Straw Poll 1
Do you support adding the following to 11ba SFD?
  An acknowledgement frame may be piggybacked with WUR mode signaling.

## Slide 14: Straw Poll 2
Do you support adding the following to 11ba SFD?
  A data frame may be piggybacked with WUR mode signaling.

## Slide 15: Reference
11-17-0575-00-00ba-spec-framework
11-17-0379-00-00ba-sfd-mac-proposal
11-17-0342-04-00ba-wur-negotiation-and-acknowledgement-procedure-follow-up
11-17-0071-00-00ba-high-level-mac-concept-for-wur