## Slide 1: WUR Acknowledgement Indication
Date: 2017-05-05
Authors:
Name | Affiliation | Address | Email
Kaiying Lv | ZTE Corp. | No.9 XiFeng Road, Xi’An, China | lv.kaiying@zte.com.cn
Bo Sun |  |  | Sun.bo1@zte.com.cn

## Slide 2: Introduction
In current spec framework for 11ba[1], the rules are defined as follows:
  The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s).
  After AP sends a unicast wake-up packet to a STA, AP waits for a timeout interval
    If AP receives any transmission from the STA within the timeout interval, then the wake-up packet transmission is successful
    Otherwise, the wake-up packet transmission fails, and AP may retransmit the wake-up packet to the STA
  802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)
From the current rules, we can see that
  A WUR mode STA can acknowledge the reception of a wake-up packet by responding to a trigger from the AP; or
  A WUR mode STA can acknowledge the reception of a wake-up packet by contending the medium using EDCA and transmitting any frame to the AP.
  An AP can continuously or simultaneously wake up multiple WUR mode STAs

## Slide 3: Motivation
The efficiency of wake up procedure needs to be considered
  When only one or just a few WUR STAs is (are) signaled to wake up, less channel contention might happen due to random backoff and different wakeup time
    channel access for acknowledgement using EDCA is supposed be more efficient
  When more WUR STAs are signaled to wake up at the same time, the channel contention might become worse
    triggered-based acknowledgement from WUR STAs would be more efficient
It is more efficient for AP to manage the access control mechanism that WUR STAs use to acknowledge the wakeup signal
  AP knows the medium condition better
  AP should have more control over the medium to utilize the resource better
  It is more power efficient for WUR STAs to acknowledge the wake up packet successfully with less effort with information of contention situation
  High efficient contention if less waked-up STAs
  Less contention collision if triggered by AP when many WUR mode STAs are waked up simultaneously in different wake-up channels and/or slightly different time

## Slide 4: Proposal (1)
An indication is carried in the unicast wake-up packet to indicate whether a trigger will be sent to trigger the acknowledgement
  When AP indicates that a trigger will be sent after the wake-up packet
    The WUR mode STAs signaled by the unicast wake-up packets shall wait within a predefined time interval for being triggered without actively contending the medium.
    If the WUR mode STAs fails to receive the trigger frame after the predefined time interval, then the WUR mode STAs signaled by the unicast wake-up packets could start the channel access using EDCA.
  When AP indicates that no trigger will be sent after the wake-up packet
    The WUR mode STAs signaled by the unicast wake-up packets can start the channel access using EDCA

## Slide 5: Proposal (2)
An ACI indication may be carried in the unicast wake-up packet to indicate the access category
  Indicate whether to use the highest priority AC_VO or the AC that the traffic belongs to. Eg. PS-Poll using AC_VO or AC_BE

## Slide 6: Conclusion
The ways of acknowledgement for unicast Wake-up packet are discussed.
We suggest that AP indicate the way of acknowledgement for unicast Wake-up packet in order to have better utilization of the resource.

## Slide 7: Straw Poll 1
Do you support that an indication shall be carried in the unicast wake-up packet to indicate whether a trigger will be sent to trigger the acknowledgement?
Y
N
A

## Slide 8: Straw Poll 2
Do you support that an indication may be carried in the unicast wake-up packet to indicate the ACI of the acknowledgement/transmission?
Y
N
A

## Slide 9: Straw Poll 2
Do you support that an indication may be carried in the unicast wake-up packet to indicate the ACI of the acknowledgement/transmission?
Y
N
A

## Slide 10: References
11-17/0575r0 “spec framework”, Po-kai Huang