## Slide 1: Comment Resolution on EDMG A-PPDU Structure
Date: 2017-05-07
Authors:

## Slide 2: Abstract
This submission proposes resolution on CID 9.
CID | Page | Line | Comment | Proposed Change
9 | 100 | 16 | A-PPDU structures are missing detailed specification that can result in potential ambiguity in interpreting the standard | Add A-PPDU structure details including the GIs, headers, etc like is provides for the single PPDU case in section 30.5.6.2.2

## Slide 3: Introduction
EDMG SC A-PPDU has been approved in 11ay [1].
In the EDMG SC A-PPDU, the PPDU structure differ depending on the index number of the jth PPDU, the channel bonding factor NCB and SISO/MIMO [2].
11ay supports different types of GI (Short/Normal/Long) [1].
  The EDMG-Header-A shall be prepended by the normal GI.
  The data symbol blocks can be prepended by the short/normal/long GI.
In this contribution, we propose PPDU structures for the EDMG SC A-PPDU with different types of GI.

## Slide 4: Problem #1
Since only normal GI is specified in 11ad [3], the L-Header within the Nth PPDU within the DMG A-PPDU and the final data symbol block within the (N-1)th PPDU within the DNG A-PPDU can share the GI.
On the other hand, 11ay supports short/normal/long GI.
  The EDMG-Header-A shall be prepended by the normal GI
  The data symbol blocks can be prepended by the short/normal/long GI
  When using short/long GI, the L-Header within the Nth PPDU and the final data symbol block within the (N-1)th PPDU can not share the GI because of no cyclicity as shown below.

## Slide 5: Proposal
Not only the final symbol block within the last PPDU within the EDMG SC A-PPDU but also the final symbol block of the all PPDUs within the EDMG SC A-PPDU shall be followed by the same GI regardless on the value of the Additional EDMG PPDU field within the corresponding EDMG-Header-A.

## Slide 6: Problem #2
The PPDU structure for the jth PPDU (1 ≤ j ≤ N) within the EDMG SC A-PPDU is different from any other type of SU PPDU structures specified in [1].
  The non-EDMG portion, the EDMG-STF and the EDMG-CEF shall not be transmitted in the jth PPDU (1 ≤ j ≤ N).
We need to specify new PPDU structure for the jth PPDU (1 ≤ j ≤ N) within the EDMG SC A-PPDU.

## Slide 7: Proposal
For j = 0:
  The 1st PPDU structure shall be the same as the SU PPDU structures specified in [1].
For 1 ≤ j ≤ N:
  The jth PPDU structure is similar to the structure of the EDMG-Header-B field and the Data field in the MU PPDU structures specified in [1].
    The EDMG-Header-A and the 1st data block are prepended by GIei64*NCB when the short GI or normal GI is used.
    The EDMG-Header-A is prepended by GIei128*NCB[1:64*NCB] and the 1st data block is prepended by GIei128*NCB when the long GI is used.
Short GI
Normal GI
Long GI

## Slide 8: Conclusion
We propose PPDU structure for the EDMG A-PPDU.
  The final block of all PPDUs within the EDMG SC A-PPDU shall be followed by the same GI as data field.
  The similar PPDU structure to the MU PPDU structure is applied to the jth PPDU (1 ≤ j ≤ N) within the EDMG SC A-PPDU.

## Slide 9: References
[1] Draft P802.11ay_D0.3
[2] 11-17-0051-03-00ay
[3] 802.11-2016