## Slide 1: Scalable Location
Date: 2017-05-11
Authors:

## Slide 2: Abstract
This presentation argues for a change to the TGaz functional requirements such as to require the development of a mode that enables concurrent location of an unlimited number of client stations.

## Slide 3: Motivation
In [1] we have seen a method presented that allows for an unlimited number of client stations to concurrently estimate their position.
This is achieved by employing broadcast transactions between anchoring stations (e.g. access points), that the client stations listen to and use for the calculation of their position.
Thus, it is possible to develop a localization protocol that enables true scalable WiFi localization.
We here argue that we therefore should make the development of such a mode part of the TGaz FRD.

## Slide 4
Proposed FRD Change

## Slide 5: Straw Poll
Do you support adding the following text to the 802.11az Functional Requirements document at the end of the ‘Scalability’ section?
“The scalable mode of the 802.11az range measurement protocol shall also support at least one mode which, in addition to the requirements listed above in this section, allows for scalable positioning meeting the following scalability mode requirements:
TGaz R28 Supports enabling an unlimited number of client STAs to concurrently compute their location for the case when the location process is terminated at the client.”
  Y: N: A:

## Slide 6: Alternative Straw Poll
Do you support modifying the 802.11az Functional Requirements document as follows?
Change:
“TGaz R19 Support locating and tracking all associated and at least 200 unassociated STAs per AP concurrently. [Ref-10]”
To:
“TGaz R19 Support enabling an unlimited number of STAs to concurrently compute their location. [Ref-12]”
And point [Ref-12] to the used TGaz document.
  Y: N: A:

## Slide 7: References
[1] “Passive Location”, Erik Lindskog, Naveen Kakani and Ali Raissinia, IEEE 802.11-17/0417r0.