## Slide 1: Discussion on FTM Protection – follow up
Date: 2017-05-09
Authors:

## Slide 2: Abstract
This submission is a follow-up from previous telecon on security aspects for “Type B” adversary

## Slide 3: Mechanism for successful rage estimation attack
VHT-LTF usage: Decoding vs. ToA
  Decoding uses the dominant path where most of the energy is concentrated to maximize likelihood of successful decoding.
  The 1st tap is used to identify the first path rather then dominant path.
Affecting ToA estimation only
  By transmitting a spoofed time advanced VHT-LTF with minimal power the ToA estimation is greatly affected with minimal impact on decoding probability.
Source: https://www.researchgate.net/publication/273443111

## Slide 4: Q: Is this attack simple to generate? A: Yes, hacker can configure NIC to transmit NDP frame in response to FTM frame at low power.
ISTA Transmission
Dozens of Nano-second shifting F.E shifting 67ns10m shift
Adversary NDP
L
-
STF
L
-
LTF
L
-
SIG
VHT
-
SIG
-
A
VHT
-
STF
VHT
-
LTF
VHT
-
SIG
-
B
Data
VHT
-
LTF
VHT – SIG - B
VHT - STF
L-STF
L-LTF
L-SIG
VHT-SIG-A
ToF Measurement
RSTA
Type B Adversary
ISTA actual position
Spoofed ISA Range
Allowed Area

## Slide 5: Q: What about timing? A: It is a bad practice to rely on PHY properties as a protection mechanism. The adversary may move around freely between the RSTA and the ISTA until the desired attack timing is obtained and the attack is successful.
ToF Measurement
RSTA
Adversary moves around
ISTA actual position
Spoofed ISA Range
Allowed Area

## Slide 6: Q: Wouldn’t it create ACK decode error on RSTA side? A: No, the spoofed signal is perceived as multipath somewhat hindering the SINR while still allow for correct decoding while giving a wrong sense of distance.

## Slide 7: Summary
REVmc FTM uses ACK frames for measurements purposes only.
The ACK doesn’t contain any information unknown to the attacker.
This submission demonstrates a measurement attack over the ACK, with no specialized HW and no impact on successful ACK decoding.
Thus, it is not useful to protect the ACK at the MAC level from these types of attack.

## Slide 8: Straw poll 1
Do you agree that for REVmc, HEz, and VHTz FTM modes the fields over which range measurements is performed shall be protected for spoofing prevention against a Type B adversary?
  Yes:
  No:
  Abstain: