## Slide 1: Resource Allocation for Unassociated STAs
Date: 2017-06-03
Authors:
Chittabrata Ghosh

## Slide 2: Abstract
In this presentation, we propose to provide the MU mechanism on resource allocation for unassociated STAs adopted in 802.11ax
Chittabrata Ghosh
May 2017
        doc.: IEEE 802.11-17/0802r1

## Slide 3: Introduction
UL OFDMA-based random access may be used for MU negotiation procedure
  MU transmission of FTM Request frames can allow multiple unassociated STAs to accomplish the negotiation procedure simultaneously
  UL OFDMA random access can also help unassociated STA at the edge of BSS to access the network quickly due to narrow band transmission
It has been agreed (SFD) that the ID for ranging operation for an unassociated STA used for measurement phase will be in the FTM Response frame
Trigger frame for
random access
DL M-BA
Contention-based UL OFDMA
FTM Request from STA1
ACK/BA to STA1
FTM response (SU format)
FTM Request from STA2
Chittabrata Ghosh

## Slide 4: M-BA frame format
The agreed M-BA structure is
A value of 15 in the TID subfield in the Per STA Info field of the M-BA frame indicate the successful acknowledgement of a management frame that requires an immediate response and is carried in the soliciting A-MPDU
Under the condition of the unassociated STA without AID, how does AP send the acknowledgement to its association request?
  According to the agreed motion, the TID value shall be set to “1111”
B0-B10= AID
B11=ACK/BA
Chittabrata Ghosh

## Slide 5: Acknowledgement to association exchange
Set AID subfield to an unique AID value, e.g., 2045, in the M-BA frame
  Provide an unique identifier for any unassociated STAs that has used an RU for random access
  RA field is added after the “Per TID info” field
  MAC address field is used to distinguish which STA’s request management frame is successfully delivered through OFDMA random access
  Both Ack type and SSC field are set to 0, keeping consistence with the parsing scheme of the implemented ax device
  Indicate that the total length of subfields following Per TID STA info subfields is 10 bytes
B0-B10= 2045
B11= BA
SSC (2 bytes )
TID=“1111”
RA (6 bytes)
Reserved (2 bytes )
Chittabrata Ghosh

## Slide 6: Per STA Info Subfield Parsing with Proposed M-BA
An associated STA that had transmitted either on a scheduled RU or an RU for random access will determine the length of the Per STA Info subfield based on the ACK Type subfield
  AID 2045 indicates that the Per STA Info subfield is for an unassociated STA
  ACK Type subfield and SSC fields are set to 0 for AID 2045, indicating the presence of the Per STA Info subfield only for an unassociated STA, and has 10 bytes
An unassociated STA that had transmitted on a random access RU will ONLY parse the remaining 10 octets following the Per TID Info subfield when B0-B10 is an AID 2045
  The STA parses Per STA Info subfield to decode the RA field
  If the RA field matches the MAC address of the unassociated STA, it interprets that the HE Trigger-based PPDU transmitted on an RU assigned for random access was received by the AP successfully.
When unassociated STAs use RUs (AID 2045) for OFDMA-based random access, the AP shall send an M-BA frame as the ACK frame solicited by the HE Trigger-based PPDUs
Finally, as agreed, the ID for unassociated STAs are signaled in successive unicast FTM Response frames
Chittabrata Ghosh

## Slide 7: Straw Poll
Do you support the resource allocation for initial FTM Request in MU negotiation for unassociated STAs to be based on OFDMA random access as depicted in Slide 3?
Y: 10 N:0 A: 6
Chittabrata Ghosh
May 2017
        doc.: IEEE 802.11-17/0802r1

## Slide 8: Motion
Move to adopt the following text to the SFD and instruct the SFD editor to include it in TGaz SFD under Subsection 3.2 and grant editorial license to SFD Editor
  The resource allocation for initial FTM Request in MU negotiation for unassociated STAs to be based on OFDMA random access as depicted in Slide 3?
Moved by: Ganesh Venkatesan
Seconded: Chittabrata Ghosh
Y:12 N:0 A: 4
Motion passes
Chittabrata Ghosh
May 2017
        doc.: IEEE 802.11-17/0802r1