## Slide 1: Supporting presentation for IEEE 802.11 WG Liaison Statement to ETSI BRAN relating to next revision of EN 301 893
15 June 2017
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: 802.11 WG LS to ETSI BRAN supports the continuing support for PD/ED sharing mechanism
  On 6 June 2017, the Chair of IEEE 802.11 WG forwarded a Liaison Statement (LS) from IEEE 802.11 WG to the Chair of ETSI BRAN
  The LS articulates IEEE 802.11 WG’s recommendations to ETSI BRAN related to the next revision of EN 301 893
    Recommendation: EN 301 893 should continue supporting the use of the “dual threshold option”
    The “dual threshold option” is the sharing mechanism using both Preamble Detection and Energy Detection currently used by IEEE 802.11a/n/ac
    It is suggested that any technology be allowed to use the option, not just IEEE 802.11 based technologies

## Slide 3: This presentation is designed to assist discussion by ETSI BRAN of 802.11 WG’s LS
  This document displays the LS in ppt form
    In left column of each page
  The LS text is accompanied by explanatory commentary by the author of this presentation
    In left column of each page
  The commentary was not approved by the IEEE 802.11 WG and represents the views of the author only (Andrew Myles, Cisco)
  The presentation is designed to facilitate discussion of the LS at the ETSI BRAN meeting in July 2017
  The presentation concludes by asserting ETSI BRAN should agree to work with 802.11 WG on potentially including PD/ED in a revised adaptivity clause

## Slide 4: The LS explains that any views contained within it are from a 802.11 WG perspective only
LS text
  This is an approved liaison statement from IEEE 802.11
  It does not necessarily reflect a position of the IEEE, the IEEE Standards Association or IEEE 802
Commentary
  The LS was developed in the 802.11 PDED ad hoc ( which has now become the IEEE 802.11 Coexistence SC)
  It was approved by the 802.11 WG on 10 May 2017 at its final plenary in Korea
    With no negative votes!
  It was not considered for approval by any other IEEE entity and represents the view of the 802.11 WG only

## Slide 5: The LS notes the 802.11 WG is particulatly interested in adaptivity clause of EN 301 893
LS text
  The IEEE 802.11 Working Group has been monitoring the work in ETSI BRAN to develop version 2.1.0 of Harmonized Standard (HS) EN 301 893
  The revised adaptivity clause in EN 301 893 is of interest to the IEEE 802.11 Working Group (WG) because it is one aspect of sharing of the 5 GHz unlicensed band in Europe, particularly as new non-802.11 technologies might be introduced into the band.
Commentary
  802.11 WG is interested in and is following the work of ETSI BRAN to develop the revised adaptivity clause in EN 301 893

## Slide 6: The LS states 802.11 WG is pleased the PD/ED mechanism is allowed for adaptivity for 802.11a/n/ac
LS text
  The IEEE 802.11 Working Group is pleased to note that EN 301 893 v2.1.0 continues the tradition of previous versions of the standard by explicitly allowing the use of IEEE 802.11 conformant equipment at the same energy detection threshold that has was defined in 1999, in combination with IEEE 802.11’s own preamble detection mechanism (which we will refer to as the “dual threshold option”).
Commentary
  802.11 WG is pleased with the decision by ETSI BRAN to continue allow 802.11a/n/ac systems to used the traditional PD/ED based sharing mechanism, at least for the time being

## Slide 7: The LS implies that ED-only is a lesser adaptivity mechanism by being more conservative
LS text
  In contrast, EN 301 893 v2.1.0 requires non-IEEE 802.11 conformant equipment to use a more conservative energy detection-only mechanism and threshold.
Commentary
  802.11 WG notes that other equipment is required to use the more conservative ED-only mechanism
  One implication is that other equipment is missing out on the benefits of the PD/ED based sharing mechanism
  This is made clearer later in the LS when it is suggested the PD/ED based sharing mechanism be made available for use by all technologies

## Slide 8: The LS notes the PD/ED mechanism was actually jointly developed by 802.11 WG and ETSI BRAN
LS text
  The inclusion of the dual threshold option in EN 301 893 recognizes ETSI BRAN’s history of developing HiperLAN/2 Physical Layer (PHY) design in close collaboration with the IEEE 802.11 WG. The jointly developed preamble and energy detection mechanisms for the HiperLAN/2 and IEEE 802.11 standards had been established when the 5 GHz band had a technology dependent assignment in Europe.
Commentary
  802.11 WG notes that the PD/ED mechanisms actually have a history going back to previous collaborations between the 802.11 WG and ETSI BRAN
  The developers of HiperLAN/2 recognised the importance of PD by their efforts to agree on a joint PD/ED mechanism with 802.11 WG

## Slide 9: The LS notes that the Wi-Fi market in Europe is continuing undisrupted in the short term
LS text
  A continued inclusion of the dual threshold option permits the industry to put existing IEEE 802.11 designs unmodified to the European market.
Commentary
  802.11 WG highlights the role played by continued inclusion of the dual threshold option in enabling the continuation of the status quo wrt 802.11 in the market
  This is a good thing because it allows Wi-Fi to continue to be a driver of great socio-economic outcomes

## Slide 10: The LS notes that EN 301 893 does not allow the use of the PD/ED mechanism by 802.11ax
LS text
  The dual threshold option in EN 301 893 v2.1.0 has been drafted in a way that it applies to existing IEEE 802.11a, 802.11n, and 802.11ac based equipment.
  However, it does not yet apply to IEEE 802.11ax equipment, which will be the basis of the next generation of 802.11.
  This is reasonable because IEEE 802.11ax was not even at draft stage when EN 301 893 v2.1.0 was being developed.
Commentary
  802.11 WG observes that the current version of EN 301 893 allows the use of PD/ED mechanism by existing versions of 802.11 but not the future version, 802.11ax
  802.11 WG notes this was a reasonable decision by ETSI BRAN given 802.11ax was nor defined at the time

## Slide 11: The LS notes the 802.11 WG has an interest in revisions to the adaptivity clause in EN 301 893
LS text
  The IEEE 802.11 WG understands that ETSI BRAN is planning to start a new effort in about July 2017 to revise EN 301 893 yet again
  We highlight two of the items that might be addressed in the revision process:
    Consider a single ED threshold limit value applicable to all technologies
    Consider a general review of the adaptivity section (including ED threshold) in light of new technologies
Commentary
  802.11 WG notes that ETSI BRAN is considering a revision of EN 301 893
  It also highlights revisions to the adaptivity clause to be of particular interest

## Slide 12: The LS asserts that the PD/ED mechanism is the best way to ensure fair and efficient use of 5GHz
LS text
  It is the view of the IEEE 802.11 Working Group that the best way to ensure fair and efficient use of the 5 GHz band is for all technologies to embrace the robust and proven, dual threshold mechanism used by the IEEE 802.11 standard.
Commentary
  802.11 WG is clear that it believes the PD/ED mechanism is the best way to ensure fair and efficient use of the 5 GHz band
  This is consistent with multiple recent LS’s from IEEE 802 to 3GPP RAN1

## Slide 13: The LS notes that 802.11 WG accepts that an ED-only mechanism should be included as an option
LS text
  The IEEE 802.11 WG recognises that the introduction of an energy detection-only mechanism (such as defined in EN 301 893), as a sharing mechanism, does have the important benefit of technology neutrality
  Therefore, the IEEE 802.11 Working Group supports the ongoing inclusion of an energy detection-only mechanism in EN 301 893
Commentary
  802.11 WG also accepts the allowance of a ED-only enhances technology neutrality in EN 301 893 by allowing vendors a choice of multiple mechanisms
  It is worth noting that previous versions of EN 301 893 also enhanced technology neutrality by allowing multiple methods
  That said, 802.11 WG believes, based on LS’s to 3GPP, that the use of an ED–only mechanism is sub-optimal

## Slide 14: The LS advocates for both PD/ED and EN-only based on fair sharing
LS text
  Allowing the use of both the energy detection-only mechanism and the dual threshold option in EN 301 893:
    Continues fair sharing of the 5 GHz unlicensed band for equipment using either the energy detection-only mechanism or the dual threshold option. Simulations in ETSI BRAN, 3GPP RAN1 and IEEE 802.11 Working Group have shown fair sharing occurs in most use cases when these mechanisms are used together with appropriate thresholds
  .
Commentary
  802.11 WG notes that fair sharing can occur (mostly) if equipment use both PD/ED (eg 802.11) and ED-only (eg LAA) mechanisms
  Other simulations have highlighted that fair sharing does not occur when 802.11ax is forced to use the same ED threshold as used by the LAA defined ED-only mechanism
    802.11ax will have less performance that both 802.11ac and LAA in this situation

## Slide 15: The LS advocates for both PD/ED and EN-only based on technology neutrality
LS text
    Promotes technology neutrality by allowing a wider diversity of sharing mechanisms to be employed at the choice of implementers, ie both the energy detection-only and dual threshold options
Commentary
  802.11 WG notes that allowing multiple options enhances “technology neutrality”, which is a requirement for HS’s
  The definition of “technology neutrality”, which is vital to this discussion, will be discussed in another presentation

## Slide 16: The LS advocates for both PD/ED and EN-only based avoiding a backward technology step
LS text
    Avoids a backward technology step, which would occur if the dual threshold option was restricted in favour of an energy detection-only mechanism
Commentary
  The PD/ED mechanism is more sophisticated than the ED-only mechanism because it takes into account information beyond just energy
  Requiring the use of a less sophisticated mechanism is contrary to the rules for Harmonised Standards, which require technology to improve over time
  Arguably even allowing ED-only is a backward step

## Slide 17: The LS advocates for both PD/ED and EN-only based on minimising the socio-economic risk
LS text
    Minimises the socio-economic risk of deprecating the well-established and proven sharing dual threshold option used by IEEE 802.11 today.
Commentary
  Wi-Fi has proven over many years that the PD/ED mechanism works
  It has also enabled significant socio-economic benefits
  Replacing the PD/ED mechanism now for a less sophisticated technology (a backward step) risks all those benefits
  It is not worth it and is not needed for any known reason!

## Slide 18: The LS advocates for both PD/ED and EN-only based on minimising the socio-economic risk
LS text
    Minimises the socio-economic risk of deprecating the well-established and proven sharing dual threshold option used by IEEE 802.11 today.
Commentary
  Wi-Fi has proven over many years that the PD/ED mechanism works
  It has also enabled significant socio-economic benefits
  Replacing the PD/ED mechanism now for a less sophisticated technology (a backward step) risks all those benefits
  It is not worth it and is not needed for any known reason!

## Slide 19: The LS states 802.11 wants to work with ETSI BRAN
LS text
  The IEEE 802.11 WG will make use of its existing liaison with ETSI BRAN to monitor ETSI BRAN’s plans to revise EN 301 893
  The IEEE 802.11 Working Group would be delighted to assist ETSI BRAN in relation to these topics.
Commentary
  802.11 WG wants to work with ETSI BRAN on these issues

## Slide 20: 802.11 WG wants to work with ETSI BRAN to include PD/ED in a revised adaptivity clause
What 802.11 WG wants/believes
  The PD/ED mechanism is better than PD-only to share 5GHz
  It is acceptable for both mechanisms to be allowed by EN 301 893, albeit not ideal
  802.11ax (or indeed any technology) should be able to continue using the PD/ED mechanism after the EN 301 893 revision
  802.11 WG wants to work with ETSI BRAN to include the PD/ED mechanism in the revised adaptivity clause in EN 301 893

## Slide 21: ETSI BRAN should agree to work with 802.11 WG on potentially including PD/ED in a revised adaptivity clause
  There is no reason for ETSI BRAN exclude an interested stakeholder
  Of course, it can’t guarantee the 802.11 WG’s desired outcome at this time
  On the other hand it should not reject it either because 802.11 WG is an important and significant stakeholder
  The most appropriate action is to ensure the EN 301 893 revision WI allows for the possibility that the PD/ED mechanism continues to be allowed … for all technologies, including 802.11ax