## Slide 1: CID 337 Super Operating Classes
Date: 2017-06-29
Authors:
Notes: July 2007

## Slide 2: Abstract
Goal is to reduce the length of (re)Association Request/Response and Probe Request/Response
Super Operating Classes replace some lists of supported Operating Classes, and removes requirement that Supported Channels be present in (re)Association Request/Response when all channels in the major band are supported – 9.4.2.54 Supported Operating Classes - The Operating Classes field lists, in descending order or preference, all single-octet operating classes that the STA is capable of operating with in this country.

## Slide 3: Standard Global Operating Classes, each with a short list of supported channels
5 GHz 20 MHz – 115, 118, 121, 124 and 125
5 GHz 40 MHz – 116, 117, 119, 120, 122, 123, 126 and 127
5 GHz 80 MHz – 128
5 GHz 160 MHz – 129
5 GHz 80+ MHz – 128 and 130

## Slide 4: Current standard

## Slide 5: Proposed Super OC practice with no Supported Channels IE 9.4.2.18 in (re)Association Request/Response
For 20 MHz support,
  Super 20 OC
  Legacy 20 OC
For 40 MHz support
  Super 40 OC
  Legacy 40 OC of primary channel
  Legacy 20 OC of primary channel
For 80 MHz support
  Super 80 OC
  Legacy 80 OC of primary channel
  Legacy 40 OC of primary channel
  Legacy 20 OC of primary channel