## Slide 1: CID 337 Cumulative Operating Classes
Date: 2017-07-12
Authors:
R1: renamed to Cumulative Operating Classes.
Added possibility of multiple cumulative classes for a maximum bandwidth
Notes: July 2007

## Slide 2: Abstract
Goal is to reduce the length of (re)Association Request/Response and Probe Request/Response
Cumulative Operating Classes replace some lists of supported Operating Classes, and removes requirement that Supported Channels be present in (Re)Association Request/Response when most/all channels in the major band are supported – 9.4.2.54 Supported Operating Classes - The Operating Classes field lists, in descending order or preference, all single-octet operating classes that the STA is capable of operating with in this country.

## Slide 3: Standard Global Operating Classes, each with a short list of supported channels
5 GHz 20 MHz – 115, 118, 121, 124 and 125
5 GHz 40 MHz – 116, 117, 119, 120, 122, 123, 126 and 127
5 GHz 80 MHz – 128
5 GHz 160 MHz – 129
5 GHz 80+ MHz – 128 and 130

## Slide 4: Current standard

## Slide 5: Proposed Cumulative OC practice with no Supported Channels IE 9.4.2.18 in (Re)Association Request/Response
For 20 MHz support,
  Cumulative 20 OC All ch; or Cumulative 20 OC not All ch …
  Legacy 20 OC
For 40 MHz support
  Cumulative 40 OC All ch; or Cumulative 40 OC not All ch …
  Legacy 40 OC of primary channel
  Legacy 20 OC of primary channel
For 80 MHz support
  Cumulative 80 OC All ch; or Cumulative 80 OC not All ch…
  Legacy 80 OC of primary channel
  Legacy 40 OC of primary channel
  Legacy 20 OC of primary channel