## Slide 1: WUR Mode Discussion
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
There are several terms related with “WUR mode” in current SFD
  However, that terms are used without any definition or description
We may need a common ground of these terms

## Slide 3: SFD text
R.4.3.A: STA can have Duty cycle mode for wake-up receiver
R.4.4.B: WUR Beacon interval can be indicated in WUR Mode element
R.4.4.C: Define a synchronization mechanism to solve the timing mismatch problems associated with WUR duty cycle mode
R.4.5.A: WUR mode signaling shall be defined for the WUR STA to enter the WUR mode
R.4.6.4.A: IEEE 802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs

## Slide 4: Terms about WUR mode
Following terms are related with “WUR mode” in SFD
  WUR mode
  WUR mode STA
  WUR Duty cycle mode
  WUR mode element

## Slide 5: WUR mode
If a STA enters into WUR mode,
  primary connectivity radio (PCR) will be turned off to save power consumption
    Transmitting/receiving a frame on PCR is not available
  wake-up radio (WUR) will be turned on to receive wake-up packet
    Transmitting a frame on WUR is not available
Wake-up radio can be turned off periodically to save more power
  This operation may be called WUR duty cycle mode

## Slide 6: Active mode
If a STA enters into Active mode,
  primary connectivity radio (PCR) will be turned on to maintain data communication
  wake-up radio (WUR) will be turned off
If existing power saving features are applied, PCR can be turned off temporary
  This operation may be called PS mode

## Slide 7: WUR Duty cycle mode
As mentioned in WUR mode, WUR duty cycle mode may be a sub-mode of WUR mode
Also an WUR STA can operate in WUR non duty cycle mode
  If a STA operates in WUR non duty cycle mode, Wake-up radio is always on
  We suggest that we call it “WUR normal mode” or “WUR AO mode”
    If we use “WUR AO mode”, WUR duty cycle mode can be abbreviated to “WUR DC mode”

## Slide 8: Default mode
Which mode is default mode of WUR mode?
  Option 1: WUR normal mode is default mode
    Only STAs that want to reduce more power consumption operate in duty cycle mode
    WUR beacon may be optional
  Option 2: WUR duty cycle mode is default mode
    All WUR STAs have a capability of duty cycle operation
    WUR beacon may be mandatory
    If a STA want to operate in WUR normal mode, its ON duration will be set to infinity or its OFF duration will be set to 0

## Slide 9: Cooperation with existing power save
WUR operation can be coupled with existing power saving features [1][2][3]
  A STA can enter to WUR mode instead of PS mode
  We may need an additional term describing the WUR mode
    Option 1: WUR normal mode (reuse)
    Option 2: WUR PS mode (new mode)
    Option 3: PS mode (don’t define in WUR)

## Slide 10: WUR Mode element
WUR Mode element is an information set for WUR operation
  WUR Mode element can be delivered during WUR negotiation and WUR mode signaling
WUR Mode information element
  General information: WUR channel, Mode indication, Transmission rate of wake-up packet, Retransmission timeout, Keep alive timeout
  Information for duty cycle mode: WUR Beacon interval, Time unit, WUR TBTT, Starting point, On/Off duration

## Slide 11: Summary
We addressed description and definition on WUR mode
  WUR mode
  WUR normal mode
  WUR duty cycle mode

## Slide 12: Straw poll 1
Do you agree to add following definition to SFD?
  WUR mode : A power management mode in which a STA is operating in WUR normal mode or WUR duty cycle mode

## Slide 13: Straw poll 2
Do you agree to add following definition to SFD?
  WUR normal mode: A power management mode in which a STA remains in doze state on the primary connectivity radio while the STA remains in awake state on the wake-up radio to receive a wake-up radio frame

## Slide 14: Straw poll 3
Do you agree to add following definition to SFD?
  WUR duty cycle mode: A power management mode in which a STA remains in doze state on the primary connectivity radio while the STA alternates between awake and doze states on the wake-up radio, and the STA in the awake state on the wake-up radio is expected to receive a wake-up radio frame

## Slide 15: References
[1] 11-17-0653-00-00ba-examples-of-integrating-wur-with-existing-power-save-protocol
[2] 11-17-0716-03-00ba-wur-with-conventional-802-11-power-save
[3] 11-17-0936-00-00ba-integration-of-wur-to-power-save-mode