## Slide 1: Signal Bandwidth and Sequence for OOK Signal Generation
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
We already agreed that the OOK waveform of wake-up packet is generated by populating some subcarriers
Also, the signal bandwidth of 4MHz was recommended to generate the OOK signal in [1]
  i.e., 13 subcarriers with the subcarrier spacing of 312.5KHz
In this contribution, by focusing on the 4MHz bandwidth, we introduce several sequences which are applied to 13 subcarriers
  Some of them were proposed in [2][3][4]
  We additionally propose a sequence which optimizes PAPR and compare it with the above sequences

## Slide 3: Signal Bandwidth
In the last f2f meeting in May, there was a lot of discussion on the OOK waveform generation
  Some members were concerned about having too many optional features in 11ba
  While other members did not want to exclude any possibilities such as multi-band transmission, concurrent transmission with 11ax frames using 11ax tone plan, etc.
In this contribution, we only focus on the following cases to propose signal bandwidth and sequence for OOK signal generation
  The conventional Wi-Fi transmitter is used, i.e., the subcarrier spacing is 312.5KHz
  Single band is used for wake-up packet transmission
In this case, we suggest using 4MHz signal bandwidth (i.e., 13 subcarriers) as a mandatory feature

## Slide 4: Sequences
As to the sequence, we propose that the length is 13 and the coefficient at the center tone is zero to prevent the DC offset
Option 1 : Optimized sequence in terms of the PAPR
  [1,1,1,-1,-1,-1,0,-1,1,-1,-1,1,-1]
Option 2 : Reuse the conventional L-STF sequence by choosing coefficients at tones of all multiples of 4 from -24 to 24 [2]
  [1,-1,1,-1,-1,1,0,-1,-1,1,1,1,1] * (1+j)/sqrt(2)
Option 3 : Reuse the conventional L-LTF sequence by choosing coefficients at tones from -6 to 6 [3]
  [1,-1,1,1,1,1,0,1,-1,-1,1,1,-1]
Option 4 : Optimized sequence in terms of the average power between CP and signal portions (similar average power between them) [4]
  [-1,-1,-1,1,1,-1,0,-1,-1,-1,1,-1,1]

## Slide 5: Comparison
PAPR and average CP power to average signal power ratio (ACASR) are examined
  PAPR is calculated by applying 4 times IFFT
    CP portion is not considered
  ACASR is calculated by comparing a CP portion of 0.8us (16 samples) and a signal part of 3.2us (64 samples)
    Note that the ACASR was utilized in [4] to obtain the sequence which minimizes it
 | Option 1 | Option 2 | Option 3 | Option 4
PAPR [dB] | 2.0589 | 2.2394 | 4.1516 | 4.0073
ACASR [dB] | -0.0455 | 0.0450 | -0.5964 | -0.0423
0.8us CP
(16 samples)
3.2us signal
(64 samples)
In back-up slides, PAPR and average power for 0.5/1/2us ON-signals which are selected from the 3.2us or 4us signal in each option are shown

## Slide 6: Discussion
In terms of the PAPR, option 1 is the best and option 2 is comparable
  Trend is similar even when we calculate the PAPR considering the CP part as shown in back-up slides
  Note that option 1 has a better PAPR than that of the conventional Wi-Fi
  Given the PAPR of the data part for the conventional Wi-Fi as shown in Appendix A, Option 3 and 4 may be also acceptable
In terms of the ACASR, option 4 is the best and option 1 and 2 are comparable
  If the average CP power is not similar to that of the signal part (i.e., the average CP power is significantly low or high compared to that of the signal part), it may cause performance degradation due to SNR decrease, ISI impact, etc.
  However, the performance gap among these four options is not huge as shown in Appendix B

## Slide 7: Conclusion
We suggested using 4MHz signal bandwidth (i.e., 13 subcarriers) as a mandatory feature when the subcarrier spacing is 312.5KHz and a single band is used for wake-up packet transmission
We also dealt with four sequences with the length of 13 for the OOK signal generation
In each sequence, the PAPR and the ACASR were investigated
From the PAPR viewpoint, it may be advisable to use option 1 or 2
From the ACASR viewpoint, it may be advisable to use option 1, 2 or 4

## Slide 8: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  When the subcarrier spacing is 312.5KHz and a single band is used for transmission of wake-up packet, the OOK waveform of wake-up packet is generated by using contiguous 13 subcarriers
    The center subcarrier should be null
Y/N/A : 19/0/36
Notes: 0

## Slide 9: Straw Poll #2
Which option do you prefer for the sequence that is applied to 13 subcarriers to generate 4us OOK ON-signal when the subcarrier spacing is 312.5KHz and a single band is used for transmission of wake-up packet?
  Option 1 : [1,1,1,-1,-1,-1,0,-1,1,-1,-1,1,-1]
  Option 2 : [1,-1,1,-1,-1,1,0,-1,-1,1,1,1,1] * (1+j)/sqrt(2)
  Option 3 : [1,-1,1,1,1,1,0,1,-1,-1,1,1,-1]
  Option 4 : [-1,-1,-1,1,1,-1,0,-1,-1,-1,1,-1,1]
  Option 5 : none of the above
Op1/Op2/Op3/Op4/Op5/A : 8/10/2/1/17/3

## Slide 10: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  When the subcarrier spacing is 312.5KHz and a single band is used for transmission of wake-up packet, a same sequence is used to generate OOK ON-signals for all of the data rates
Y/N/A :

## Slide 11: Motion
Move to add the following to the 11ba SFD
  When a single band is used for transmission of wake-up packet, the OOK waveform of wake-up packet is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5KHz
    The center subcarrier is TBD
Move : Eunsung Park
Second : Shahrnaz Azizi
Y/N/A : 31/2/9

## Slide 12: References
[1] IEEE 802.11-17/0655r4 OOK Signal Bandwidth for WUR
[2] IEEE 802.11-17/0656r0 WUR PHY Performance Study with Phase Noise and ACI
[4] IEEE 802.11-17/373r1 Performance Investigations on Single-carrier and Multiple-carrier-based WUR
[4] IEEE 802.11-17/0676r1 WUR Link Budget Analysis Follow-up : Data Rates and SIG Bits Protection

## Slide 13: Appendix

## Slide 14: Appendix A
PAPR of the data part for 802.11ac in 20MHz

## Slide 15: Appendix B
125Kbps data rate with Manchester coding
PER for the payload of 48 bits
CFO and phase noise applied
TGnD Channel
UMi NLoS Channel

## Slide 16: Back Up

## Slide 17: PAPR and Average Power
4us ON signal
Sample idx | Option 1 | Option 2 | Option 3 | Option 4
1~64 + CP | 1/0.9896 (2.0611) | 1/1.0104 (2.2371) | 1/0.8717 (4.2759) | 1/0.9903 (3.9954)
average normalized signal power / average CP power
(PAPR [dB])

## Slide 18: PAPR and Average Power
2us ON signal – select first or second 32 samples in 64 samples and insert 8 CP
Sample idx | Option 1 | Option 2 | Option 3 | Option 4
1~32 + CP | 1/1.1249 (2.0003) | 1/0.9585 (2.2804) | 1.0208/0.9599 (4.2364) | 1/0.9853 (3.9930)
33~64 + CP | 1/1.1249 (2.0003) | 1/0.9585 (2.2804) | 0.9792/0.9208 (4.2142) | 1/1.0021 (4.0538)
average normalized signal power / average CP power
(PAPR [dB])

## Slide 19: PAPR and Average Power
1us ON signal – select 16 samples and insert 4 CP
Sample idx | Option 1 | Option 2 | Option 3 | Option 4
1~16 + CP | 1.0104/0.6224 (2.4872) | 0.9896/1.2087 (2.1466) | 0.8508/0.5245 (2.4873) | 1.0528/0.5378 (4.3540)
17~32 + CP | 0.9896/1.0616 (2.0884) | 1.0104/0.7695 (2.5338) | 1.1908/0.8107 (3.8541) | 0.9472/1.6514 (2.4228)
33~48 + CP | 1.0104/0.6224 (2.4872) | 0.9896/1.2087 (2.1466) | 1.0867/1.8506 (3.0136) | 1.0097/0.8239 (3.1590)
49~64 + CP | 0.9896/1.0616 (2.0884) | 1.0104/0.7695 (2.5338) | 0.8717/1.1911 (2.5171) | 0.9903/0.6927 (4.1239)
average normalized signal power / average CP power
(PAPR [dB])

## Slide 20: PAPR and Average Power
0.5us ON signal – select 8 samples and insert 2 CP
Sample idx | Option 1 | Option 2 | Option 3 | Option 4
1~8 + CP | 0.9790/1.1004 (1.3079) | 0.9376/1.2076 (2.4105) | 1.0005/0.5909 (1.7353) | 0.8634/1.3160 (3.4441)
9~16 + CP | 1.0418/0.3149 (2.9152) | 1.0415/0.9058 (2.0841) | 0.7011/0.5081 (2.8402) | 1.2422/0.4491 (4.0059)
17~24 + CP | 0.8543/1.5432 (1.8291) | 1.0624/0.7648 (2.2233) | 1.4217/1.0102 (2.7253) | 0.9091/1.1600 (1.4824)
25~32 + CP | 1.1249/0.8059 (1.8259) | 0.9585/0.4148 (3.0083) | 0.9599/0.5754 (3.1953) | 0.9853/1.7010 (2.3394)
33~40 + CP | 0.9790/1.1004 (1.3079) | 0.9376/1.2076 (2.4105) | 0.7551/1.0588 (2.4608) | 1.0823/0.0836 (3.5187)
41~48 + CP | 1.0418/0.3149 (2.9152) | 1.0415/0.9058 (2.0841) | 1.4182/2.4842 (2.0556) | 0.9371/0.5553 (1.9997)
49~56 + CP | 0.8543/1.5432 (1.8291) | 1.0624/0.7648 (2.2233) | 0.8226/0.9240 (3.2464) | 0.9785/2.1116 (2.8054)
57~64 + CP | 1.1249/0.8059 (1.8259) | 0.9585/0.4148 (3.0083) | 0.9208/1.3197 (1.1498) | 1.0021/1.0948 (3.9048)
average normalized signal power / average CP power
(PAPR [dB])

## Slide 21: PAPR and Average Power
2us ON signal – select first or second 40 samples in 80 samples (16 CP + 64 samples)
Range | Option 1 | Option 2 | Option 3 | Option 4
first 2us | 2.1228 | 2.1942 | 4.2783 | 3.9978
last 2us | 2.0003 | 2.2804 | 4.2734 | 3.9930
PAPR [dB]

## Slide 22: PAPR and Average Power
1us ON signal – select 20 samples
Range | Option 1 | Option 2 | Option 3 | Option 4
first 1us | 2.1307 | 2.5952 | 2.4949 | 4.0556
second 1us | 2.1051 | 1.8271 | 4.1335 | 3.9408
third 1us | 1.5464 | 2.4375 | 2.7863 | 2.6718
last 1us | 2.5072 | 2.1289 | 3.8081 | 4.1905
PAPR [dB]

## Slide 23: PAPR and Average Power
0.5us ON signal – select 10 samples
Range | Option 1 | Option 2 | Option 3 | Option 4
first 0.5us | 2.0925 | 2.0040 | 3.5382 | 3.0997
second 0.5us | 1.4864 | 3.0897 | 0.6931 | 2.5252
third 0.5us | 1.2842 | 1.4725 | 1.4750 | 3.1864
forth 0.5us | 3.1182 | 2.0661 | 3.0394 | 2.0944
fifth 0.5us | 1.9052 | 3.0277 | 3.3159 | 2.3913
sixth 0.5us | 0.9761 | 1.9179 | 2.3144 | 2.9717
seventh 0.5us | 3.5048 | 1.4446 | 3.2492 | 3.6372
last 0.5us | 1.3877 | 2.7417 | 1.5553 | 3.1733
PAPR [dB]

## Slide 24: PAPR and Average Power
2us ON signal – select 40 samples minimizing PAPR in 80 samples (16 CP + 64 samples)
Option 1 | Option 2 | Option 3 | Option 4
20:59 (1.7991) | 5:44 (2.1154) | 26:65 (3.8325) | 27:66 (3.2642)
sample index
(PAPR [dB])

## Slide 25: PAPR and Average Power
1us ON signal – select 20 samples
Option 1 | Option 2 | Option 3 | Option 4
7:26 (1.4413) | 20:39/52:71 (1.7142) | 5:24 (1.5005) | 44:63 (2.2851)
sample index
(PAPR [dB])

## Slide 26: PAPR and Average Power
0.5us ON signal – select 10 samples
Option 1 | Option 2 | Option 3 | Option 4
5:14 (0.9759) | 28:37 (1.3515) | 12:21 (0.6061) | 44:53 (1.0537)
sample index
(PAPR [dB])