## Slide 1: Definition of WUR Mode
Date: 2017-07-10
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com

## Slide 2: Background
In [1,2], it is agreed that we will define TBD signaling for entering WUR Mode. However, the detailed definition of WUR mode remains undefined.
In this presentation, we provide our thought for the definition of WUR Mode
  The proposal aligns with the examples shared in [3] and the high level concept presented in [4]

## Slide 3: Consideration for Integrating WUR Mode with Current Power Management Mode
We think there is no need to define new power management mode for WUR Mode
  This is similar to the definition of WNM Sleep Mode
  As a result, there is no need to define corresponding signaling for transition between new power management mode and old power management mode, which is likely to reuse the current signaling as we have discussed in [3]
Proposal: Simply define that STA follows the duty cycle schedule agreed between AP and non-AP STA when STA is in the Doze state
  Focus on the key feature
  Keep most of the baseline spec about power management mode unchanged
  Saving tremendous time for spec writing and backward spec compatibility

## Slide 4: Consideration for Integrating WUR Mode with Current Power Save Protocols
As discussed in [3], for unscheduled power save protocols like PSM, PSP, and U-APSD, WUR works naturally with these protocols by introducing WURx capability when STA is in doze state
For scheduled power save protocols, like TWT or schedule for WNM sleep mode, we need additional description
  To enable long sleep under WUR Mode, the existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (ex. TWT, schedule for WNM sleep mode) is suspended
  Specifically, STA is not required to wake up during the service period if the service period is suspended
  The parameters of the negotiated service period for the non-AP STA’s PCR schedule is still saved by the AP and non-AP STA when the negotiated service period is suspended

## Slide 5: Conclusion
We provide further details for the definition of WUR Mode
  Focus on the key feature of enabling WURx capability when STA is in the Doze state
  Suspend existing negotiated service period of PCR and still save the corresponding parameters for the service period
  The proposal does not exclude adding other definitions in the future

## Slide 6: Straw Poll 1
Do you support that if a non-AP STA is in WUR mode, then
  the non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the Doze state
  the existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (ex. TWT, schedule for WNM Sleep Mode) is suspended
    STA is not required to wake up during the service period if the service period is suspended
    The parameters of the negotiated service period for the non-AP STA’s PCR schedule is still saved by the AP and non-AP STA when the negotiated service period is suspended

## Slide 7: Reference
[1] 11-17-0575-01-00ba Spec Framework
[2] 11-17-0379-04-00ba SFD MAC proposal
[3] 11-17-0653-00-00ba Examples of Integrating WUR with Existing Power Save Protocol
[4] 11-17-0936-00-00ba Integration of WUR to Power Save Mode