## Slide 1: Address structure in unicast wake-up frame
Date: 2017-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
WUR frame contains transmitter address (e.g., short BSS identifier) and/or receiver address (e.g., STA ID)
  In SFD(17/575r1): The identifier of transmitter and/or receiver in a wake-up frame shall not be the MAC address.
    Because the MAC address is large overhead (48 bits)
We need to decide the exact format of transmitter address and receiver address considering the packet overhead and false alarm
In this contribution we discusses the detailed RX/TX identifier structure for unicast WUR frame

## Slide 3: STA(RX) identifier (1/5)
Option 1: AID (e.g., 11 bits) of WLAN
  AID is spared with legacy STAs (11n/ac/ax).
  The WUR mode STAs may be less than legacy STAs.
  Some of WUR mode STAs can enter the PCR mode to receive or send WLAN frame
  Therefore, it is not efficient that AID for WLAN is always used in unicast wake-up frame because of WUR frame overhead, especially in small number of WUR mode STAs
  Overhead comparison of 11bits AID per data rate [1]
Data rates | Overhead of 11bits AID
WLAN(OFDM) - MCS0 | About 2 us
11ba – 250 kbps | 44us
11ba – 125 kbps | 88us
11ba – 62.5 kbps | 176 us
11ba – 31.25kbps | 352 us

## Slide 4: STA(RX) identifier (2/5)
Option 2 : new ID for WUR mode STAs[2-4]
  AP assigns WUR ID (WID) to STA with WUR capability before the STA enters the WUR mode
    E.g.,) Association, WUR parameter negotiation, or WUR mode entering
  WUR ID is used in WUR mode (i.e., WUR frames)
  The length of WUR ID will be shorter than AID (e.g., 6, 8)
AP
STA
WUR-REQ
WUR-RSP
(WID=1)
WUR entering
ACK
PCR mode
WUR packet
(WID=1)
PS-Poll
ACK
WUR mode
PCR mode

## Slide 5: STA(RX) identifier (3/5)
Option 3: Variable WUR ID
  AP assigns a WID to a STA with WUR mode capability through PCR
  WID size is included in WUR packet
    E.g.,) 0 – 11 bits WID, 1- 6 bits WID
    1 bit Flag (F): 0 indicates 11 bits WID and 1 indicates 6 bits WID
    This information can be combined with other field (e.g., Frame Type )
      E.g.,) FT=0 indicates unicast WUP w/ 11 bits WID and FT=1 indicates unicast WUP w/ 6 bits WID
  If the indication is 0, the WUR STA compares its 6 LSBs of WID with the WID in WUP. If the indication is 1, the WUR STA compares its 11 LSBs of WID with the WID in WUP
FT
Unicast WUP
TxID
11bits WID
FCS
F=0
FT
TxID
6bits WID
FCS
F=1

## Slide 6: STA(RX) identifier (4/5)
Option 4 : Combination of AID and short WID
  AP can assign short WUR ID (e.g., 6 bits, fixed size) to a STA with WUR capability. That is, AP may not assign WUR ID to a STA with WUR capability due to no space of WID
  If WUR ID is allocated to a WUR STA, AP uses WUR ID in WUR frame for the STA. Otherwise, AP uses AID in WUR frame
  Signaling of indicating if WUR frame contains AID or WID
    1 bit Flag (F): 0 indicates 11 bits AID and 1 indicates 6 bits WID
    This information can be combined with other field (e.g., Frame Type )
      E.g.,) FT=0 indicates unicast WUP w/ 11 bits AID and FT=1 indicates unicast WUP w/ 6 bits WID
FT
Unicast WUP
TxID
AID
FCS
F=0
FT
TxID
WID
FCS
F=1

## Slide 7: STA(RX) identifier (5/5)
Option 5 : Combination of AID and Short AID (SAID)
  Short AID is N least significant bit(LSB)s of AID. Therefore, in addition to AID, AP doesn’t have to assign SAID to WUR STA.
  WID size indication is included in unicast WUP
    1 bit Flag (F): 0 indicates 11 bits AID and 1 indicates 6 bits SAID
    This information can be combined with other field (e.g., Frame Type )
      E.g.,) FT=0 indicates unicast WUP w/ 11 bits AID, FT=1 indicates unicast WUP w/ 6bits SAID
  For STAs with the same SAID, AP uses AID instead of SAID
FT
Unicast WUP
TxID
AID (11bits)
FCS
F=0
FT
TxID
6 bits SAID
FCS
F=1

## Slide 8: BSS(TX) identifier
Long BSS identifier can prevent the false alarm but increase the overhead of WUR frame
There are several options as short BSS(e.g.,) identifier in WUR frame
  The 9 LSBs of BSSID (PBSSID) is used as AP’s identifier of VHT-SIG-A in VHT UL PPDU
    PBSSID collision may happen but not often due to long length
  6bits BSS Color is used as AP’s identifier in HE-SIG-A of HE PPDUs
    Due to its small size, the BSS Color disabling and BSS Color change procedures have also been defined to minimize the BSS Color collision.
In [5], 8 bits BSS Color was proposed for very dense networks
  The largest stadium WLANs require 10 bits in 2.4-GHz or for a reuse=3 plan
It seems like that 8 bits (or 10 bits) is enough for the size of BSS identifier
[7] 11-15/1136r1, BSS Color Field Size Measurements

## Slide 9: Conclusion
Need to decide the structure of TX/RX identifiers considering the several points such as packet overhead, false alarm, implementation, etc.
Proposed
  RX identifier Option 1: legacy AID (11bits)
    Option 2: new ID only for WUR ID (WID) (e.g., 8 bits)
    Option 3: variable WIDs (e.g., 6 bits and 11 bits)
    Option 4: AID + Short WID(s) (e.g., 6 bits)
    Option 5: AID + Short AID(s) (e.g., 6 bits)
    See the appendix for comparison of each option
  TX identifier
    8 or 10 bits BSS identifier (e.g., partial BSS identifier or BSS Color)

## Slide 10: References
[1] 11-17-0965-00-00ba-data-rate-for-range-requirement-in-11ba
[2] 11-17-0054-03-00ba-wur-mac-issus
[3] 11-17-0071-00-00ba-high-level-mac-concept-for-wur
[4] 11-17-0379-04-00ba-sfd-mac-proposal
[5] 11-15/1136r1, BSS Color Field Size Measurements

## Slide 11: Straw Poll 1
Do you agree the following?
  11ba shall define the short RxID to be included in unicast wake-up frame
    Short RxID is the receiver identifier of which length is shorter than 11 LSBs of AID

## Slide 12: Straw Poll 2
Which option do you prefer as Short RxID?
  Option 1: Short AID
    Short AID is N least significant bit(LSB)s of AID (N is TBD)
  Option 2: WUR ID
    WUR ID is assigned during WUR negotiation on PCR

## Slide 13: Straw Poll 3
Which option do you prefer as TX identifier?
  Option 1: BSS Color
  Option 2: Partial BSSID (Partial BSSID is N least significant bit(LSB)s of BSSID)

## Slide 14: Straw Poll 4
Which option do you prefer as the size of TX identifier?
  Option 1: 6 bits
  Option 2: 8 bits
  Option 3: 10 bits
  Option 4: more than 10 bits

## Slide 15: Appendix: Comparison of each option
 | Overhead | New ID alloc. | Flexibility | ID size indication
Option 1 (AID only) | High | No | Fixed size | No
Option 2 (WID) | Low | Yes | Fixed size | No
Option 3 (Variable WID) | Medium | Yes | Flexible | Yes
Option 4 (AID + WID) | Medium | Yes (Not all) | Flexible | Yes
Option 5 (AID + S-AID) | Medium | No | Flexible | Yes