## Slide 1: Address structure in unicast wake-up frame
Date: 2017-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
WUR frame contains transmitter address (e.g., short BSS identifier) and/or receiver address (e.g., STA ID)
  In SFD(17/575r1): The identifier of transmitter and/or receiver in a wake-up frame shall not be the MAC address.
    Because the MAC address is large overhead (48 bits)
We need to decide the exact format of transmitter address and receiver address considering the packet overhead and false alarm
In this contribution we discusses the detailed RX/TX identifier structure for unicast WUR frame

## Slide 3: STA(RX) identifier (1/3)
Option 1: AID (e.g., 11 bits) of WLAN
  AID is spared with legacy STAs (11n/ac/ax).
  The number of WUR mode STAs may be less than that of legacy STAs.
  Some of WUR mode STAs can stay in the PCR mode to receive/send WLAN frame from/to AP
  Therefore, it is not efficient that AID for WLAN is always used in unicast wake-up frame because of WUR frame unnecessary overhead, especially in the small number of WUR mode STAs
  Overhead of 11bits AID per data rate [1]
Data rates | Overhead of 11bits AID
WLAN(OFDM) - MCS0 | About 2 us
11ba – 250 kbps | 44us
11ba – 125 kbps | 88us
11ba – 62.5 kbps | 176 us

## Slide 4: STA(RX) identifier (2/3)
Option 2 : new ID for WUR mode STAs[2-4]
  AP assigns WUR ID (WID) to STA with WUR capability through the PCR
    E.g.,) Association, WUR parameter negotiation, or WUR mode entering
  WUR ID is used in WUR mode (i.e., WUR frames)
  The length of WUR ID will be shorter than that of AID (e.g., 6, 8 bits)
AP
STA
WUR-REQ
WUR-RSP
(WID=1)
WUR entering
ACK
PCR mode
WUR packet
(WID=1)
PS-Poll
ACK
WUR mode
PCR mode

## Slide 5: STA(RX) identifier (3/3)
Option 3: Variable WUR ID
  AP assigns an 11bits WID to a STA with WUR mode capability through PCR
  WID size can be indicated in WUR packet
    E.g.,) 0- 11 bits WID, 1- 6 bits WID (6 LSB of 11bits WID)
    The Frame Type (FT) can indicate the size of WID
  If the FT is 0, the WUR STA compares its 11bits WID with the WID in WUP
  If the FT is 1, the WUR STA compares 6 LSBs of its WID with the WID in WUP.
FT=0
Unicast WUP
TxID
11bits WID
FCS
FT=1
TxID
6bits WID
FCS

## Slide 6: BSS(TX) identifier
Long BSS identifier can prevent the false alarm but increase the overhead of WUR frame
There are several options as short BSS(e.g.,) identifier in WUR frame
  The 9 LSBs of BSSID (PBSSID) is used as AP’s identifier of VHT-SIG-A in VHT UL PPDU
    PBSSID collision may happen but not often due to long length
  6bits BSS Color is used as AP’s identifier in HE-SIG-A of HE PPDUs
    Due to its small size, the BSS Color disabling and BSS Color change procedures have also been defined to minimize the BSS Color collision.
In [5], 8 bits BSS Color was proposed for very dense networks
  The largest stadium WLANs require 10 bits in 2.4-GHz or for a reuse=3 plan
It seems like that 8 bits (or 10 bits) is enough as the size of BSS identifier
[5] 11-15/1136r1, BSS Color Field Size Measurements

## Slide 7: Conclusion
Need to decide the structure of TX/RX identifiers considering the several points such as packet overhead, false alarm, implementation, etc.
Proposed
  RX identifier
    Option 1: legacy AID (11bits)
    Option 2: new ID only for WUR ID (WID) (e.g., 8 bits)
    Option 3: variable WIDs (e.g., 6 bits and 11 bits)
  TX identifier
    8 or 10 bits BSS identifier (e.g., partial BSS identifier or BSS Color)

## Slide 8: References
[1] 11-17-0965-00-00ba-data-rate-for-range-requirement-in-11ba
[2] 11-17-0054-03-00ba-wur-mac-issus
[3] 11-17-0071-00-00ba-high-level-mac-concept-for-wur
[4] 11-17-0379-04-00ba-sfd-mac-proposal
[5] 11-15/1136r1, BSS Color Field Size Measurements

## Slide 9: Straw Poll 1
Do you agree the following?
  R.4.2.B. The WUR Action frame sent by an AP through the PCR includes a WUR receiver identifier (WID)
    WID uniquely identifies a WUR STA within a BSS
    WID is included in a unicast wake-up packet as the receiver identifier to wake up the WUR STA
    The size of WID is TBD and how it is computed is TBD
  Y/N/A : 25/0/6

## Slide 10: Straw Poll 2
Which option do you prefer as TX identifier included in the unicast WUR packet?
  Option 1: BSS Color (The size is TBD)
  Option 2: Partial BSSID (Partial BSSID is N least significant bit(LSB)s of BSSID)
  Option 3: abstain
  Option 1: 10, Option 2: 4, Option 3: 15

## Slide 11: Straw Poll 3
Do you agree the following?
  BSS Color / Partial BSSID is included in a WUR packet sent by an AP as a transmitter address
  The size of the BSS Color / Partial BSSID is TBD

## Slide 12: Motion
Move to add the following into 11ba SFD
  R.4.2.B. The WUR Action frame sent by an AP through the PCR includes a WUR receiver identifier (WID)
    WID uniquely identifies a WUR STA within a BSS
    WID is included in a unicast wake-up packet as the receiver identifier to wake up the WUR STA
    The size of WID is TBD and how it is computed is TBD
Moved by: Jeongki Kim
Seconded by: Kiseon Ryu
Result: Passed by unanimous consent