## Slide 1: Power saving operation for WUR STAs in duty cycle mode
Date: 2017-0x-0x
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Upon receiving the wake-up frame intended for the STA, the STA turns on its primary connectivity radio
AP may send a broadcast wake-up frame for waking up multiple WUR STAs
  In SFD [1]: After the transmission of broadcast wake-up frame, the AP can transmit broadcast/multicast frames through primary connectivity radio after the preparation period.
WUR duty cycle in 11ba SFD [1]
  STA can have Duty cycle mode for wake-up receiver (WURx)
  The period of the WUR duty cycle as shown below is a multiple of a basic unit. The basic unit is indicated by the AP. The on duration in each period for WUR duty cycle as shown below is larger than or equal to a minimum wake-up duration. The minimum wake-up duration is indicated by the AP.

## Slide 3: Motivation (1/2)
A WUR STA, especially in duty cycle mode, may waste its power after receiving the wake-up frame for it
Example 1: A wake-up frame (WUF) can be sent for WUR STAs to update system parameter by receiving Beacon [x]
On
On
On
On
On
On
On
On
B
Wake-up frame
AP
S1
S2
S3
S4
Awake state in PCR
On
On duration in WUR duty cycle
B
B
B
B
WLAN Beacon

## Slide 4: Motivation (2/2)
A wake-up frame can be sent for WUR STAs to receive DTIM for group addressed BU
On
On
On
On
On
On
On
On
B
Wake-up frame
AP
S1
S2
S3
S4
Awake state in PCR
On
On duration in duty cycle
B
D
B
B
WLAN
Beacon
D
DTIM Beacon
G
Group addressed BU
G

## Slide 5: Proposal (1/6)
For case 1
  If WUR STA can know that the WUF is for Beacon reception, the STA can wake up until the next TBTT without unnecessary power consumption
  For this purpose, AP includes the Beacon reception indicator in WUF
On
On
On
On
On
On
On
On
B
WUF with Beacon RX indicator
AP
S1
S2
S3
S4
Awake state in PCR
On
On duration in WUR duty cycle
B
B
B
B
WLAN Beacon
Additional power saving period
Notes: Beacon을 받도록 하는 WUF를 받지 못하면 ,, system parameter update.
BSS Change count를 이용하는 좋아보임…
1 bit나 2 bits이용…

## Slide 6: Proposal (2/6)
For case 2
  For WUR STAs to receive DTIM, AP includes the DTIM reception indicator in WUF.
  If the next Beacon is DTIM Beacon, AP may simply include the Beacon reception indicator in WUF instead of DTIM reception indicator
On
On
On
On
On
On
On
On
B
WUF w/ DTIM RX indicator
AP
S1
S2
S3
S4
Awake state in PCR
On
On duration in duty cycle
B
D
B
B
WLAN
Beacon
D
DTIM Beacon
G
Group addressed BU
G
Additional power saving period

## Slide 7: Proposal (3/6)
WUR STAs may wake up every WUR Beacon TX time to synchronize with its associated AP
For WUR STAs that are required to receive every WUR Beacon, Beacon reception indicator can be delivered in WUR Beacon w/o sending additional wake-up frame during their ON-Durations
WB_On
On
On
WB_On
B
WB
AP
S1
B
B
B
S2
On
On
WB
WUR Beacon w/ Beacon RX indicator
On
On duration in duty cycle
B
WLAN
Beacon
On duration for WUR Beacon
WB_On
Awake state in PCR

## Slide 8: Proposal (4/6)
DTIM reception indicator can also be delivered in WUR Beacon
WB
WUR Beacon w/ DTIM RX indicator
On
On duration in duty cycle
B
WLAN
Beacon
On duration for WUR Beacon
WB_On
B
AP
S2
B
D
B
G
WB_On
On
On
WB_On
S1
S2
On
On
WB
Awake state in PCR
D
DTIM Beacon
G
Group addressed BU
Additional power saving period

## Slide 9: Proposal (5/6)
Wake-up frame format
  RX ID may not be included in broadcast wake-up frame
  Wake-up reason
    0: Normal wakeup
    1: Next Beacon reception
    2: Next DTIM reception
  Wake-up reason info can be combined in other field (e.g., Frame Type)
    E.g., FT= 0: Broadcast WUF for Beacon RX, FT=1: Broadcast WUF for DTIM RX
WUR Beacon
  Wake-up indicator
    0: No wake-up
    1: Wake-up for next Beacon reception
    2: Wake-up for next DTIM reception
Frame Type
TX ID
(RX ID)
Wake-up reason
FCS
Frame Type
TX ID
Wake-up indicator
FCS
Timestamp
Notes: Time sync 공유할 때는,
time sync 공유하지 않을 때 사용하는 것, 추가. Wakeup completion time,
둘 다 살릴 수 있는 방법.

## Slide 10: Proposal (6/6)
By wake-up reason field/wake-up indicator field, STA in WUR duty cycle mode can save more power
  The STA can adjust the start time of wake-up procedure based on its wake-up delay and next Beacon/DTIM TX time
  The STA can re-enter the WUR mode after receiving Beacon or Group address BU
    That is, if there aren’t these fields, the STA cannot know if it can enter the WUR mode after receiving Beacon/Group address BU or not
Notes: Time sync 공유할 때는,
time sync 공유하지 않을 때 사용하는 것, 추가. Wakeup completion time,
둘 다 살릴 수 있는 방법.

## Slide 11: Conclusion
To reduce the power consumption of WUR STAs that are in duty cycle mode, the Beacon reception indicator or DTIM reception indicator need to be included in a wake-up frame or WUR Beacon
  The following fields can be included
    Wake-up reason (in broadcast WUF)
      0: Next Beacon reception
      1: Next DTIM reception
    Wake-up indicator (in WUR Beacon)
      0: No wake-up
      1: Wake-up for Next Beacon reception
      2: Wake-up for Next DTIM reception

## Slide 12: References
[1] 11-17-0575-01-00ba-spec-framework

## Slide 13: Straw Poll 1
Do you agree the following?
  A WUR Beacon frame contains the following wake-up indicator
    Wakeup indicator
      0: No wake-up
      1: Wake-up for Next Beacon reception
      2: Wake-up for Next DTIM reception

## Slide 14: Straw Poll 2
Do you agree the following?
  A broadcast wake-up frame contains the following wake-up reason information
    Wake-up reason
      0: Next Beacon reception
      1: Next DTIM reception
    This information may be combined with other field (e.g., frame type).