## Slide 1: WUR Data Rates
Date: 2017-07-08
Authors:

## Slide 2: Multiple Data Rates
TGba has decided to support multiple data rates [1]
  “R.3.3.D: IEEE 802.11ba supports multiple data rates for the payload part of the wake-up packet”
We need to agree on the values of those data rates
Design and Simulations of various data rates were provided in May [2]
[1] Po-Kai Huang, “Specification Framework for TGba,” IEEE 802.11-17/575r1, May 2017
[2] Steve Shellhammer and Bin Tian, “Data Rates and Coding,” IEEE 802.11-17/670r0, May 2017

## Slide 3: Link Budget (Channel Model D) (From [2])
MR Data Rate (Mb/s) | Frequency Band (GHz) | MR SNR (dB) | TX Power Delta (dB) | Noise Figure Delta (dB) | Impairment Budget (dB) | WUR SNR (dB)
6 | 2.4 | 10 | 4 | 8 | 2 | -4
6 | 5 | 10 | 7 | 8 | 2 | -7
1 | 2.4 | 2 | 4 | 8 | 2 | -12
Wake-up Radio SNR
Main Radio SNR
Difference in TX power due to Regulations
Difference Receiver Noise Figure
Budget for Impairment Loss
Note: SNR is defined with a 20 MHz noise bandwidth for easy comparison. It can be converted to a 4 MHz bandwidth (for example) by
[2] Steve Shellhammer and Bin Tian, “Data Rates and Coding,” IEEE 802.11-17/670r0, May 2017

## Slide 4: Data Field Designs

## Slide 5: Link Budget Margin
Design | Data Rate (kb/s) | 10%-PER SNR (dB) Model D | Margin 6 Mb/s 2.4 GHz | Margin 6 Mb/s 5 GHz | Margin 1 Mb/s 2.4 GHz
Manchester Code | 250 | 1.0 | -5.0 | -8.0 | -13.0
Manchester Code | 125 | -1.1 | -2.9 | -5.9 | -10.9
Repetition Code & Manchester Code | 62.5 | -2.9 | -1.1 | -4.1 | -9.1
BCC & Manchester Code | 62.5 | -5.3 | 1.3 | -1.7 | -6.7
BCC & Repetition & Manchester | 31.25 | -7.4 | 3.4 | 0.4 | -4.6
Positive Link Budget Margin shown in GREEN
Negative Link Budget Margin shown in RED, indicates the number of dB short of matching the main radio link budget
If WUR needs to operate at higher reliability, like 1% PER, then link budget of the WUR, compared to main radio, is even worse
All cases are based on Regulatory TX power limit

## Slide 6: BCC
Use of BCC provides 2.4 dB gain over 2x repetition code, at the same data rate
BCC with Manchester Code meets the range of 6 Mb/s in 2.4 GHz band
BCC Power Consumption
Based on our power estimates the Energy to Viterbi decode a 100 bit payload is
Decoding a PHY payload occurs at every beacon, and also once in a while for a wake-up packet. Beacons occur approximately every 10 second
Hence the power consumption for BCC is approximately,
This is significantly less power consumption than the RF, and hence does not impact overall power consumption

## Slide 7: Number of Data Rates
In order to limit complexity two data rates is preferred to having three or more data rates
Requirements (our opinion) for these two data rates
Low Data Rate
  Sufficient Receiver Sensitivity to reach “cell edge” stations
High Data Rate
  Sufficient Receiver Sensitivity to reach the most of the stations

## Slide 8: Data Rate Recommendations
Low Data Rate
The 62.5 kb/s can meet (with BCC) or close to meet (without BCC) the range of the 6 Mb/s PHY in the 2.4 GHz frequency band, hence it is a good choice for the low data rate
High Data Rate
The 250 kb/s design is a good choice for the high rate providing improved spectral efficiency while still meeting the range of many of the stations in the network

## Slide 9: Straw Poll
Do you support the following?
IEEE 802.11ba will support the following data rates: 62.5 and 250 kb/s
  Support of any other data rates is TBD