## Slide 1: WUR coexistence with existing power save mode
Date: 2017-07-11
Authors:

## Slide 2: Abstract
Discussions on WUR mode transition along with existing power save mode
Follow-up issues for better integration with unscheduled power save protocol

## Slide 3: Power save mechanisms in 802.11
802.11 power save mechanism defines two Power Management modes:
  Active mode: The STA remains in the awake state
  Power save mode: The STA enters the awake state to receive or transmit frames. The STA remains in the doze state otherwise.
    Normal PS mode(PS-poll), U-APSD
After successful frame exchange with PM subfield indication, STA may change its PM mode
  AP shall maintain for each associated STA a Power Management status

## Slide 4: New power save mechanisms in TGba
TGba introduces additional power save mechanism
  STA may transit its WUR mode between on/off
    STA may use WUR mode request frame or element for state transition
  In WUR mode, STA only receives WUP and may wake up its PCR
In the mentioned 3 modes, possible actions and expected reactions of STA could be different
In order to integrate WUR with PCR power save mechanism seamlessly, it is important to define how STA maintains and transits its state among them

## Slide 5: WUR mode transition with PM mode (1)
1) Including WUR mode as another PM mode
  One transition diagram consists of three modes
    Active, PS, WUR
  State transition diagram might become more complicated
  Transition conditions for each mode must be further defined
    May require additional signaling for each transition
  Require to define additional PM mode in the baseline
    As well as corresponding behaviors
Option (1) is not preferable
  Implementation complexity
  Requiring many changes to existing PM mode behavior

## Slide 6: WUR mode transition with PM mode (2)
2) Maintaining WUR mode separate from PM mode
  AP maintains PM mode and WUR mode of each associated STA independently
  STA might use both PS mode and WUR mode simultaneously
    Similar with WNM sleep mode
Option 2) seems more beneficial, since:
  State transition diagram is simpler
  No additional signaling methods are necessary for mode transition
    Little or no modification is required for baseline PM mode

## Slide 7: Further consideration on option (2)
Applying option (2), we may reuse the baseline power save spec text as it is
The baseline requires a non-AP STA in PS mode to wake up periodically
  Beacon period for unscheduled power save protocols
    Normal power save mode, U-APSD
  Scheduled service period for scheduled power save protocols
    WNM sleep, TWT
As the periodic wake-up events can be replaced by WUP transmission, we can relieve the wake-up requirements
  In order to save more power
  For example, non-AP STA using an unscheduled power save protocol, it may not wake-up to receive Beacon frame

## Slide 8: Follow-up issues for better integration with unscheduled power save protocol
WUR allows AP to wake-up a non-AP STA to listen when it has a buffered BU
  AP doesn’t have to wait until the STA wakes up by itself
    Low latency can be achieved while STA saves more power
However, unless a wake-up STA responds with an expected frame, AP may not deliver the buffered BU immediately
  In normal PS mode and U-APSD, AP can deliver buffered BUs for a STA in PS mode only when it receives a specific frame
    PS-poll (normal PS mode) or trigger frame (U-APSD)
  In such case low latency gain of WUR may not be achieved
  And STA will consume more power

## Slide 9: WUR with normal PS mode
For a STA using normal PS mode, AP delivers buffered BU only when it receives PS-poll from the STA
  If the STA transmits a frame other than PS-poll in response to unicast WUP, it cannot retrieve buffered BU
    STA might wait until the next beacon reception to retrieve BUs
Nevertheless the intends to respond with PS-poll, it should transmit it using AC_BE
  AC_BE is defined to to reduce the likelihood of collision following a Beacon frame
It is better to respond with PS-poll when a STA using normal PS mode receives unicast WUP
  In such case, the transmission of PS-poll could have higher priority
WUP
QoS Data or Null
Ack
BU
PS-poll
Ack or single BU
Latency
Beacon

## Slide 10: WUR with U-APSD
A STA using PS mode may choose which ACs use U-APSD
  The ACs using U-APSD are regarded as trigger-enabled/delivery-enabled AC
  Other ACs use normal PS mode
According to 11.2.3.6 AP operation during the CP
  “For a STA using U-APSD, the AP transmits one BU destined for the STA from any AC that is not delivery-enabled in response to PS-Poll frame from the STA.”
  “The AP transmits BUs destined for the STA and using delivery-enabled ACs during an unscheduled SP.”
Upon the reception of a unicast WUP, the STA may not know for which AC it should retrieve buffered BUs
Latency and power consumption will increase until an appropriate retrieving frame is sent
  As well as unnecessary channel occupation
WUP
PS-poll
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for VO
WUP
trigger frame
Ack
VO
VI
U-APSD
BE
BK
Normal PS
BU for BE
trigger frame
Ack
SP start
BU
Latency
SP early termination
QoS Null EOSP:1
Ack
PS-poll
Ack or single BU
Latency

## Slide 11: Proposal (1)
We can consider including some information in unicast WUP to optimize non-AP STA’s wake-up behavior
  E.g., AC bitmap (4 bits), U-APSD/PS-poll flag
Assuming AC bitmap is included in each unicast WUP
  indicating presence of buffered BU for each AC
STA can adapt its response behavior with given information
  It can choose a proper response type and access class
  Improving efficiency of wake-up event without modification of legacy PS mode
WUP
PS-poll
Ack
VO
VI
BE
BK
Normal PS
BU for BE
BU
Latency
AC bitmap
Channel Access using AC_VI
VO
VI
U-APSD
BE
BK
Normal PS
WUP
trigger frame (AC_VO)
Ack
BU for VO
BU (EOSP:0)
Ack
BU (EOSP:0)
Latency
AC bitmap
Ack
SP start
STA might choose its response type and access class

## Slide 12: Proposal (2)
If a WUR non-AP STA uses U-APSD, all ACs shall be set to trigger/delivery-enabled AC
  To avoid ambiguity without having information in WUP
STA will respond with the expected frame if it is willing to retrieve buffered BUs
WUP
PS-poll
Ack
VO
VI
BE
BK
Normal PS
BU for BE
BU
Latency
VO
VI
U-APSD
BE
BK
WUP
trigger frame (AC_VO)
Ack
BU for VO
BU (EOSP:0)
Ack
BU (EOSP:0)
Latency
Ack
SP start

## Slide 13: Summary
We have discussed WUR mode transition along with existing power save mode
  Maintaining WUR mode and PM mode separately
Follow-up issues for better integration with unscheduled power save protocol
  1) Adding information in unicast WUP
    E.g., AC bitmap
  2) Additional condition for WUR STA using unscheduled power save mode

## Slide 14: Strawpoll 1
Do you support the following?
A non-STA may use both PS mode and WUR mode simultaneously
  If the non-AP STA is using one of unscheduled power save protocols (e.g., normal PS mode, U-APSD), it may not wake-up to receive Beacon frame
Y/N/A

## Slide 15: Strawpoll 2
Do you support the following?
Unicast wake-up signal shall contain an information to optimize wake-up response behavior of the destined STA
Y/N/A

## Slide 16: Strawpoll 3
Do you support the following?
If a WUR non-AP STA uses U-APSD, all ACs shall be set to trigger/delivery-enabled AC
Y/N/A