## Slide 1
Considerations on WUP bandwidth and CCA
Date: 2017-07-11
Authors:

## Slide 2: Introduction
WUP is consist of full-bandwidth legacy preamble part and narrow band 11ba specific part[1]
  R.3.1.A: A 20MHz non-HT preamble is prepended in any WUR PPDU, including L-STF, L-LTF and L-SIG fields. A 20MHz OFDM symbol, with tone spacing 312.5 KHz and BPSK, and of duration 4 us, is present immediately after the L-SIG field and right before the narrow band portion of any WUR PPDU.
WUR payload use OOK for its 11ba specific part[1]
  Use OOK for modulation of the payload portion of the wake-up packet. The Preamble design is TBD. The operation in DFS channels is TBD.
  The OOK waveform of wake-up packet is generated by populating TBD number of 802.11 OFDM subcarriers
    The WUR preamble part is TBD
    The operation in DFS channel is TBD

## Slide 3: Transmission power in a single WUP
In the PAR document, WUR range shall be the same range of primary connectivity radio[2]
  5.2.b. Scope of the project: … The WUR is a companion radio to the primary connectivity radio and meets the same range requirement as the primary connectivity radio. …
In order to meet the same range requirement as the PCR, transmit power of narrow bandwidth part shall be controlled appropriately
  If we assume “same range requirement” means that allocating same power to single OFDM tone with identical tone spacing, power ratio between full-band signal and narrow band signal is identical to bandwidth(number of tone) ratio
  In other words, same Power/Tone for PCR and WUR

## Slide 4: Coexistence problem of WUP
If transmit power of narrow bandwidth part is controlled well, WUR STA does not have any problem to decode its full-band and narrow band signal
However, some legacy STAs may not detect the narrow band signal with 20MHz CCA

## Slide 5: Coexistence problem of WUP
Because of power gap between full-band signal and narrow band signal, legacy 802.11 devices would get false CCA report
In WUR interference area, narrow band WUR signal would interfere legacy devices but the devices cannot detect it

## Slide 6: Full-band TX and narrow band RX
In order to avoid false CCA, full-band WUR signal could be considered as an example of solution
Although transmitted signal is full-band signal OOK WUR signal, WUR RX demodulate it with narrow band OOK WUR signal

## Slide 7: Conclusions
In order to satisfy PAR requirement, transmit power control on narrow-band part of WUP needs to be performed to adjust transmission range of narrow-band signal
Narrow band WUR signal with power control may cause false CCA problem to legacy STAs
Full-band WUR signal transmission and narrow band receiving could be solve the false CCA problem
We need more discussions about the false CCA problem and its solutions when we design WUR signal

## Slide 8: References
[1] 11-17-0575-01 “Specification Framework for TGba”
[2] 11-16-1045-09 “A PAR Proposal for Wake-up Radio”