## Slide 1: Performance Evaluation of OOK Waveform Coding Schemes with Impairments
Date: 2017-07-10
Authors:

## Slide 2: Abstract
In this contribution, we evaluate two waveform coding (WFC) schemes
  Sequence-based on-off keying (OOK) and
  Masking-based OOK
  under carrier frequency offset (CFO), considering standalone, frequency domain multiplexing, and concurrent transmission with 11ax signal scenarios

## Slide 3: Introduction
It has been agreed to use on-off keying (OOK) symbols for 802.11ba WUR payload [1]
Different OOK schemes with Manchester coding (WFC) are proposed for 802.11ba wake-up signal (WUS) payload [2-6]. For example,
  Masking a fixed OFDM symbol [2,3,4]
  Using shaping sequences in frequency [6]
  Using multiple OFDM symbol [5]
It is not trivial to determine which scheme is better for 802.11ba and other WLAN standards when different scenarios, such as frequency domain multiplexing, concurrent transmission (e.g., 11ax+11ba), or standalone operations (only 11ba) are considered
In this study, we compare masking-based OOK and sequence-based OOK under the impairment due to CFO

## Slide 4: Masking-based WFC OOK Symbols
Masking-based WFC OOK symbols are generated by applying a mask to a fixed OFDM symbol. For example, by using 11n OFDM numerology
  A fixed sequence, e.g., [1 -1 1 1 1 1 0 1 -1 -1 1 1 -1] is first mapped around DC subcarrier
  Time domain signal is generated via an IDFT operation of size of 64
  After CP is prepended to OFDM symbol, the OFDM symbols is masked to generate Manchester coded OOK symbols
Since this method masks the OFDM symbol, the original sequence property in the frequency domain cannot be maintained and spreads across the frequency domain
IDFT
(64)
Mapping
Sequence
Masking for Logic 1
Masking for Logic 0
CP+
Logic 1 in time
CP
Logic 0 in time
Data
4 s
4 s

## Slide 5: Sequence-based WFC OOK Symbols
Mapping
DAC
WFC OOK
sequence 1a (Logic 1)
WFC OOK
sequence 1b (Logic 0)
WFC OOK
sequence 2a (Logic 1)
WFC OOK
sequence 2b (Logic 0)
WFC OOK
sequence 3a (Logic 1)
WFC OOK
sequence 3b (Logic 0)
MHz
CP+
802.11ba
802.11ax
RF
IDFT
(256)
time
(e.g., 4 )
s
IDFT output
Amplitude
Sequence 1a/1b affects the first 4
Sequence 2a/2b affects the second 4
Sequence 3a/3b affects the third 4
In [6], we propose to generate the WFC OOK symbol(s) by designing sequences in frequency which remove masking operation
This method has three main benefits:
  Perfect orthogonality between 802.11ax data and 802.11ba for concurrent Tx
  Localized energy in the spectrum to increase coverage range of 11ba
  Enables envelope detector based WURs and correlator-based WURs
An example with 3 OOK symbols are provided as below:
+
+
+

## Slide 6: Simulation Assumptions
Sequence-based OOK:
  The base sequence is derived based on ZC-sequence of length of 7 (The OOK sequences are generated by applying DFT of size of 48, see appendix for the mapping). Frequency domain shaping is applied [6]. The OOK symbol duration is 4.
Masking-based OOK:
  A fixed sequence, e.g., [1 -1 1 1 1 1 0 1 -1 -1 1 1 -1] is first mapped around DC subcarrier. Time domain signal is generated via an IDFT operation of size of 64. After CP is prepended to OFDM symbol, the OFDM symbols is masked to generate Manchester coded OOK symbols. The OOK symbol duration is also 4.
  The BW for WUS is 4 MHz (Sampling rate Fs = 20 MHz). Channel is AWGN.
2nd order Butterworth filter ( = 2.5 MHz, Fs = 20 MHz) is used at 11ba receiver
Three scenarios are considered:
  11ba standalone, 11ba+11ax concurent transmision, 11ba multiplexing (Allocations are provided in the appendix). The BW for 802.11ax OFDM is 20 MHz where .
The impairments: CFO (1 MHz [7] and 2 MHz [8])
WUR compares the energy on first half and second half of the OOK symbols to detect the bit.
The SNR definition given in [7] is taken into account (see appendix for the definition).

## Slide 7: Spectral Analysis
Sequence-based OOK symbols are more confined than masking-based OOK symbols. This means less ACI in the cases of concurrent and frequency domain multiplexing scenarios
Standalone
11ax+11ba concurrent transmission
Frequency multiplexing

## Slide 8: BER Performance (Standalone)
Since sequence-based OOK symbols yield better accumulation after WUR filter, it yields slightly superior performance as compared to masking-based OOK symbols
CFO with 2MHz degrades both of schemes by 1.5 dB for standalone case

## Slide 9: BER Performance (11ax-11ba Concurrent Transmission)
Using 2nd order Butterworth filter causes negligible BER degradation in the case of concurrent transmission for both masking and sequence-based OOK symbols
CFO causes more degradation to 11ba BER performance in the case of concurrent transmission as compared to that of 11ba standalone scenario
While sequence-based OOK symbol do not cause interference to 11ax STAs, masking-based OOK symbols causes significant interference to 11ax STA
11ba performance
11ax performance
ACI due to
11ba
CFO
3 dB

## Slide 10: BER Performance (11ba Multiplexing in Frequency)
The interference due to WUSs in frequency is milder than that of concurrent transmission due to the increased separation between the WUSs in frequency (see the allocation given in appendix)
Since the sequence-based OOK symbols are confined in frequency, they causes less interference to each other. It yields ~2 dB gain as compared masking-based OOK symbols when there is CFO @ 2 MHz

## Slide 11: Conclusions and Discussion (1)
Numerical analysis shows that
  While the sequence-based OOK symbols enable concurrent transmission without interference to 11ax STAs, the masking-based OOK symbols cause more than 3 dB degradation to 11ax STAs at 1e-2 BER
  Since the sequence-based OOK symbols are localized in frequency, which enables capturing more energy than masking-based OOK.
  When WUSs are multiplexed in frequency domain, the sequence-based OOK symbols yield a 2 dB gain as compared to the masking-based OOK symbols when there is CFO of 2 MHz in the case of multiplexing scenario
  CFO causes more BER degradation in the case of concurrent transmission than in the case of 11ba standalone scenario. So, the requirement on CFO needs to be carefully determined.

## Slide 12: Conclusions and Discussion (2)
TGba may need to decide whether concurrent transmission with 11ax and/or multiplexing are desirable capabilities for 11ba since they directly impact on the waveform requirements and selection.
Multiple waveforms have been proposed in TGba, each has certain characteristics and capabilities. To speed up the project and finalize the decision on the waveform, it may be necessary for the group to have a set of specific design requirements associated with a set of system capabilities.

## Slide 13: SP1
Do you think the TGba should agree on a set of requirements, e.g., PAPR, ACI, ACR, before making the decision on waveforms?
  Y: 5
  N: 1
  A: 14

## Slide 14: SP2
Do you agree that the concurrent transmission with 11ax signals (as current defined in the 11ax spec draft) should be one of the 11ba system capabilities?
  Y: 2
  N: 4
  A: 13

## Slide 15: SP3
Do you agree that frequency domain multiplexing transmission of multiple WUSs should be one of 11ba system capabilities?
  Y: 15
  N: 2
  A: 6

## Slide 16: Motion
Move to add to the 802.11ba SFD:
  “802.11ba should support frequency domain multiplexing transmission of multiple WUSs.”
  Y:
  N:
  A:

## Slide 17: References
[1] Shahrnaz Azizi et al., Intel, “Motion for the High Level PHY Design”, IEEE 802.11-17/0368r1, Mar. 2017
[2] Justin Jia Jia et al., Huawei, “Performance Investigations on Single-carrier and Multiple-carrier-based WUR”, IEEE 802.11-17/0373r1, Mar. 2017
[3] Junghoon Suh et al., Huawei, “Waveform Generation for Waveform Coding”, IEEE 802.11-17/0376r0, Mar. 2017
[4] Eunsung Park et al,. LG, “Various Symbol Types for WUR”, IEEE 802.11-17/0350r0, Mar. 2017
[5] Steve Shellhammer, Qualcomm, “WUR Modulation and Coding”, IEEE 802.11-17/0366r0, Mar. 2017
[6] Alphan Sahin et al., Interdigital, “On the Coexistence of 802.11ax and 802.11ba Signals”, IEEE 802.11-17/0659r1, Mar. 2017
[7] Shahrnaz Azizi, Intel, “IEEE 802.11 TGba Simulation Scenarios and Evaluation Methodology Document”, IEEE 802.11-17/0188r05, Jan. 2017
[8] Leif Wilhelmsson, Ericsson, “Concurrent transmission of data and a wake-up signal in 802.11ax – Follow-up”, IEEE 802.11-17/0385r0, Mar. 2017

## Slide 18: Appendix

## Slide 19: Appendix - DFT Input Mapping for OOK Symbol with Manchester Coding
DFT Input Index
1
2
8
23
24
30
31
15
16
Symbol 1 = 0
S
0
9
17
32
0
0
0
0
0
0
0
0
38
39
45
46
48
1
2
8
23
24
30
31
15
16
Symbol 1 = 1
0
S
9
17
32
0
0
0
0
0
0
0
0
38
39
45
46
48
1
2
8
23
24
30
31
15
16
Symbol 2 = 0
0
0
9
17
32
S
0
0
0
0
0
0
0
38
39
45
46
48
1
2
8
23
24
30
31
15
16
Symbol 2 = 1
0
0
9
17
32
0
S
0
0
0
0
0
0
38
39
45
46
48
1
2
8
23
24
30
31
15
16
Symbol 3 = 0
0
0
9
17
32
0
0
S
0
0
0
0
0
38
39
45
46
48
1
2
8
23
24
30
31
15
16
Symbol 3 = 1
0
0
9
17
32
0
0
0
S
0
0
0
0
38
39
45
46
48

## Slide 20: Appendix - Allocation
-4
-16
-17
-42
RU3
RU2
-43
-68
-70
RU1
-95
-96
4
16
17
42
RU7
RU8
43
68
70
RU9
95
96
-121
121
-34
33
49
116
-116
-49
-83
-82
-1
0
83
82
-42
RU3
RU2
-43
-68
-70
RU1
-95
-96
42
RU7
RU8
43
68
70
RU9
95
96
-121
121
-34
33
Standalone
11ba:
11ba multiplexing:
11ba+11ax concurrent transmission:
Standalone
11ax:
-34
33
3.75 MHz (48 tones)

## Slide 21: Appendix – SNR Definition
In [2], SNR is defined as “SNR over 20 MHz, means SNR = E[s^2] / E[n^2], where the expectation is sampling is done at 20 MHz samples”
The figure shows the temporal characteristics of sequence-based OOK symbols at 20 dB SNR.
It has also been agreed to consider full OOK symbol duration for signal power calculation
3 dB
SNR: 20 dB