## Slide 1: UL transmission behavior of WUR STA
Date: 2017-07-13
Authors:

## Slide 2: Abstract
In this contribution,
  We discuss the uplink transmission behaviors of a WUR STA in the WUR mode
  We propose to define a guard period to avoid status mismatch problem after UL transmissions of a WUR STA

## Slide 3: UL behavior of WUR STA
When a STA is using both WUR mode and PS mode,
  The STA enters the awake state to receive or transmit frames.
  Otherwise, the STA remains in the WUR doze state where it turns off the main radio and uses WURx to receive WUP
A WUR STA may enter the awake state whenever it has data to transmit
  After a successful UL transmission, it may enter the WUR doze state
  Unless the STA uses an explicit mode change signaling, the STA’s operating mode will not change
The aforementioned behaviors is aligned with the existing power save protocol

## Slide 4: Status mismatch problem after UL transmissions
After a successful UL transmission, the WUR STA may not immediately enter the WUR doze state in order for another UL transmissions
During that time, if the AP transmits a WUP to the STA, the STA cannot receive the WUP
  It incurs unnecessary waste of resources
    Increased uplink latency and power consumptions to the STA
    Unnecessary channel occupation
However, it is hard for the AP to define when would be the right time to send a WUP to the STA

## Slide 5: Application of the guard period
To avoid the mismatch problem, a guard period can be considered after a successful UL transmission
  The guard period starts at the end of WUR STA’s UL transmission sequence
  The guard period is renewed by a subsequent UL transmission of the same STA
Within the guard period,
  The AP should not send a WUP to the STA
  The STA should not expect to receive any WUP from the AP
    If it has no more uplink data, it should enter the doze state before the period ends

## Slide 6: Conclusions
We have discussed the uplink transmission behaviors of a WUR STA in the WUR mode
We have proposed a guard period to avoid status mismatch problem after UL transmissions of a WUR STA

## Slide 7: Strawpoll
Do you agree with the following?
  After a successful uplink transmission of a STA in WUR mode, AP does not transmit a unicast wake-up packet to the STA for a guard period.