## Slide 1: IEEE 802.1AS REV D5.0 Review Comments
Date: 2017-07-10
Authors:

## Slide 2: Motivation/Background
IEEE 802.1AS REV project includes use of IEEE 802.11-2016 Fine Timing Measurement as an additional 802.11 protocol to generate timestamps that 802.1AS would use for clock synchronization
IEEE 802.1AS REV project includes use of IEEE 802.11ak General Links for interfacing 802.11 MAC SAP to IEEE 802.1AC
802.1AS Rev D5.0 WG Ballot is currently open and closes July 13th, 2017.

## Slide 3: Summary of comments
 | Type | Count | 
1 | Editorial | 4 | 
2 | Technical | 2 | Needs discussion with ARC
 |  | 8 | Needs discussion with 802.1AS
 |  | 1 | Needs discussion with 802.11md amd 802.11az
Notes:   Should the Capabilities bit(s) apply to all ranging protocols? Or should we allow for indications in the Beacon to indicate Initiator/Responder capabilities for each Ranging Protocol independently? What about Ranging Protocols that do not have a distinct Initiator/Responder?

## Slide 4: Comments that need discussion with 802.11 ARC
802.11 MAC interfacing with ISS without support for 802.11ak
Figures 7.8 and 8.2 in IEEE 802.1AS D5.0
Open Issues:
  Should 802.1AS over 802.11 require 802.11ak?
  If 802.11ak is required how would current implementations of 802.11 and 802.1AS-2011 be addressed?

## Slide 5: Comments that requires discussion in 802.11md and/or 802.11az
What is the “disconnect” between IEEE 802.11-2016 and IEEE 802.1AS REV D5.0?
  IEEE 802.1AS D5.0
    Use FTM with the following parameters
      ASAP=1
      Single Burst (Burst Exponent = 0)
      FTMs per Burst – infinite number of FTMs (not explicit in D5.0)
  IEEE 802.11-2016 Fine Timing Measurement
    Does not have a mechanism to indicate “infinite” for FTMs per Burst

## Slide 6: Requirements
Simple Change
Must not break existing IEEE 802.11-2016 implementations of Fine Timing Measurement

## Slide 7: Proposed Solution-A
Amend 802.1AS REV D5.0 to use multiple burst instead of single burst
Issues
  Still does not allow for “infinite” number of FTM frames to be sent; as the maximum number of bursts is limited to 215
  May cause discontinuity in the flow of time information from the top of the network to the leaf
    This is because all burst excepting the first one needs to be started with a FTM Request frame from the Slave to the Master

## Slide 8: Recap of Multiburst FTM Session

## Slide 9: Fine Timing Measurement Parameters Element
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory)
Octets | 1 | 1 | 1 | variable | variable | 11
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 10: Burst Duration Field
Value | Represents
0-1 | Reserved
2 | 250 us
3 | 500 us
4 | 1 ms
5 | 2 ms
6 | 4 ms
7 | 8 ,ms
8 | 16 ms
9 | 32 ms
10 | 64 ms
11 | 128 ms
12-14 | Reserved
15 | No Preference
12 | forever
13-14 | Reserved
Initiator: Burst Duration field set to 15 (no preference) and FTMs per Burst set to 0 (no preference)
Responder: Burst Duration field set to 12 (forever) and FTMs per Burst set to 0 (infinite)

## Slide 11: Proposed Solution-B
Amend IEEE 802.11-2016 to allow for a new choice for the number of FTMs per Burst
  Use one of the reserved values from the possible values for Burst Duration (values 12-14 are reserved in IEEE 802.11-2016)
  Initiator sets FTMs per burst to 0 (indicating no preference) and sets Burst Exponent to 0 (Single Burst)
  Responder sets Burst Duration to 12 (indicating “Forever”) and sets Burst Exponent to 0 (Single Burst)
  Responder sets FTMs per Burst to 0 (currently disallowed in IEEE 802.11-2016) indicating “infinite” FTMs (new behavior)

## Slide 12: Proposal-C
Open to other suggestions