## Slide 1: 11BA Power Save
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Frame Exchange through PS-Poll
After receiving PS-Poll from a STA, the frame for the STA may not be ready in the AP.
  STA may waste its power.
.11PHY Header
Data MPDU
Ack
AP
STA
PS-Poll
TXOP
.11PHY Header
Data MPDU
Ack
AP
STA
PS-Poll
Ack

## Slide 3: Unicast Wakeup and Frame Exchange
If an AP receives PS-Poll from the STA solicited by unicast LP Wakeup frame, the AP shall not respond with Ack.
  The responding frame to PS-Poll in this case will be data/management frame.
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
.11PHY Header
PS-Poll
TXOP

## Slide 4: Group Wakeup Recap[2]
A group STAs can wake up together to receive group frames, receive DL MU PPDU.
Static groups (group ID, group member) which are similar to 11ac’s DL MU group are maintained through Action frame.
Dynamic group (multicast group without group announcement/negotiation) are defined through different methods:
  Part of multicast MAC address is put in AID field of LP Wakeup frame.
  The hash result of multicast MAC address is put in AID field of LP Wakeup frame.
  AID bit map which is similar to AID bitmap of TIM element is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
  AID set which includes multiple AIDs is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
It seems that part of multicast MAC address or hash result of multicast MAC address being put in AID field of LP Wakeup frame is better for the reception of group frames. AID set/bitmap and/or sequential multiple LP Wakeup frames is better for DL MU reception.

## Slide 5: Static Group Allocation
It seems that static group is easy to be supported.
The STAs can be grouped together through TWT negotiation.
The static group ID can be a value from 0 to maximal group ID value, e.g. 63, 127, 255 etc.
The group member ID can be used to identify STAs in the group through bitmap if required.
The AP can announce multicast group for multicast MAC address.
  With this, unique group ID can be used for triggering group STAs in the group.
The LP Wakeup frame is defined as follows: partial TST time may be added for synchronization.
Type
Group ID
FCS
Bits:
3
8
4
11
CBSSID
or
Type
Group ID
FCS
Bits:
3
8
4
11
CBSSID
Member Bitmap
8
CBSSID = compressed BSSID
CBSSID = compressed BSSID

## Slide 6: Straw Poll 1
Do you support that if an AP receives PS-Poll from the STA solicited by unicast LP Wakeup frame, the AP shall not respond with Ack?

## Slide 7: Straw Poll 2
Do you support static group for triggering group STA wakeup through LP Wakeup frame?

## Slide 8: Straw Poll 3
Do you support static group for LP Wakeup frame to trigger multicast frame transmission?

## Slide 9: Straw Poll 4
Do you support static group being combined with TWT?

## Slide 10: Reference
[1] 11-16/1460R01 WUR MAC consideration
[2] 11-17/642R2 Wake Up Frame Followup
[3] 11-17/124R0 WUR MAC and Wakeup Frame
[4] 11-17/437R0 WUR MAC and Wakeup Frame