## Slide 1: Relay Threat Model for TGaz
Date: 2017-07-12
Authors:
Name | Affiliations | Address | Phone | email
Wei Wang | Google Inc. |  |  | weiwa@google.com
Roy Want | Google Inc. |  |  | roywant@google.com

## Slide 2: Abstract
The relay threat model occurs when two attackers collaborate to fake the distance between two stations, making them appear closer than they really are.
11az should be resilient to a relay attack in both associated and unassociated modes.

## Slide 3: Background
Wireless Relay Attacks have been used to defeat wireless car locks and pose a real threat to property
https://www.wired.com/2016/03/study-finds-24-car-models-open-unlocking-ignition-hack/
Bridging the gap
Attacker Box A
Near Owner
Attacker Box B
Near Car

## Slide 4: Mitigating Relay Attacks
Using range and location can be a good defense against relay attacks, assuming that the range/location of each party can be validated.

## Slide 5: Applications using RTT range for secure operation
Associated (with prior shared keys)
Building door locks
Car door locks
Document access (e.g. only at work)
Cloud Service Access (e.g. only within home)
Unassociated (no prior shared keys)
Proof of presence at a location
Proximity transfer of a redeemable wireless coupon
Control of a public IoT device with a wireless token

## Slide 6: Ranging in 11mc
FTM_Req
FTM
FTM(t4- t1)
FTM RESPONDER
MOBILE
Ack
Ack
t1
t2
t3
t4
Ack
Distance (d) can be used to verify a condition:
d < [opening criterion],
But ONLY if you can trust it.

## Slide 7: Relay Attack #1: Faking a Range in 11mc
Attacker Box A
Attacker Box B
t1
t4
t2
t3
FTM(t4- t1)
FAKE (t4- t1)
FTM_Req
FTM_Req_Ack
Ack
FTM
t2 ‘
t3 ‘
t1 ‘
t4’
FTM RESPONDER
MOBILE

## Slide 8: Relay Attack #2: Faking a Range in 11mc
Attacker Box A
Attacker Box B
t1
t4
t2
t3
FTM(t4- t1)
FTM (t4- t1)
FTM_Req
FTM_Req_Ack
FAKE (Ack)
FTM
VALID_SIG
Ignore t4’
t1 ‘
t3 ‘
t2 ‘
FTM RESPONDER
MOBILE

## Slide 9
11az Authentication can prevent a relay attack
if…
each packet is authenticated
there is a shared symmetric key

## Slide 10
What about the unassociated mode in 11az as there are likely no shared keys via AP association?
But unassociated modes are useful for:
Proof of presence at a location
Proximity transfer of a redeemable wireless coupon
Control of a public IoT device with a wireless token
Solutions
Ref: 11-16-1498r1 (Qi Wang et al., Broadcom) “FTM Security in Associated and Un-associated States”
Ref: 11-16-1508r0 (Naveen Kakani et al., Qualcomm) “FTM Frame Exchange Authentication”

## Slide 11: Separation of Concerns
11az
11az
APP/OS
CLOUD SERVICE
CHECKS IF X1 = X2, THERE IS NO RELAY ATTACK
APP/OS
DERIVED X1
DERIVED X2
Relay Attack

## Slide 12: Relay Attack Defense without Shared Keys
t1
t4
t2
t3
FTM(t4- t1) + Nonce-AB
FTM + Nonce-A
(Ack + Nonce-B)
MOBILE
FTM RESPONDER
Verify
AB + (t4-t1) at
APP Level
Verify
AB + (t4-t1) at
APP Level

## Slide 13: Simplified relay attack solution for unassociated 11az
Attacker Box A
Attacker Box B
t1
t4
MOBILE
t2
t3
FTM(t4- t1) + Nonce-AX
FTM (t4- t1) + Nonce-AB
FTM_Req
FTM + Nonce-A
Ack + Nonce-B
t1’
ignored t4’
t3’ generated
t2’
FTM_Req_Ack
(Ack + Nonce-X)
Verify
AB + (t4-t1) at
APP Level
FTM + Nonce-A
Verify
AB + (t4-t1) at
APP Level
FTM RESPONDER

## Slide 14: Conclusion
If encryption is not supported in the FTM negotiation - because of silicon complexity - because of interaction time - because of power consumption
Then range integrity can still be obtained by making the
2 nonces + (t4-t1) accessible to the App layer
At the expense of having the range data overheard
[which may not be a problem in many use cases].

## Slide 15: Straw Poll
11az protocol shall support a mode where range integrity can be obtained without authentication and encryption via upper layer out-of-band communication.
Y: N: A:

## Slide 16: Motion
Move to adopt the functional requirement depicted below, and instruct the FRD editor to include it in the FRC under section 2.1.6, in a subsection dealing with ranging integrity without cryptography, and give editorial license.
“The 11az protocol shall support a mode where range integrity can be obtained without authentication and encryption via upper layer out-of-band communication.”
Y: N: A:

## Slide 17: References
11-16-1498r1 (Qi Wang et al., Broadcom) “FTM Security in Associated and Un-associated States”
11-16-1508r0 (Naveen Kakani et al., Qualcomm) “FTM Frame Exchange Authentication”
Radio attack lets hackers steal 24 different car models
https://www.wired.com/2016/03/study-finds-24-car-models-open-unlocking-ignition-hack/